## Slide 1: Views on Rel-20 SON/MDT
RP-250333
RAN#107
Incheon, S.Korea
March 12-14,2025
Agenda : 15.2.9.2

## Slide 2: Further SON enhancements for LTM
Rel-19 SON/MDT for LTM covered the following aspects for intra-CU LTM:
  Optimize MCG LTM failure and success scenarios (e.g., via RLF Report, SHR enhancements)
  Optimize RACH-less LTM
As a continuation, we propose the following to be considered as part of a potential Rel-20 SON/MDT WI:
  Optimize SCG LTM failure and success scenarios
  Optimize inter-CU LTM scenarios
  Optimize conditional LTM scenarios
Note : R20 SON/MDT WI is expected to be small if it happens, so scope MUST be limited.

## Slide 3: Further SON/MDT enhancements for NTN
Rel-19 SON/MDT for NTN covered the following aspects:
  Optimizing intra-NTN mobility scenarios (e.g., time-based, location-based CHO)
  New granularity for collecting logged MDT in NTN (e.g., geographical area based)
As a continuation, we propose the following to be considered for potential Rel-20 SON/MDT WI:
  Optimize TN-NTN mobility
  Optimize access in NTN (e.g., via RA/CEF Report enhancements)
  Further logged MDT enhancements for NTN (e.g., new event triggers)
  Distinguishing SON/MDT reports collected over NTN and TN

## Slide 4: SON/MDT for Aerial UEs
Rel-20 SON/MDT WI can consider the following aspects related to Aerial UEs e.g.,
  Logged MDT enhancements for Aerial UEs (e.g., height-dependent area scope or triggers)
  MRO for Aerial UEs (e.g., RLF/SHR enhancements)
  Distinguishing SON reports collected from Aerial UEs and terrestrial UEs

## Slide 5: Logged MDT enhancements for LP-WUR
Rel-19 LP-WUR WI specified support for Low Power Wake-up Radio (LP-WUR) operation including
  RRM measurement relaxations for MR and measurement offloading from Main Radio (MR) to LP-WUR
  Support for LP-SS (Low Power - Synchronization Signal)
  Support for LP-WUS (Low Power Wake Up Signal)
The current logged MDT framework collects radio measurements (based on SSB) when UE is in RRC_IDLE and RRC_INACTIVE and doesn’t consider whether UE operates in LP-WUR or is receiving LP-SS (instead of SSB).
Therefore, we propose that a potential Rel-20 SON/MDT WI can include the following
  Logged MDT enhancements for LP-WUR

## Slide 6: RA Report enhancements for SBFD aware UEs
Rel-19 Full Duplex WI specified enhancements to support RACH in SBFD symbols/slots by SBFD aware UEs and is specifying two types of RACH configurations for SBFD aware UEs
  Option 1: Use a single RACH configuration, but the existing parameters might be configured differently for SBFD slots, or new parameters might be introduced for SBFD slots
  Option 2: Use two separate RACH configurations - one legacy RACH configuration and one additional RACH configuration
Rel-20 SON/MDT WI can specify RA Report enhancements for SBFD aware UEs e.g., for the following network optimization objectives:
  Collect statistics about the RO type used (SBFD RO or legacy RO)
  Optimize switching between RO types (SBFD RO vs. legacy RO)
  Optimize SBFD specific RACH resources and parameters

## Slide 7: Summary - Rel-20 SON/MDT WI objectives
Rel-20 SON/MDT WI is not our high priority. If WI is agreed, then scope has to be limited.
Following are potential objectives, and down selection may be needed.
  Continue to optimize the following features via SON/MDT
    Further SON/MDT enhancements for LTM (for SCG LTM, inter-CU LTM, conditional LTM)
    Further SON/MDT enhancements for NTN (TN-NTN mobility, RA/logged MDT enhancements)
  New features to optimize via SON/MDT (select one max or none)
    SON/MDT enhancements for Aerial UEs
    RA Report enhancements for SBFD aware UEs
    Logged MDT enhancements for LP-WUR