## Slide 1: View on Ambient IoT in Rel-20
NTT DOCOMO, INC.
3GPP TSG RAN meeting #107
Incheon, Korea, March 12-14, 2025
Agenda Item: 15.2.3
Document for: Discussion
RP-250361

## Slide 2: Ambient IoT in Rel-18 and 19
In Rel-18
  TSG-level study item has been conducted and the study outcomes are captured in TR38.848
In Rel-19
  WG-level study item has been conducted and the study outcomes are captured in TR38.769.
  New WID RP-243326 was approved at the RAN#106.
General Scope
The definitions provided in TR 38.848, TR 38.769, and decisions, etc. made during the Rel-19 SI in RAN WGs are taken into this WI, and the following is the exclusive general scope:
The overall objective shall be to standardize the following Ambient IoT device:
  Device 1: ~1 µW peak power consumption, has energy storage, RF envelope detector receiver, initial sampling frequency offset (SFO) up to 10X ppm, neither R2D nor D2R amplification in the device. The device’s D2R transmission is backscattered on a carrier wave provided externally.
Deployment scenario 1 with Topology 1, according to D1T1-B.
FR1 licensed spectrum in FDD, with R2D in DL spectrum and D2R and CW in UL spectrum.
Spectrum deployment in-band to NR and standalone, with A-IoT BS located indoor.
Traffic types DO-DTT, DT, for rUC1 (indoor inventory) and rUC4 (indoor command).
Carrier wave transmission for waveform 1 only, without hopping, per the following cases in TR 38.769:
  Case 1-4 for D1T1-B
Proximity determination via Solution 1 in TR 38.769 only.
Device (un)availability via Direction 1 in TR 38.769 only.

## Slide 3: Approved work plan in Rel-20
According to RP-243280, the following work plan in Rel-20 A-IoT was approved for enhancement from Rel-19 A-IoT.
Details and whether study phase is necessary or not for Rel-20 A-IoT should be further discussed.
Workplan for Rel-20:
  Includes D2T2
  Includes Device 2
  A limited number of additional use cases, deployments, connectivity topologies, devices, traffic types in TR38.848 as a starting point
  Note: work on D2T2, device 2 shall follow the Rel-19 study conclusions, and further down-selection of architecture options for topology 2 may be needed. For indoor use cases, deviations from Rel-19 study conclusion shall be well justified and agreed.
  Details to be discussed at a later RAN plenary meeting, including the need for study phase.
For both Rel-19 and Rel-20, co-ordination with SA2/3 is expected

## Slide 4: Ambient IoT in Rel-20
Deployment scenario
  In Rel-19, it focuses on device indoor scenario with inventory and command use cases.
  Extension for outdoor scenario is more attractive to enlarge the use case and market of A-IoT.
  Proposal: Support device outdoor scenario, i.e., deployment scenario 4 in TR38.848, for A-IoT in Rel-20.
    Targeting the equivalent coverage as legacy NR.
    Legacy NR BS and A-IoT reader can be co-located
Topology
  For device indoor scenario, D1T1 is supported in Rel-19 and D2T2 is noted in TR-243280 for Rel-20.
  For device outdoor scenario, at least D4T1 should be studied. In addition, D4T2 can be considered for coverage extension.
  Proposal: Support at least D4T1 for outdoor scenario in Rel-20.
    FFS: D4T2
Device type
  In TR-243280, it is noted to support device 2 in TR38.769 in Rel-20.
  For outdoor scenario, device 2b can be the baseline for coverage evaluation.
    According to the coverage evaluation in Rel-19 SI in RAN1, hundreds or a few thousands meter distance can be achievable by device 2b while it is challenging by device 2a which requires externally generated CW.
  Proposal: Study device 2b as baseline for coverage evaluation of outdoor scenario in Rel-20.
    Further study the additional device type to achieve the target coverage with practical parameters if necessary.

## Slide 5: Ambient IoT in Rel-20
Use cases
  Use cases for outdoor scenario were studied and captured in TS22.840 and TR38.848.
  In addition to the use cases of inventory and command which are supported for indoor scenario in Rel-19, sensor use cases are interested especially for outdoor scenario.
  Proposal: Support at least rUC6 (sensors) in TR38.848 for outdoor scenario in Rel-20.
Traffic type
  In Rel-19, DT and DO-DTT traffic types are supported, i.e., D2R transmission is always triggered by reader.
  To support use cases of sensors, it is necessary to support DO-A traffic type.
  Proposal: Support DO-A traffic at least for outdoor scenario in Rel-20.
Device (un)availability
  In Rel-19, only direction 1 in TR38.769 is assumed for device (un)availability.
  Given that the peak power consumption on device 2 is much larger than that for device 1, sustainable operation time for device 2 is expected to be shorter than that for device 1.
    It is essential for reader to be aware of the device (un)availability considering the short sustainable operation time for device 2.
  Proposal: Support direction 2 in TR38.769 for device (un)availability at least for device 2 in Rel-20.

## Slide 6: Ambient IoT in Rel-20
RAN2/3 aspects
  Architecture/protocol stack option
    RRC based solution is prioritized since it can reuse NGAP indications between AIOTF and gNB introduced in Rel-19.
    In addition, NAS based or UP based solution can be supported up to SA decision. (But RAN impact is FFS.)
  AIoT air interface
    Rel-19 is a baseline.
    Device 2 specific functionality (e.g., energy status reporting) can be in Rel-20 scope.
  Uu interface
    RRC configurations of AIoT reader functionalities.
    UE capabilities for intermediate UE.
    Intermediate UE is in CONNECTED state. Open to discuss whether to support temporary out of connection condition.
  Proposal: Support RRC based solution for Topology 2.
  Proposal: Support device 2 specific functionalities (e.g., energy status reporting) if needed.
  Proposal: Support RRC configurations and UE capabilities of AIoT reader functionalities.

## Slide 7: Proposed scope for Ambient IoT in Rel-20
Proposal: Study Item for outdoor scenario followed by Work Item in Rel-20.
  At least coverage and co-existence with legacy NR for outdoor scenario should be evaluated in the Study Item which requires at least 2Q.
  Potential general scope for the Study Item:
General Scope
Ambient IoT device Type:
  Device 2b as baseline: ≤ a few hundred µW peak power consumption has energy storage, initial sampling frequency offset (SFO) up to 10X ppm, both R2D and/or D2R amplification in the device. The device’s D2R transmission is generated internally by the device.
At least Deployment scenario 4 with Topology 1.
FR1 licensed spectrum in FDD, with R2D in DL spectrum and D2R in UL spectrum.
Spectrum deployment at least in-band to NR, with A-IoT BS located outdoor.
Traffic types at least DO-A for rUC6 (outdoor sensors).
Device (un)availability via Direction 2 in TR 38.769.
Note: Work Item for enhancements on indoor scenario, e.g., D2T2, device 2, can be considered in Rel-20 as well.