## Slide 1: Views on Rel-20 AI for Mobility
3GPP TSG RAN Meeting #107 RP-250418
Incheon, Korea, March 12-14, 2025
Agenda Item: 15.2.4
Source: Lenovo
Document for: Discussion

## Slide 2: AI for Mobility
  Motivation:
  Rel-19 SI (RP-242393). The following use cases have been discussed.
    RRM measurement prediction: Cell-level measurement prediction/L3 beam-level measurement prediction (UE sided model and NW sided model)
    Measurement event predictions: L3 event prediction (UE sided model)
    RLF prediction: UE sided model
    HO failure prediction: deprioritized.
  Predication for L1 measurement result for LTM purpose
    LTM based on L1 measurement report has been supported in Rel-18 and Rel-19. Both Intra-CU LTM and Inter-CU LTM are supported.
  Predication for Lower layer event based L1 measurement report for LTM purpose
    Lower layer event based L1 measurement report is supported in Rel-19.
Observation 1: In Rel-19 SI, there has been good progress on RRM measurement prediction/Measurement event prediction/ RLF prediction.
Observation 2: In Rel-19 SI, HO failure prediction has been deprioritized.
Observation 3: LTM based on L1 measurement report and Lower layer event based L1 measurement report have been supported in Rel-18/Rel-19.

## Slide 3: AI for Mobility
  Objective:
  RRM measurement prediction (UE sided model and NW sided model)
  Measurement event predictions: L3 event prediction (UE sided model)
  RLF prediction (UE sided model)
  Enhanced LCM for AI based mobility
  Potential specification impacts of AI/ML aided mobility: e.g., UE assistance information for network sided model, Network configuration, prediction report from UE
  Additional objective: Study LTM related prediction
  Prediction for L1 measurement result for LTM purpose , e.g., inter-cell L1 prediction.
  Prediction for Lower layer event for LTM purpose
Proposal 1: AI for Mobility with the following objectives can be supported in Rel-20 for 5GA.
  RRM measurement prediction/L3 measurement event predictions/RLF prediction.
  Enhanced LCM for AI based mobility and relevant signaling impact.
  Proposal 2: LTM related prediction can be studied in Rel-20 as follows.
  Prediction for L1 measurement result for LTM purpose, e.g., inter-cell L1 prediction.
  Prediction for Lower layer event for LTM purpose.

## Slide 4: thanks