## Slide 1: Rel-20 AI/ML for NR Air Interface
Huawei, HiSilicon, Vodafone
3GPP TSG RAN#107 RP-250493
Incheon, Korea, March 12-14, 2025
Agenda Item: 15.2.1

## Slide 2
Views on whether to explore new use cases for 5G-A
Based on RP-243292 Chair’s summary endorsed in RAN#106 meeting, there is one question as copied below on 5G-A new use cases for AI/ML air interface in Rel-20:
The Rel-19 use cases for AI/ML air interface are exemplary and not all of them are related to widely commercialized features
  Beam management: not widely commercialized
  Positioning: not widely commercialized
  CSI compression: focuses on FDD in Rel-19
  CSI prediction: focuses on FDD
Adoption of AL/ML in commercial deployments requires strong justification from cost-benefit point of view. New use cases, with high gains obtainable in widely deployed scenarios, make AI/ML features more likely to be commercialized.
The start of commercialization for AI/ML air interface in 5G-A can pave the way for commercialization from day 1 in 6G.
  Observation: There is strong need to explore new use cases with high gains obtainable in widely deployed scenarios in Rel-20 for 5G-Advanced, to make AI/ML more likely to be commercialized.

## Slide 3
  Study and specify a limited set of new use cases for AI/ML air interface for 5G-Advanced in Rel-20:
    Focus on use cases with high gains obtainable in widely deployed scenario(s), e.g. apply to both FDD and TDD
    Examples for further discussion
      Extension of CSI compression for TDD
      Overlaid DMRS and data with one-sided AI/ML channel estimation
Proposal

## Slide 4
Reference
[1] RP-242884 Rel-20 AIML for NR Air Interface