## Slide 1: Rel-20 SBFD
Huawei, Hisilicon
3GPP TSG RAN Meeting #107
Incheon, Korea, March 12-14, 2025
Agenda Item: 15.2.10
RP-250495

## Slide 2
SBFD status in Rel-18 and Rel-19
Rel-18 SBFD (Study Item)
  Four different SBFD Deployment Cases* were defined and studied as in TR38.858
  Various gNB-to-gNB CLI handling schemes were studied including beam nulling, beam pairing, DL/UL power control and UL resource muting
Rel-19 SBFD (Work Item)
  Deployment case 1 and inter-subband CLI handling were prioritized
  Deployment case 2 and Deployment case 3 were not prioritized
  Intra-subband CLI handling was not optimized
*Note: SBFD Deployment Cases from TR 38.858
Case 1: Non-coexistence case with single SBFD subband configuration
Case 2: Non-coexistence case with multiple SBFD subband configurations
Case 3: Co-channel co-existence case between TDD and SBFD
Case 4: Adjacent-channel co-existence case

## Slide 3
The traffic statistics of one city in China exhibits significant disparities in UL resource utilization across different base stations (scattered BS sites in red are with higher UL resource utilization)
Observation: Uplink capacity demands are geographically imbalanced which requires support of different SBFD subband configurations cross different gNBs (i.e. deployment case 2)
Challenges for practical SBFD deployment
Geographically imbalanced uplink traffic demands
SBFD Cells
TDD Cells
Upgrading existing TDD network with SBFD macro base stations
  Observation: Both upgrading existing TDD network with SBFD macro base stations and deploying new SBFD small cell base stations require TDD-SBFD co-channel co-existence handling
Co-channel Co-existence between TDD and SBFD
TDD Cells
SBFD cells
Deployment case 3-1
Deployment case 3-2
Deploying new SBFD small cell base stations
Aggressor gNB
D
D
D
U
D
D
D
D
D
U
U
U
U
Victim gNB
U
U
U
U
D
D
D
U
D
D
D
D
D
U
U
U
U
D
D
D
D
D
D
D
U
D
D
D
D
D
D
D
D
U
D
D
D
D
D
U
U
U
U
D
D
D
D
Aggressor gNB
Victim gNB
Observation 1: Issues for deployment case 2 and case 3 should be carefully addressed for successful SBFD deployments, and intra-subband gNB-to-gNB CLI is the key challenge.
CLI
CLI

## Slide 4
Necessity for intra-subband CLI handling enhancements
INR analysis for Deployment case 2
INR analysis for Deployment case 3
Deployment case 3-1
Deployment case 3-2
Observation 2: Due to strong intra-subband CLI from aggressor gNB, the interference to noise ratio can be 55.5 dB for macro deployment and 33 dB for indoor small cell deployment.
Observation 3: To achieve 1dB sensitivity degradation, INR should be -6dB  enhancement in intra-subband gNB-to-gNB CLI handling is needed for Deployment case 2 and 3
Observation 4: Intra-subband gNB-to-gNB CLI handling enhancements are also beneficial for Dynamic SBFD.
Parameters (4GHz/100MHz) | Values
Inter-site Distance (m) | 300m (Macro-Macro)
TX power (dBm) | 50
TX Array Gain (dB) | 0
TX antenna gain (dB) | 5
Pathloss (dB) | 95
penetration loss (dB) | 0
Rx antenna Gain (dB) | 5
Rx interference (dBm) | -35
Noise Figure (dB) | 3.5
Noise Power (dBm) | -90.5
INR (dB) | 55.5
Parameters (4GHz/100MHz) | Values
Inter-site Distance (m) | 100m (Macro-Indoor)
TX power (dBm) | 50
TX Array Gain (dB) | 0
TX antenna gain (dB) | 5
Pathloss (dB) | 84
penetration loss (dB) | 30
Rx antenna Gain (dB) | 5
Rx interference (dBm) | -54
Noise Figure (dB) | 7
Noise Power (dBm) | -87
INR (dB) | 33
Parameters (4GHz/100MHz) | Values
Inter-site Distance (m) | 300m (Macro-Macro)
TX power (dBm) | 50
TX Array Gain (dB) | 0
TX antenna gain (dB) | 5
Pathloss (dB) | 95
penetration loss (dB) | 0
Rx antenna Gain (dB) | 5
Rx interference (dBm) | -35
Noise Figure (dB) | 3.5
Noise Power (dBm) | -90.5
INR (dB) | 55.5

## Slide 5
Proposal for intra-subband gNB-to-gNB CLI handling enhancements
Observation 5:
DL power back off was studied as one of the gNB-to-gNB CLI handling schemes in 38.858
Subband-level DL power back off provides significant UL throughput improvement with moderate DL throughput loss as power reduction only applies to PRBs which overlapping with SBFD UL subband
Proposal 1: Specify subband-level downlink power back off including corresponding enhancements in CSI measurement and report [RAN1, RAN4]
  Support frequency-dependent PDSCH EPRE to CSI-RS EPRE ratio for CSI derivation
  Extend gNB RE power control dynamic range as needed
Proposal 2: Other enhancements studied in TR38.858, e.g. uplink resource muting for gNB-to-gNB channel measurement, can also be considered
Frequency
Power
Frequency
Power
Intra-subband CLI
DL
UL
DL
DL
DL
DL
Illustration of subband-level downlink power back off
Performance of subband-level downlink power back off for deployment case 3-1
(IRC and Tx beam nulling are used)
Aggressor gNB
Victim gNB

## Slide 6
Summary
In this contribution, we have the observations and proposals as follows:
Observation 1: Issues for deployment case 2 and case 3 should be carefully addressed for successful SBFD deployments, and intra-subband gNB-to-gNB CLI is the key challenge.
Observation 2: Due to strong intra-subband CLI from aggressor gNB, the interference to noise ratio can be 55.5 dB for macro deployment and 33 dB for indoor small cell deployment.
Observation 3: To achieve 1dB sensitivity degradation, INR should be -6dB  enhancement in intra-subband gNB-to-gNB CLI handling is needed for Deployment case 2 and 3
Observation 4: Intra-subband gNB-to-gNB CLI handling enhancements are also beneficial for Dynamic SBFD.
Observation 5:
DL power back off was studied as one of the gNB-to-gNB CLI handling schemes in 38.858
Subband-level DL power back off provides significant UL throughput improvement with moderate DL throughput loss as power reduction only applies to PRBs which overlapping with SBFD UL subband
Proposal 1: Specify subband-level downlink power back off including corresponding enhancements in CSI measurement and report [RAN1, RAN4]
  Support frequency-dependent PDSCH EPRE to CSI-RS EPRE ratio for CSI derivation
  Extend gNB RE power control dynamic range as needed
Proposal 2: other enhancements studied in TR38.858, e.g. uplink resource muting for gNB-to-gNB channel measurement, can also be considered