## Slide 1: Views on NR-enabled UAV in 5G-A Rel-20
RP-250558
3GPP TSG RAN Meeting #107
Incheon, Korea, March 12-14, 2025
Source: ZTE Corporation, Sanechips
Agenda: 15.2.8.3

## Slide 2
Background & Motivation
As part of additional RAN2-led Candidate Topics in [1], further analysis is provided to verfiy the needs for enhancement in Rel-20:
  For the Rel-19 scope, the following conclusion is made based on the inputs for additional package discussion [2]:
    Additionally, other enhancements, e.g., address the UL interference, UE identification and necessary status information exchange with CN is also proposed by companeis to address the needs of real deployment.
  For the commerical needs, as an essential part of “low altitude economy” strategy, extensive trials have been conducted in various scenarios and for different applications, e.g., logistics, transportation, agriculture, meteorology, river inspection and smart tourism (ref: https://www.zteitalia.it/en/2020/06/09/zte-wins-best-practice-award-for-5g-network-and-terminal-coordination/).
  Then, it can be forseen that mutual benefits can be achieved with the 5G-A enabled UAV serivce.
[1] RP-243292 RAN Chair's summary of 5G Advanced in Rel-20.pptx
[2] RP-232627 Moderator’s summary for REL-19 RAN2 additional topics
Conclusions Large operator support for UAV as one of the most important Rel-19 topics (within the items in this offline) from a commercial and mission critical perspective. Architectural changes will not be part of the UAV work (i.e. any architectural enhancements can be considered under NTN) Starting point of an acceptable objective: Mobility enhancements Specifying new CHO triggering events Studying/specifying LTM enhancements for UAV No transmit zone (if SA2 will also do work on this) Enhancements for RRC_IDLE/RRC_INACTIVE

## Slide 3
Potential objective: Mobility enhancements
Overview：
  As captured in TR 36.777, the number of detectable cells and the range of the detected cells increases as UAV altitude increases. Besides, UAV UE moves faster compared to ground UEs. Thus, more frequent handover shall be triggered for UAV UE. Improving mobility robustness and reducing mobility latency are key points to be considered for UAV mobility enhancements.
  In Rel-16, CHO is introduced to improve mobility robustness. Considering the characteristics of UAV, there could be more candidate cells available for CHO, and different candidate cells in different altitude ranges. Thus, the height information and/or flight path information reported by the UE can be considered for CHO candidate cell preparation and CHO triggering.
  In Rel-18, LTM is supported to enable fast cell switch and reduce mobility interruption time. Similarly, different candidate cells would be detectable in different altitude ranges, including some far-away cells. And measuring L1 RS resources from multiple candidate cells would cause large UE power consumption.
  For Rel-18 UAV, height-dependent measurement resource configuration has been introduced for RRM measurement to indicate the specific measurement resources in different altitude ranges. The similar mechanism can be considered for L1 measurement, as well as early sync resources for LTM candidate, to enable more effective LTM preparation and triggering for UAV UE.
Detailed objective on Mobility enhancements [RAN2, RAN3]:
  Specify CHO enhancements, e.g. height-based and/or flight-path based CHO triggering events;
  Specify LTM enhancements, e.g. height-dependent L1 measurement configuration and/or candidate configuration for LTM.

## Slide 4
Potential objective: Mitigation of RLFs due to NTZ
Overview：
  At RAN#104, the following principles were agreed for NTZ:
    RAN is not involved in process of informing or enforcing NTZs
    UE is responsible for following NTZ regulations
  Subsequently, at SA2#164 a UE based solution was agreed for key issue#3 for NTZ (see S2-2409542)
    As a result of the above, NTZ regulations will enforced by the UE upon entering an NTZ (which is five dimensional – 3D in space + frequency and time)
    Upon entering NTZ, the UE does not transmit any signalling or data
    If in connected mode, this means that there will be a radio link failure
      Note that although DL quality of the cell may be good, RLF will be detected in NW due to lack of UL
      When NW detects such RLF, it may also release the UE context both in RAN and CN
      Number of RLFs is a key KPI in the network and deterioration in this KPI is not desirable
      Since the UE is aware of the NTZ information, UE should be able to mitigate this impact, e.g. by indicating to the network that the quality of the current frequency/cell is no longer good before entering the NTZ
Detailed objective on mitigating RLFs due to UE entering NTZ:
  Specify UE based mechanisms to mitigate the radio link failures due to the UAV UE entering NTZ [RAN2]
    NOTE: The solution should not result in RAN receiving the NTZ information or require RAN to enforce UE behaviour when it is located within the NTZ(s) and should be complimentary to any solutions that SA2/CT1 develop for this.

## Slide 5
Potential objective: UAV identification & status report
Overview：
  To enable the application, e.g., trajectory recognition, for the aerial UE, it is necessary that gNB knows the aerial UE specific identification, and it can be used to match the aerial UE identification for communication and the aerial UE identification. Besides, the gNB has no idea whether the UE supports aerial capable function until reception of the UE capability report. Early identification of aerial capable UE can help the gNB to select AMF supporting aerial service.
  The aerial UE should be identified and may require separate handling by operator. To adequately support aerial UE, gNB may conduct specific measurements for the aerial UE and send measurement data to 5GC. This allows the network to provide further assistance to aerial UE.
Detailed objective on UE identification：
    Support aerial UE identification management [RAN3, RAN2]
    Specify signaling and procedures for aerial UE to report aerial UE identifier to gNB, e.g. reporting remote ID, aerial UE indication.
    Specify signaling and procedures for delivering the aerial UE related information (e.g., UE identifier, altitude and velocity information) in both split and non-split gNB architectures, between 5GC and gNB, and between gNBs.

## Slide 6
Summary & Objectives
According to the previous discussion, as one additional RAN2-led topic in Rel-20, the following proposed objectives:
  Support mobility enhancements for aerial UE [RAN2, RAN3]:
    Specify CHO enhancements, e.g. height-based and/or flight-path based CHO triggering events;
    Specify LTM enhancements, e.g. height-dependent L1 measurement configuration and/or candidate configuration for LTM.
  Support enhancement to mitigate RLFs due to UE entering NTZ [RAN2]:
    Specify UE based mechanisms to mitigate the radio link failures due to the UAV UE entering NTZ.
    NOTE: The solution should not result in RAN receiving the NTZ information or require RAN to enforce UE behaviour when it is located within the NTZ(s) and should be complimentary to any solutions that SA2/CT1 develop for this.
  Support aerial UE identification management [RAN3, RAN2]
    Specify signaling and procedures for aerial UE to report aerial UE identifier to gNB, e.g. reporting remote ID, aerial UE indication.
    Specify signaling and procedures for delivering the aerial UE related information (e.g., UE identifier, altitude and velocity information) in both split and non-split gNB architectures, between 5GC and gNB, and between gNBs.
Potential estimated TU:
Working group | TU
RAN2 | 0.5 TU
RAN3 | 0.5 TU

## Slide 7: Thanks