## Slide 1: Views on MIMO for Rel. 20
RP-250650
3GPP TSG RAN #107
Incheon, Korea, March 12-14, 2025
Agenda Item: 15.2.2
Source: CEWiT

## Slide 2
© CEWiT 2025
2
CSI-RS Overhead Reduction
Motivation
In Rel. 19, number of CSI-RS ports have been extended to 128
The resource overhead increases proportionally with the number of ports
Increased resource overhead effects the overall system performance
Methods to reduce the CSI-RS resource overhead at least for periodic CSI-RS should be studied in Rel. 20
Proposal
Specify at least one of the following schemes to facilitate CSI-RS overhead reduction for periodic CSI-RS and associated reporting without changes to the existing precoders
  Schemes based on sounding of partial panel
  Schemes based on adaptive frequency and time density
  Schemes based on virtualization

## Slide 3
© CEWiT 2025
3
UL Precoder Enhancements
Motivation
Uplink performance has been a bottleneck in NR for various reasons
Uplink performance is heavily impacted by the constraints in the UL precoder design such as
  Only Wideband precoder can be used
  Low-resolution precoders are used
With the introduction of CPE devices (up to 8Tx antennas), the precoder design for UL should be enhances to fully exploit the increased number of Tx antennas
Rel. 20 should study methods to improve uplink performance by enhancing the precoder design
Proposal
Specify UL precoder enhancements for facilitating at least one of the following
  Subband based precoding
  High resolution wideband precoding