## Slide 1: Views on Network Energy Saving for Rel. 20
RP-250653
3GPP TSG RAN #107
Incheon, Korea, March 12-14, 2025
Agenda Item: 15.2.7.2
Source: CEWiT

## Slide 2
© CEWiT 2022
2
Introduction
Adapting the transmission/reception procedures at gNB to reduce energy consumption
  Based on traffic condition, UE feedback/assistance information, etc.
Motivation:
  Reduce energy consumption of network
  Reduce operational cost and environmental impacts
Rel. 18 studied various energy saving techniques in time, frequency, spatial and power domains
  Defined evaluation procedure, metrics and KPIs
  Analyzed various energy saving techniques in terms of Energy saving gains, effect on legacy operation and specification impacts.
The outcome of the study is captured in TR 38.864

## Slide 3
© CEWiT 2022
3
State of art
Rel. 18 WI focused on
  Adaptation of DTX/DRX pattern for gNB (Technique A-4)
    Configuration and activation/deactivation of DTX/DRX pattern
    Impact on various signals/channels and UE behavior
  Adaptation of spatial elements (Technique C-1)
    Port adaptation and TxRu adaptation
    Procedures and Configuration for determining the adaptation pattern
      Impacts on CSI-RS measurement and reporting framework
    Signaling exchanges and UE behavior
  Power adaptation (Technique D-1)
    Procedures and Configuration for determining the adaptation pattern
      Impacts on CSI-RS measurement and reporting framework
    Signaling exchanges and UE behavior

## Slide 4
© CEWiT 2022
4
State of art cont’d…
Rel. 19 WI focused on
Adaptation of SSB and PRACH in time domain
  Dynamic adjustment of SSB burst periodicity for SCell based on network conditions
    Configuring two SSB patterns: one with large and one with small periodicity
    Switching between the SSB patterns based on network condition
  Introduction of additional PRACH resources.
    Procedures and signalling exchanges for dynamic activation/deactivation of the additional resources.
On-demand SSB in SCell for UEs in connected mode
  Adaptation comprises enabling/disabling transmission of SSB in Scell by the gNB
  Procedures for on-demand SSB
    Configuration and Signaling exchanges for on-demand SSB
On-demand SIB1 in Scell for UEs in idle/inactive mode
  Case 2: UE obtains wake up signal (WUS) configuration from Cell A, UE transmits UL WUS on NES Cell, and UE receives on-demand SIB1 from NES Cell
  Procedures for On-demand SIB1
    Signaling and content of WUS configuration
    Details on transmission of SIB1 and UE behavior for different scenario.

## Slide 5
Rel. 20 NES Proposals

## Slide 6
© CEWiT 2022
6
On-demand SSB for IDLE/INACTIVE UE
Motivation
  Rel. 19 supports on-demand SIB1 in Scell based on UL WUS from UE
  Rel. 19 on-demand SSB is applicable only for NCD SSB and UEs in connected mode
  In both cases, the gNB still need to transmit CD-SSBs periodically (e.g. with 20 ms periodicity) for synchronization
    Reduces sleep time of gNB and restricts energy saving gains
  Turning off SSB transmissions allows for deeper sleep at the gNB and greater NES gain
On-demand SSB for Idle/Inactive UE should be supported in Rel. 20
  gNB transmitting SSB based on WUS
  Provide significant energy saving gains as observed in TR 38.864, as shown below.
    For UEs in RRC_IDLE/INACTIVE without C-DRX and no DL transmission including SSB before WUS reception, NES gains reach 83.7% (52.5%) with Cat-1 (Cat-2) BS power model at zero or low load.
  Considered in Rel. 19 and dropped due to time constraints and lack of consensus

## Slide 7
© CEWiT 2022
7
On-demand SSB for IDLE/INACTIVE UE
On-demand SSB for multi cell scenarios:
  Extend the On-demand SIB1 framework in Rel. 19 to SSB
  NES cell transmitting SSB on request from UE
    UE transmit UL-WUS to request SSB
    UE can transmit a UL-WUS to NES Cell or Anchor Cell
  The UE receives WUS configuration from Anchor Cell.
  gNB monitors for WUS on NES Cell based on the configuration.
Impact on legacy UE is minimum
  Legacy UE can use SSB of anchor cell for initial access
  In case NES cells not serving legacy UEs
Fig. 1: On-demand SSB in multi cell scenario

## Slide 8
© CEWiT 2022
8
On-demand SSB for IDLE/INACTIVE UE
Proposal 1
  Specify procedures and signaling method(s) for On-demand SSB for IDLE/INACTIVE UE in multi cell scenarios [RAN1/2]
    UE obtains UL WUS configuration from Anchor Cell, UE transmits UL WUS on Anchor Cell, UE receives on-demand SSB from NES Cell

## Slide 9
© CEWiT 2022
9
  Motivation
  Rel-18 DTX/DRX is limited to specific signals, such as PDSCH and a subset of PDCCH.
  Rel-18 DTX/DRX is not applicable to common signals such as SSB
    Transmissions of common signals reduces sleep time of gNB
    Results in frequent switching between active and sleep states
    Reduces NES gains significantly
    Sparser SSB transmission occasions, when longer periods are enabled, impacts meaurements and performance at UE
  Rel. 19 considered adaptation of cell specific signals under certain scenarios (E.g., multi cell scenario, adaptation of NCD SSBs, etc.)
  Extending Cell DTX/DRX operation to common signals in multi cell scenario should be supported in Rel.20
  A multi cell scenarios with Pcell (Anchor cell) and SCells (NES cells) can be considered.
  Cell DTX/DRX pattern can be enabled for common signals of SCells (NES cells)
  gNB transmit SSB only during active period of the cell DTX/DRX pattern and no transmissions during inactive period
  Impact on legacy UEs is minimum
    legacy UEs can be served by the SSBs in PCell (Anchor cell)
    In case Scell (NES cell) is not serving legacy UEs
Enhancements for DTX/DRX Adaptation

## Slide 10
© CEWiT 2022
10
Enhancements for DTX/DRX Adaptation:
Proposal 2
  Specify procedures and signaling methods for extending Cell DTX/DRX operation to common signals in multi cell scenario
  Transmission of SSBs with certain periodicities within active period of cell DTX/DRX pattern and no transmission in non active period
  Increasing reliability of activation/deactivation of cell DTX/DRX pattern

## Slide 11
© CEWiT 2022
11
Enhancements for SSB adaptation within a burst:
Motivation
  Rel. 19 SSB adaptation is at SSB burst level with minimum flexibility
    Number of SSBs and SSB indices are same in SSB burst with higher and lower periodicities
  The network conditions (E.g., load, UE arrival rate, etc.) can vary across SSB beams within a burst
  Dynamic switching to lower/higher periodicity may not be needed for all beams within a burst
Rel. 19 SSB adaptation should be extended to SSB beams within a burst
  Number of SSBs and SSB indices in SSB bursts with lower and higher periodicities can be different
  Adaptation of SSBs within a burst was discussed in Rel.19 and dropped due to time constraints
    Adapting number of beams within SSB burst
    Periodicity adaptation for SSB beams
  Impact on legacy UE is minimum, if enabled for multi carrier scenario and for SSB configuration not applicable for legacy UE

## Slide 12
© CEWiT 2022
12
Enhancements for SSB adaptation within a burst:
Performance evaluations
  Performance is evaluated in a 21 cell deployment using Energy consumption model with set 1 and category 1 defined in TR. 38.864.
    Transmission of SSB burst, with constant number of active beams, with 20ms periodicity is assumed as baseline.
    Adaptation includes an always-on SSB burst with 160 ms periodicity and an additional SSB burst with 20 ms periodicity and fewer/no active beams based on load.
  Figure 2 represent an average NES gain of 33.5% observed for low and light load scenarios with average throughput degradation of -16.3%.
Fig. 2: SSB adaptations within a burst
Chart: Adaptation of transmitted SSBs in a burst
| 0.1 | 0.2
Energy Saving | 0.3518 | 0.3192
Throughput loss | -16.8 | -15.89

## Slide 13
© CEWiT 2022
13
Extend Rel. 19 SSB time domain adaptations to beam(s) within an SSB burst
  Adapt the number of transmitted SSBs and SSB indices for the SSB burst with lower and higher periodicities
  Procedures and signaling methods for extending SSB time domain adaptations to beam(s) within an SSB burst
Enhancements for SSB adaptation within a burst:
Proposal 3

## Slide 14
© CEWiT 2022
14
Adaptation of Transmission Reception Points
Multi-transmission/reception point (m-TRP) was introduced in Rel. 16
  M-TRP can improve the reliability and throughput, especially in cell edge scenario
  Rel. 18 studied dynamic switching between single TRP and m-TRP operation for NES (Technique C-2)
  Significant energy saving is observed in TR 38.864 as given below
    Semi-static TRP adaptation: 36.9 % ~ 41.6 %
    Dynamic TRP adaptation: 19.7 % ~ 28.7 %
  No impact on legacy UE is foreseen, if implemented for UE specific signals/channels
Support adaptation of the number of TRPs transmitting and/or receiving signals and channels
  Dynamic switching between single-TRP and m-TRP operation based on network condition
  Procedures and signaling methods for adapting number of TRPs transmitting and/or receiving signals and channels

## Slide 15
© CEWiT 2022
15
Adaptation of Transmission Reception Points:
Proposal 4
Support adaptation of the number of TRPs transmitting and/or receiving signals and channels
  Dynamic switching between single-TRP and m-TRP operation based on network condition
  Procedures and signaling methods for adapting number of TRPs transmitting and/or receiving signals and channels

## Slide 16
© CEWiT 2022
16
Summary
  Proposal 1: Specify procedures and signaling method(s) for On-demand SSB for IDLE/INACTIVE UE in multi cell scenarios [RAN1/2]
  UE obtains UL WUS configuration from Anchor Cell, UE transmits UL WUS on Anchor Cell, UE receives on-demand SSB from NES Cell
  Proposal 2: Specify procedures and signaling methods for extending Cell DTX/DRX operation to common signals in multi cell scenario
  Transmission of SSBs with certain periodicities within active period of cell DTX/DRX pattern and no transmission in non active period
  Increasing reliability of activation/deactivation of cell DTX/DRX pattern
Proposal 3: Extend Rel. 19 SSB time domain adaptations to beam(s) within an SSB burst
Adapt the number of transmitted SSBs and SSB indices for the SSB burst with lower and higher periodicities
Procedures and signaling methods for extending SSB time domain adaptations to beam(s) within an SSB burst
Proposal 4: Support adaptation of the number of TRPs transmitting and/or receiving signals and channels
Dynamic switching between single-TRP and m-TRP operation based on network condition
Procedures and signaling methods for adapting number of TRPs transmitting and/or receiving signals and channels
Following NES techniques are supported for WI phase in 5G-A in Rel. 20

## Slide 17
© CEWiT 2022
17
Thank You