## Slide 1: Release-20 NR Sidelink Relay Enhancements for Public Safety
RAN#107, Incheon, South Korea March 12-14, 2025
RP-250156
FirstNet, AT&T, LG Electronics, Kyocera International, SOFTIL, SyncTechno Inc., Netherlands Police, Norwegian Communication Authority, Motorola Solutions, UK Home Office, National Institute of Standards and Technology (NIST)

## Slide 2: Background: multi-hop SL Relay Enhancement for Public Safety
We consider public safety use cases and their requirements to facilitate mission critical Prose/D2D communications among public safety personnel in all coverage scenarios including off-network.
Release-18 (R18) NR SL U2U solution is not sufficient to provide much-needed coverage extension for out-of-coverage public safety personnel for mission critical public safety use cases due to terrain limited coverage.
Public safety community has been requesting the support for multi-hop relaying since Release-17. As captured in 'RP-213496 Moderator's summary of discussion [94e-16-R18-SLRelayEnh]', RAN Chair's suggestion was "focus on single hop; multi-hop is then rather for future REL".
Both U2N and U2U multi-hop features were requested in R19, but due to 1TU allocation, only U2N was added in the package.
In public safety community’s opinion, R20 is the right time to incorporate multi-hop U2U SL Relay enhancement to ensure communication to public safety personnel who are otherwise not reachable by R18 single-hop SL U2U Relaying. Any delay will deprive public safety personnel an important tool. Public safety has a concern that if this feature is not included in R20, it may be difficult to include in near future releases due to focus on new areas for 6G

## Slide 3: U2U multi-hop NR SL Relay Enhancement for Public Safety
This scenario presents a public safety use case requiring multi-hop U2U relaying to facilitate mission critical Prose/D2D communications among public safety personnel in an off-network areas.
In this scenario, there is a group of fire fighters that parachute into a remote mountainous wilderness to fight a forest fire. The fire fighters spread out across the fire line that spreads over several mountains. Due to the location, there is no network coverage but the need to communicate is high so they can keep each other informed of the conditions. The ability to support both private 1-to-1 calling, and group calling is mission critical to the fire fighter’s safety and enable them to do their job.
Release-18 SL U2U single-hop relay is not sufficient to reach each other by 1-hop SL coverage range. Multi-hop SL U2U relaying (at least two additional hops/relays on top of Release-18 relay) is necessary to ensure communication among fire fighters.
Source Remote UE
Target Remote UE
Public safety use case requiring multi-hop U2U relaying (two additional U2U Relays)
U2U
Relay UE
U2U
Relay UE
U2U
Relay UE

## Slide 4: Objectives and Proposal for SL Relay Enhancement for Public Safety
We consider public safety use cases and their requirements to facilitate mission critical Prose/D2D communications among public safety personnel in all coverage scenarios including off-network in R20.
Our Objective is to enhance R18 NR SL U2U Relaying feature to multi-hop SL U2U for secured L2-based relaying in R20.
Proposal: RAN Plenary agree to include enhancements for NR Sidelink secured L2-U2U multi-hop relay as a part of the Rel-20 package.

## Slide 5
Thank you!