## Slide 1: Motivation for New WI MBMS support for EN-DC
3GPP TSG RAN Meeting #78
Lisbon, Portugal, December 18 - 21, 2017
Agenda item: 9.1.2

## Slide 2: Motivations
Cellular system is overwhelming conventional terrestrial broadcast
  There are nowadays many users who watch TV programs by using smartphones or tablets instead of conventional TV screens. The percentage of those users is highly increasing in many countries
Many users are consuming TV/video on demand nowadays by using unicast bearers for eMBB.
  It is not likely that multiple users are consuming same contents at the same time. This chance in which broadcast transmission is beneficial would normally happen only in hot spot.
NR can provide higher quality of services than LTE MBMS e.g. for eMBB and V2X
  NR MBMS can provide more numbers of UHD TV channels and higher capacity over NR resources for basic V2X service in dense areas
In REL-14 study on V2X, it has been identified that small area broadcast is much beneficial than large area broadcast and unicast transmissions.
  Large area broadcast requires high resource capacity to broadcast V2X messages in a range of several hundreds of meters from a source UE
  Many small clusters of MBMS areas should be configured to provide V2V service over MBMS

## Slide 3: MBMS in a hot spot
For initial 5G, it is interesting to deploy NR gNBs for capacity boosting as the secondary node of EN-DC.
Offloading PTP traffic to PTM traffic is beneficial in a hot spot during prime time, e.g. Football/Baseball Stadium and Apartment/Condominium where (many) multiple users are likely interested in the same content at the same time.
Support of MBMS over NR SgNB can provide efficiency. However, E-UTRAN supporting EN-DC cannot currently use NR SgNB resource to provide MBMS services.
Macro LTE cell
Small NR cell
Small NR cell
Stadiums
Apartment/Condominium

## Slide 4: MBMS for basic V2X service
The study on V2X concluded that it is feasible to support transport for V2V, V2I/N and V2P services over Uu. However, capacity problem of LTE MBMS has been identified in TR36.885 for Uu transport of basic V2X service:
  “Unicast cannot meet the capacity requirements for Urban cases and Freeway cases option 1.“ (ISD for urban = 500m, ISD for Freeway option 1 = 1732m)
It is useful to use MBMS for support of V2X over Uu. However, NR does not support MBMS service on the radio, yet. Thus, basic V2X service provided by MBMS bearers cannot use SCG resource in EN-DC.
NR PDSCH designed for unicast could be used to support V2X service over MBMS as well as eMBB.
  CoMP-like solution is already considered in NR PDSCH, noting that CoMP based MBMS has been studied in the Rel-14 study on V2X.
  Small area of MBMS broadcast should be the main target for V2X, considering that large area of MBMS broadcast is not essential and may cause capacity problem.

## Slide 5: MBMS based on EPC
MBMS is currently based on EPC. Since EPC supports no direct interface with NR RAT, MBMS cannot be supported in standalone NR for the timing being.
  NR gNB cannot join IP multicast of a MBMS service provided by MBMS CN nodes in EPC.
MBMS service area
LTE
eNB
NR
gNB
“NR RAT is not connected to EPC for control plane”
EPC
LTE
eNB
BM-SC

## Slide 6: NR MBMS based on EPC
MBMS service can be enabled in NR RAT by leveraging LTE MeNB based on EPC MBMS architecture in REL-15
  MBMS service could be served by unicast radio bearer over SCG cells in EN-DC (probably without any standard impact), if LTE MeNB supports MBMS.
  However, we need some work to support MBMS radio bearer over SCG cells in EN-DC
MBMS service area
NR MBMS
EN-DC
UE
NR
UE
EPC
BM-SC
MeNB
SgNB
EN-DC

## Slide 7: NR PDSCH design for MBMS
The L1 design agreed by RAN1 will support broadcast on NR PDSCH from multiple TRPs only with very minor impact. No additional L1 channel is needed for small area MBMS broadcast.
  RAN1 agreement on NR reception:
  Single NR-PDCCH schedules single NR-PDSCH where separate layers are transmitted from separate TRPs
  Multiple NR-PDCCHs each scheduling a respective NR-PDSCH where each NR-PDSCH is transmitted from a separate TRP
  Note: the case of single NR-PDCCH schedules single NR-PDSCH where each layer is transmitted from all TRPs jointly can be done in a spec-transparent manner
  Note: CSI feedback details for the above case can be discussed separately
MBMS transmission on NR PDSCH from the same gNB could be quickly specified in REL-15 for basic V2X service and eMBB use cases.

## Slide 8: Proposed WI objectives for NR MBMS in EN-DC
Specify MCCH/MTCH mapped to PDSCH over NR SCG cells (RAN2, RAN1)
Specify mapping LTE MBMS EPS bearer onto NR radio bearer (RAN2, RAN3)
Enable ‘basic’ NR MBMS transmissions on PDSCH (RAN1, RAN2)
Specify necessary signaling for MBMS transmission (RAN2, RAN3)

## Slide 9: Proposed Work Plan
Approve the work item on NR MBMS in EN-DC connected to EPC for the last stage of REL-15 or the earliest stage of REL-16
  0.5 TU per meeting is requested for RAN1, RAN2 and RAN3, assuming that LTE MBMS is considered as a baseline.
Consider the study on MBMS in standalone NR connected to 5GC in REL-16.