## Slide 1
Motivation for new WI: Enhancements on scheduling and control for NR
3GPP TSG RAN Meeting #78
Lisbon, Portugal, December 18 - 21, 2017
Agenda Item: 9.1.1
RP-172511

## Slide 2: Motivation
More flexible, low-latency scheduling for multi-service provision is a key advantage of NR over LTE.
An innovative scheduling/resource allocation framework was settled down in R15 by introducing new tools, e.g. BWP and symbol-level scheduling.
In order to limit DCI overhead meanwhile realizing the flexible scheduling, a signaling framework of “RRC-configured resource set + DCI-based indexing” is employed.
However, due to the expedited standardization process (leading to a cautious design principle) in R15, the potential of the two tools were not fully exploited, e.g.
  Only a single resource table/set can be configured for PDSCH/PUSCH/PUCCH.
  Only contiguous time resource allocation is supported.
  Only single active BWP is supported for a UE.
Further enhancements on the time and frequency resource allocation should be taken into account in R16 NR, together with some other potenital improvements on PDCCH/PUCCH.

## Slide 3: Multiple resource sets/tables (1)
The challenge of NR resource allocation is the limited number of configurable resources (16 for PDSCH/PUSCH and 8 for PUCCH) covering diverse use cases due to bitwidth in DCI.
Configurable resources for all cases are constrained in a single resource set.
Example for R15 NR
BWP 1 BWP 2
BWP 3 BWP 4
PDSCH type A
PDSCH type B
CP-OFDM
DFT-s-OFDM
Long-duration resources (e.g. ≥4 symbols)
Short-duration resources (e.g. 1-3 symbols)
Single resource set/table
Agreement in RAN1#91 meeting:
  Only a single resource set/table is configurable in R15 NR for a PHY channel.
  Number of each type of resources (e.g. long or short-duration) is very limited.
  Not all durations and staring symbols are well supported.

## Slide 4: Multiple resource sets/tables (2)
Long-duration resources
Resource set 2
In R16 NR, multiple configurable resource sets for different use cases can provide N-fold increase of configurable resources, and then more scheduling flexibility and reduced resource collision.
  Use legacy PHY differentations (e.g. active BWP, PDSCH mapping type, UL waveforms) and no additional DCI overhead is needed.
1-symbol duration, transmission starting from any symbol and multi-slot scheduling with different symbol allocations in different slots can be supported in R16 NR.
Different resource sets/tables can be configured for different BWP configurations, PDSCH mapping type A and B, UL CP-OFDM and DFT-s-OFDM.
Example for R16 NR
BWP 1 BWP 2 BWP 3 BWP 4
PDSCH type A
PDSCH type B
Long-duration resources
Short-duration resources
Resource set 1
Short-duration resources
Resource set 4
Resource set 3
Resource set 6
Resource set 5
Resource set 8
Resource se 7

## Slide 5: Non-contiguous time resource allocation (1)
5
“Fragmented resource” issue in NR: Due to semi-static DL/UL assignment, dynamic SFI and multiplexing between long and short durations.
Since only contiguous resource allocation is supported in R15, the fragmented resource cannot be effectively scheduled.
Example for R15 NR
Agreement in RAN1#90 meeting:
  Starting symbol + number of symbols
  Starting slot + number of slots
UE-side determination of available slots/symbols based on DL/UL assignment or SFI is not specified for PDSCH/PUSCH with concerns about robustness (specified for multi-slot PUCCH).
↓ | ↓ | ↓ | ↓ |  | ↑ | ↑ | ↓ | ↓ | ↓ | ↓ |  | ↑ | ↑
SFI
DL resource allocation
Fragmented DL resource due to SFI
DL grant 1
DL grant 2
Slot
To schedule fragmented DL resource, two DL grants are needed with doubled DCI overhead.
DL resource allocation
Fragmented DL assignment due to multiplexing between long and short durations
DL grant 1
for UE1
Slot
DL grant 2
for UE1
UE2’s transmission

## Slide 6: Non-contiguous time resource allocation (2)
In R16 NR, fragmented time resource can be scheduled with two options:
  Option 1: Support non-contiguous resource allocation, e.g. slot/symbol-level bitmap
    Slightly larger RRC overhead. No additional DCI overhead.
    Subframe-level bitmap has been specified for NB-IoT
  Option 2: Support UE-side determination of available slots/symbols based on DL/UL assignment or SFI.
Example of Option 1:
Bitmap-based resource allocation
Slot
1 1 1 1 1 0 0 0 1 1 1 1 1 1
Symbol-level bitmap
Example of Option 1:
UE-side determination of Bitmap-based resource allocation
Slot
↓ | ↓ | ↓ | ↓ |  | ↑ | ↑ | ↓ | ↓ | ↓ | ↓ |  | ↑ | ↑
SFI
Determined symbols by UE based on SFI
A number of symbols indicated by DL grant

## Slide 7: Multiple active BWPs for a UE
Frequency
R15 NR
Focus on “single active BWP” case.
Agreement in RAN1#90 meeting:
Time
BWP1 (SCS=15kHz)
R16 NR
“multiple active BWPs” case can be taken into account to support more effective multi-numerology transmission for multi-service provision.
  Enable fast switching between different numerologies without BWP switching (TDM)
BWP2 (SCS=60kHz)
Frequency
Time
BWP1 (SCS=15kHz)
  Enable simultaneous transmission between different numerologies (FDM)
BWP2 (SCS=60kHz)

## Slide 8: Enhancements on NR control channels
PDCCH enhancements
  DCI formats for PHY commands
  2-stage DCI
PUCCH enhancements
  HARQ-ACK UCI compression:.
    For CBG-based transmission, varied transmission durations and carrier aggregation
    Dynamic HARQ-ACK codebook based on the actual number of scheduled PDSCHs and the actual number of scheduled CBGs in each PDSCH
      Reduce HARQ-ACK payload ,and thus improve PUCCH coverage
    Multi-level HARQ-ACK compression
      Avoid the restriction on DL scheduling caused by the limitation of PUCCH, adapt to various coverage requirements, and minimize DL efficiency loss
  HARQ-ACK in PUSCH in case DL grant after UL grant