## Slide 1
3GPP TSG RAN Meeting #78
Lisbon, Portugal, December 18 - 21, 2017
RP-172513
Motivation for new WI: Enhancements on URLLC services for NR

## Slide 2: Background: URLLC in Rel15
Rel15, the first release supporting Non-standalone NR, is planed to freeze at RAN#78.
URLLC is one of key features for 5G. In Rel-15 NR, the fundamental mechanisms of URLLC were discussed:
  Non-slot based data transmission and scheduling
  Multiplexing data with different transmission duration
  Self-contained subframe
  Grant free transmission
  SR enhancement
  PDCP duplication
However, system reliability enhancement, system efficiency optimization and enhancement on specific scenario(i.e uplink power limitation) may not be fully discussed and specified during Rel-15.
Further study on the URLLC enhancement shall be taken into account in Rel-16 NR work item.

## Slide 3: Scope of URLLC enhancement
URLLC enhancement for Rel16 includes the following items:
  System reliability enhancement
  Grant free capacity optimization
  Non-slot transmission optimization
  Uplink coverage improvement

## Slide 4: System reliability enhancement
Reason for System reliability enhancement
  As the number of potential users or the traffic arrival rate increases, resource congestion will occur. And resource congestion leads schedule latency, which may not be acceptable by URLLC and impacts reliability of URLLC.
  To meet high reliability requirement, redundant resource allocation, such as K repetition is agreed in Rel15 to achieve robust transmission. However, it will further increase risk of resource congestion.
Possible enhancements
  Support fast CSI feedback
    Evaluate system performance of fast CSI feedback
    If needed, specify signaling procedure and mechanism on fast CSI feedback
  Support flexible and advanced multi-user multiplexing
    Evaluate system performance of flexible and advanced multi-user multiplexing scheme
    If needed, specify orthogonal/non-orthogonal signature
    If needed, specify signalling procedure and mechanism on flexible and advanced multi-user multiplexing

## Slide 5: Grant free capacity optimization
Reason for Grant free capacity optimization
  The multi-user multiplexing mainly relies on spatial multiplexing, which is restricted by UE distribution and the knowledge of instantaneous channel state information (CSI) of frequency-selective fading. Therefore, multiplexing capacity is very limited.
  Collision randomization mechanism is introduced in grant free, such as UE-specific hopping pattern. However, if the number of potential users for grant-free transmission is high or the traffic arrival rate is high, the transmission reliability will be poor .
Possible enhancements
  Support flexible and advanced multi-user multiplexing
    Evaluate system performance of flexible and advanced multi-user multiplexing scheme
    If needed, specify orthogonal/non-orthogonal signature
    If needed, specify signalling procedure and mechanism on flexible and advanced multi-user multiplexing

## Slide 6: Non-slot transmission optimization
Reason for Non-slot transmission optimization
  Non-slot transmission is usually used for URLLC to reduce latency. And 2-symbol PDSCH/PUSCH, is a typical use case.
  DMRS design in Rel15 focuses on slot and non-slot data transmission with longer duration . The ratio of DMRS resource element and data resource element is about 10% for slot and non-slot data transmission with longer duration. But for 2-symbol data transmission, the ratio of DMRS resource element and data resource element becomes large .
  In addition, Control channel overhead is also too large for 2-symbol data transmission.
Possible enhancements
  Support flexible DMRS structure
    Evaluate link level performance of flexible DMRS structure
    If needed, specify signaling procedure and mechanism on flexible DMRS structure.
  Support Grant free transmission in downlink
    Study and specify grant free transmission in downlink.

## Slide 7: Uplink coverage improvement
Reason for Uplink coverage improvement
  Better fulfill the 95% coverage requirement by ITUR for URLLC, including DL and UL. However, due to uplink maximum transmit power is limited, which is much less than downlink maximum transmit power, uplink coverage will be the bottleneck of system coverage.
  In LTE, repetition is used to improve uplink coverage. However, due to low latency requirement for URLLC, repetition number is limited and uplink coverage issue can not be resolved completely.
Possible enhancements
  Support advanced UL receiver
    Evaluate system performance of advanced UL receiver, such as Multi-panel receiver and UL CoMP.
    If needed, specify signaling and mechanism on advanced UL receiver.
  Support enhanced power control mechanism and power-efficient techniques.
    Study and specify enhanced power control mechanism and power-efficient techniques

## Slide 8
Thanks!