## Slide 1
Title: Motivation for New WI on Power Class 2 UE for LTE bands 31 & 72
Source: Nokia, ArgoNET
Document for: Information
Agenda Item: 10.1.5
3GPP TSG RAN Meeting #83 RP-190292
Shenzhen, China, March 18-21, 2019

## Slide 2: Motivation 1/2
450MHz LTE bands are being refarmed & deployed globally with a focus on critical voice and MTC services
  e.g. PPDR, PMR and critical MTC/IoT applications requiring very high coverage probability
Performance of antennas in 450MHz can be limited by small device size (e.g. IoT sensor, metering device) which needs to be compensated
  Coverage Enhancement Modes cannot be used in many cases due to stringent latency requirements (e.g. real-time monitoring for smart grid, critical voice services, …)
  However many 450MHz use cases are not constraint by battery power (e.g. electricity smart meter, alarm panel, industrial router, …)
Typically 450MHz UE do require discrete RF front-end design which is implemented in addition to mainstream cellular bands / FEM solutions
  This gives more flexibility for device suppliers to implement different UE power class configurations depending on the use case

## Slide 3: Motivation 2/2
Power Class 1 with 31dBm already standardised for B31 & B72
  Mainly driven by PPDR vehicular modem designs, however
    PC1 not suitable for low cost UE designs built on COTS SAW components
    PC1 does not allow for small form factor designs e.g. required in MTC
Power Class 2 with 26dBm has been standardised for TDD bands
  e.g. HPUE already introduced for B41
Power Class 2 is feasible to be implemented also for FDD bands
  e.g. by targeting only non-hand held form factors similarly as PC1

## Slide 4: Scope of the WI
New Work Item to introduce new power class for LTE bands 31 & 72
  specify UE power class 2 with +26dBm
  include LTE and eMTC UE categories
  consider full- and half duplex FDD operation for eMTC
  power class 2 is not targeted for smartphone/handheld form factor