## Slide 1
Views on NR light in Rel-17
3GPP TSG RAN Meeting #85 RP-191902
Newport Beach, USA, September 16-20, 2019
Agenda item: 8.2.1
Notes: 1st,

## Slide 2: Use cases and design requirements for NR light
Use cases
  Smart wearable, e.g. smart watch, glasses, health care
  Low end smartphones
  Smart home appliances
  High end MTC
Key design requirements
  Peak data rate: target peak data is scenario dependent.
    Relatively lower data rate for smart wearables, 10~100Mbps
    Higher data rate for low end smartphones, e.g. 200Mbps
  UE power consumption, e.g. target for 2 week battery life for smart watch with typical usage (not standby only), with low battery capacity (e.g. <500mAh)
  Reduced device complexity and cost
  To enable a device design with smaller form factor
  Typical eMBB service latency
  Seamless switching/service continuation across different devices, especially for wearable use case, e.g. a voice call to a smart watch can be switched to a smartphone without significant interruption, or vice versa.
  The potential use cases for NR-light UEs are expected to be diverse, it is important to have a study phase to discuss and document the different use cases together with the key requirements.

## Slide 3: Potential enhancements for NR-light
UE complexity reduction techniques
  Reduced UE supported BW by reusing Rel-15 initial access design, e.g. DL BW down to 5MHz/10MHz for 15KHz/30KHz in FR1. UE capability of supported DL BW and UL BW should be decoupled.
  Efficient operation for reduced bandwidth Ues in a wideband system, including co-exitence with wideband Ues.
  Reduced UE Rx antennas, including 1Rx and 2Rx
  UE catetories targeting different data rates
  PDCCH monitoring capability reduction
  Relaxed UE processing time capability
Further UE power saving beyond Rel-16 for RRC IDLE/INACTIVE and RRC CONNECTED states, details refer to [1]
New UE power class with lower Tx power
  A UE design with integrated transceiver and PA can be enabled by a lower Tx power class, which provides significant benefit for reducing device size and cost
Coverage compensation focusing on coverage loss due to NR-light features, for example reduced UE Rx antenna, reduced BW, lower UE Tx power class, etc.
Seamless switching/service continuation across different devices

## Slide 4: Other considerations
The potential scope of NR-light may overlap with other Rel-17 working areas
  The power saving features proposed in NR light overlap with the Rel-17 further enhanced UE power saving.
    The UE power saving features should be commonly applicable for both NR-light UEs and normal smartphones.
  The coverage compensation features proposed in NR light overlap with the Rel-17 coverage
    The coverage enhancement features should be commonly applicable for both NR-light UEs and normal smartphones.
Reference
  [1] RP-191901, Views on Further enhanced NR UE power saving in Rel-17, vivo

## Slide 5
Thanks