## Slide 1
Potential RAN1 scope adjustment for Rel-16 eURLLC and IIOT
3GPP TSG RAN Meeting #85 RP-191906
Newport Beach, USA, September 16-20, 2019
Agenda item: 9.4.5
Notes: 1st,

## Slide 2: Overall progress of eURLLC and IIOT WI in RAN1
WI | Objectives | Progress achieved so far | Remaining work to be completed | Overall progress
eURLLC [1] | PDCCH enhancements [3] | Use new DCI format for eURLLC scheduling Basic framework for enhanced UE PDCCH monitoring capability reporting | Remaining details of new DCI format Remaining details of enhanced UE PDCCH monitoring capability reporting and gNB configuration | OK
 | UCI enhancements [4] | Basic framework for sub-slot based PUCCH for HARQ-ACK Basic framework for separate HARQ-ACK codebook constructions for different service types | Remaining details for sub-slot based PUCCH for HARQ-ACK Remaining details for separate HARQ-ACK codebook constructions for different service types | OK
 | PUSCH enhancements [5] | Down-selection of different options for enhanced PUSCH repetition for both DG and CG PUSCH | Remaining details of enhanced PUSCH repetition for both DG and CG PUSCH based on option 4 | A bit slow
 | Enhanced scheduling/HARQ [6] | Identification of different options for out-of-order HARQ-ACK for PDSCH Identification of different options for out-of-order PUSCH scheduling Identification of different options for overlapping PDSCHs | Down-selection from different options for out-of-order HARQ-ACK for PDSCH and detailed design Down-selection from different options for out-of-order PUSCH scheduling and detailed design Down-selection from different options for overlapping PDSCHs and detailed design | Slow
 | UL inter-UE multiplexing [7] | Basic framework for UL cancelation scheme Basis framework for UL power control scheme for DG-PUSCH | Remaining details for UL cancelation scheme Remaining details for UL power control scheme for DG-PUSCH Down-selection of solutions and detailed design for UL power control scheme for CG-PUSCH | OK
 | Enhanced UL configured grant [8] | Basic framework for multiple active configured grant | Remaining details for multiple active configured grant | OK
IIOT [2] | UL intra-UE UL data/control and control/control collision handling [9] | 18 scenarios identified for UL intra-UE channel collision [7] | Design for the identified 18 scenarios | Slow
 | DL SPS enhancements [10] | Shorter DL SPS periodicity down to 1slot Multiple active DL SPS configurations | Detailed design for DL SPS enhancements, in particular HARQ-ACK feedback design | OK

## Slide 3: Potential scope adjustment
There is no dedicated RAN1 TU allocated to IIOT WI, the RAN1 impact of IIOT WI is organized together with eURLLC WI
Based on the current progress, there is high risk to complete the following items on time, which are related to intra-UE multiplexing between different service priority (e.g. eMBB and URLLC)
  Enhanced scheduling/HARQ
    out-of-order HARQ-ACK for PDSCH
    out-of-order PUSCH scheduling
    Handling of overlapping PDSCHs
  UL data/control and control/control collision handling
Potential solutions
  Option 1: Down-scope these items from current Rel-16 WIs and postpone to Rel-17
  Option 2: De-prioritize these items in RAN1 discussion
  Option 3: Narrow-down the scope to only consider the simple solutions to these items, for example
    For out-of-order HARQ-ACK for PDSCH and out-of-order PUSCH scheduling, only consider the out-of-order operation with same processing timeline
    For UL data/control and control/control collision handling, only consider the dropping of low priority channel when collides with high priority channel

## Slide 4: References
[1]. RP-191584, Revised WID: Physical Layer Enhancements for NR Ultra-Reliable and Low Latency Communication (URLLC), Huawei, HiSilicon
[2]. RP-191561, Revised WID: Support of NR Industrial Internet of Things (IoT), Nokia, Nokia Shanghai Bell
[3]. R1-1909877, Summary of Friday afternoon offline discussion on PDCCH enhancements, Huawei
[4]. R1-1909848, Offline summary#3 on UCI enhancements for URLLC, OPPO
[5]. R1-1909826, Summary of Wednesday/Friday offline discussion on PUSCH enhancements for NR eURLLC (AI 7.2.6.3), Nokia, Nokia Shanghai Bell
[6]. R1- 1909772, Summary #2 of Enhancements to Scheduling/HARQ, Qualcomm Incorporated
[7]. R1-1909774, Summary#2 of UL inter UE Tx prioritization/multiplexing, vivo
[8]. R1-1909784, Offline Summary for 7.2.6.6 Enhanced UL configured grant transmission, NTT DOCOMO, INC.
[9]. R1-1909492, Summary of email discussion [97-NR-05] on handling intra-UE collision scenarios for URLLC UCI enhancements, OPPO
[10]. R1-1909851, Summary#4 of 7.2.6.7 Others, LG Electronics

## Slide 5
Thanks