## Slide 1: Views on Rel-16 UE Power Saving

## Slide 2: Undecided power saving scope in RAN#84
There are two remaining power saving objectives to be determined in RAN#85.
  UE assistance information.
  Power saving techniques to reduce PDCCH monitoring on activated SCells for CA and DC (EN-DC in particular).
Power saving WID: Specify, if agreed, the mechanism to provide UE assistance information [RAN2, RAN1]: Study and select among the following UE assistance information for RAN2 by RAN#85: power preferred information (baseline LTE PPI in a well-defined manner) and UE's preference on C-DRX, BWP and SCell configuration [RAN2]. <Skipped> Note: The following objective may be considered in RAN#85 pending progress on SCell dormant behaviour and will be re-evaluated in RAN#85 Study and specify (if agreed) power saving techniques to reduce PDCCH monitoring on activated SCells for CA and DC (EN-DC in particular). Solutions (e.g. power saving signal/channel, enhancing Rel-15 DRX procedure) are to be discussed

## Slide 3: Background on UE assistance information in RAN#84
There were too many different proposals for UE assistance information to be included in power saving WID in RAN#84.
  Each company has different preference for UE assistance information.
  Not enough time to be converged during RAN#84.
Finally, the followings were agreed in RAN#84:
  One more RAN2 meeting to make a converged UE assistance information for power saving.
  If RAN2 makes a converged UE assistance information in RAN2#107, only converged UE assistance information will be remained and other not converged one will be removed from power saving WID in RAN#85.
Not converged UE assistance information in RAN2 should be removed from the WID for power saving.

## Slide 4: RAN2 discussion in RAN2#107
UE's preference on C-DRX is the only converged UE assistance information for power saving.
LTE PPI (power preferred inform) is excluded from UE assistance information.
There were still different understanding for BWP and SCell configuration.
  Eventually, no consensus was reached for these two UE assistance information.
There are no consensus on BWP and SCell configuration for UE assistance information.
Agreements in RAN2#107: - C-DRX configuration will be provided in UE assistance. Include the following DRX configuration parameters in UE assistance: long DRX cycle, short DRX cycle, DRX inactivity timer, short DRX cycle timer. FFS DRX on duration and DRX start offset - BWP and SCells UE assistance there is not enough consensus. - LTE PPI is excluded from UE assistance.

## Slide 5: Concerns about BWP and SCell configuration
Untrustworthy information can be reported.
  Not clear how the UE knows QoS for the DL traffic.
  Requested BWP/SCell configuration may be inappropriate for overall frequency resource status of the network.
There are too many different proposals for BWP/SCell configuration.
  Considering power saving TU, it seems that including BWP/SCell configuration for UE assistance information may be unrealistic plan in power saving.
The requested BWP/SCell configuration may be unnecessary.
  Network vendors have their own algorithms to determine this configuration.
BWP and SCell configuration should be removed from the objective for UE assistance information in power saving WID.

## Slide 6: Background on SCell ‘dormancy’ behaviour
‘dormancy’ behaviour was discussed in DC/CA enhancement WI in RAN2#106.
  ‘dormancy’ behaviour makes a UE stop monitoring PDCCH which is related to power saving.
  Send LS to RAN1/4 to ask about feasibility and benefit of ‘dormancy’ behaviour.
In RAN#84, it was finally determined to wait pending progress on SCell dormant behaviour and the related objective for power saving will be re-evaluated in RAN#85.
Agreements in RAN2#106: - SCell dormant state like LTE euCA will not be introduced in NR. - ‘dormancy’ behaviour will be studied as a solution for fast return to SCell utilisation for data transfer. The 'dormancy' behaviour implies that the UE stops monitoring PDCCH but continues other activities such as CSI measurements, AGC and beam management. RAN1/4 input required on feasibility and benefit.

## Slide 7: Progress on ‘dormancy’ behaviour in DC/CA WI
No discussion on ‘dormancy’ behaviour in RAN2#107, but only received reply LS from RAN1 and RAN4.
  From RAN1 perspective, L1 based mechanism for transitioning between ‘dormancy-like’ and ‘non dormancy-like’ behaviour on activated SCells can be supported.
  From RAN4 perspective, it is feasible to introduce dormancy behaviour.
‘dormancy’ behaviour would be discussed further based on the reply LS from RAN1/4 in the DC/CA enhancement WI at next RAN2 meeting.
It is better to discuss all mechanisms related to DC/CA in the DC/CA enhancement WI for consistency.
  Power saving mechanism for DC/CA is more relevant to and tightly coupled with DC/CA enhancement WI.
Remove the objective of power saving mechanism for activated SCells for CA/DC and, if needed, discuss in DC/CA enhancement WI.

## Slide 8: Proposals for UE Power Saving scope
Only UE's preference on C-DRX should be remained in the objective for UE assistance information.
LTE PPI, BWP and SCell configuration should be removed from the objective in power saving WID.
Power saving techniques to reduce PDCCH monitoring on activated SCells for CA and DC should be removed from the power saving WID.
Approve the proposed power saving WID.

## Slide 9: Proposed power saving WID
Proposed Power saving WID: Specify, if agreed, the mechanism to provide UE assistance information [RAN2, RAN1]: UE's preference on C-DRX [RAN2]. Study and select among the following UE assistance information for RAN2 by RAN#85: power preferred information (baseline LTE PPI in a well-defined manner) and UE's preference on C-DRX, BWP and SCell configuration [RAN2]. NOTE: additional UE assistance information for RAN1-specific power saving techniques to indicate what setting of parameters related to this Work Item will lead to power savings for the UE can be included if agreed in RAN1. <Skipped> Note: The following objective may be considered in RAN#85 pending progress on SCell dormant behaviour and will be re-evaluated in RAN#85 Study and specify (if agreed) power saving techniques to reduce PDCCH monitoring on activated SCells for CA and DC (EN-DC in particular). Solutions (e.g. power saving signal/channel, enhancing Rel-15 DRX procedure) are to be discussed Enhancements to Rel-15 DRX procedure can be studied further if they do not violate the general principle of single DRX configuration per MAC entity