## Slide 1: Power Saving feature for Release 17
3GPP TSG RAN#85
Newport Beach, CA, USA
Sep. 16-20, 2019
Agenda Item: 8.1.8
RP-191932

## Slide 2: Motivation/Background
As UE vendors are deeply engaged in the 5G commercialization, we are all aware several issues to fully and successfully launch the 5G devices.
  One is the power consumptions to be improved for 5G handset. The current test shows that we should do more works and make it more power efficient.
  Power efficiency for UE are also meaningful to the entire 5G ecosystem
It was also in intensive standardization discussion for how to improve it by current Release 16 NR WID of Power saving. The WID of power saving (RP-191607) focuses on the following aspects after last update:
  PDCCH-based power saving signal/channel design and corresponding procedure in MAC; Other power saving schemes including the cross-slot scheduling;
  UE adaptation to the maximum number of MIMO layers under the BWP framework;
  UE assistance information;
  RRM relaxation for RRC IDLE/INACTIVE;
There are still some other aspects/techniques need to be further considered in Release 17 to save UE power, if we could not finish them in Release 16
RP-191932

## Slide 3: Scope for Release 17 power saving
Further C-DRX enhancements:
  C-DRX operation in MAC layer and related spec. can be enhanced to reduce PDCCH monitoring, considering the supporting of CA, DC operations and other operations together
Incomplete part of Release 16 PDCCH-based power saving signal/channel enhancements:
  BWP switching mechanism triggered by power saving signal/channel
  Measurement enhancement related to BWP switching triggered by power saving signal/channel
In case of not supported in Release 16, more dynamic PDCCH monitoring reduction/adaptation compared to the existing schemes:
  DCI based PDCCH monitoring occasion skipping;
  DCI based dynamic PDCCH monitoring periodicity switching;
FR2 power saving optimization:
  As FR2 experienced high power consumption challenges, specific enhancement should be done for FR2, e.g. beam management, etc.
NR-U specific enhancements:
  PDCCH-based power saving signal/channel robustness considering LBT failure;
  DRX enhancements considering LBT failures, e.g., DRX Active time adaptation to channel occupancy time;
RP-191932

## Slide 4: Release 17 power consumption evaluation methodology
The Release-16 power consumption evaluation methodology has been proof to be a useful one and is the good base of the power saving technologies under standardization
  It is not a exhaustive one to cover all the use cases. Multiple carriers operation was not considered, for example
To meet more use cases, we suggest to extend UE power consumption model
Release 17 should support traffic model for services with low latency requirement.
  Gaming Traffic requires shorter latency and is a important part of 5G network. XR/AR/VR traffic also share similar requirement
More simulation assumptions should be introduced for real 5G network
  CA with SCell dormancy behavior;
  NR-U power scaling regarding LBT;
  FR2 power consumption property including Analogy BF, BW scaling and RF;
  Common reference UE behavior in beam-management;
  Measurements and other for UE procedure in paging monitoring;
RP-191932