## Slide 1: Agenda Item : 14 Source : Samsung Title : Discussion on SFN-sync in NR-DC Document for : Discussion and Decision
3GPP TSG RAN meeting #85 RP-191956
Newport Beach, USA, Sep 3-7, 2019

## Slide 2: Introduction
@ RAN# 84, it was discussed whether or not synchronous NR-NR DC requires SFN synchronization.
No conclusion was reached. RAN tasked RAN1 to follow up on this issue. If no progress, RAN#85 could discuss this issue again.

## Slide 3: Discussions in WGs
Whether synchronous NR-NR DC means SFN sync was discussed in RAN2 (RAN2#106, Mar 2019) , RAN4 (RAN4#90bis, Apr 2019) and RAN1 (RAN1#98, Aug 2019)
RAN2 concludes as followings
  RAN2 understanding is that sync NR-DC implies at least slot synchronization and it does not imply SFN synchronization
In RAN4 LS to RAN2 (R4-1904823),
  From RAN4 point of view, synchronous NR-DC only requires slot boundary synchronization
In RAN1 LS to RAN/RAN2 (R1-1909882),
  There is no consensus in RAN1 on how to clarify what “synchronous” in synchronous NR-DC means in Rel-15, although it is commonly understood in RAN1 that synchronous means at least slot-level synchronization
In summary, two WGs (RAN2, RAN4) understand synchronous NR-DC is not about SFN-sync and one WG (RAN1) could not reach consensus

## Slide 4: Technical aspects
The argument for SFN-sync is that search time can be reduced and physical layer procedures as for CA can be reused
The argument against SFN-sync is that, even with SFN-sync of MCG and SCG,
  CA physical layer cannot be reused for PSCell addition
  Search time reduction is a minor enhancement (rarely applicable)
  Limiting NR-NR DC in late drop only to synchronous operation is to minimize UE specification/ implementation impact.
 | CA physical layer procedure (i.e. SCell addition) | PSCell addition in SFN-sync NW
PBCH decoding | No | No
Random access | No | Yes
SIB1 decoding | No | Yes

## Slide 5: Additional aspects
In LTE DC, EN-DC, and NE-DC, synchronous operation is not about SFN-sync. Mandating SFN-sync only to Rel-15 NR-NR DC is imposing new requirements, particularly both to NW vendors and service providers
As pointed out in R1-1908245, SFN sync between different GNBs of different vendors would be very difficult if not impossible

## Slide 6: Concluding Remarks
No consensus was achieved in RAN1 for requiring SFN-sync for NR-DC
There is consensus in RAN2/RAN4 that SFN-sync is not required
It is not likely that companies having different views will change their opinions at the RAN plenary
It is not likely that RAN2 and RAN4 will change their conclusions and reach a different consensus if they discuss the same issue again
Proposal: RAN may either not discuss further this issue or confirm the conclusions reached by the WGs (when applicable) that synchronous operation between MCG and SCG requires only that slot-boundaries are synchronized