## Slide 1: Motivation for new WI on Introduction of NB-IoT in AAS specification
Ericsson
RP-192013

## Slide 2: Motivation of new WI
The current AAS specification does not include support for NB-IoT
AAS implementations with integrated antenna and radio may be expected from bands upwards from around 2.5GHz
NB-IoT is supported for several relevant bands
Support for band 42/43 for NB-IoT has recently been introduced
Scenarios may exist in which AAS is deployed for eMBB capacity enhancement with user specific beamforming for eMBB and support for NB-IoT in cell wide beams
It would be undesirable for the RAN4 specifications to preclude such scenarios

## Slide 3: Expected workload
The aim of the WI is to migrate existing NB-IoT requirements supported for E-UTRA in MSR to AAS
Existing procedures for translating conducted requirements to OTA can be adopted:
  ”Scaling” from conducted to TRP emissions requirements
  Direct translation of directional TX requirements
  Translation of RX requirements by means of ”sensitivity RoAoA”
Existing test procedures and MU expected to be re-used for all requirements
Workload of 0.25 TU in 2Q foreseen