## Slide 1: 3GPP TSG RAN Meeting #88e RP-20xxxx Electronic Meeting, June 29 - July 3, 2020
Title: Intermediate summary of FR2_fallback
Source: Nokia (moderator)

## Slide 2: Scope of the [FR2_fallback] email discussion
Goal: Find a way forward on FR2 fallback. We shall not return this discussion to the WGs, but aim to make a decision at this RAN plenary, and approve all necessary CRs.
Input contributions covered: RP-201199, RP-200875, RP-201035

## Slide 3: Moderator’s questions for discussion
Can we confirm that the technically endorsed RAN2 CRs in RP-201199 impact only FR2 intra-band CA (or DC) with combination of contiguous and non-contiguous CCs. No other FR2 fallbacks like FR2 contiguous intra-band CA fallbacks or FR2 inter-band CA fallbacks are impacted by the CRs.
Are there any specific concerns related to single carrier as fallback for FR2 intra-band CA (or DC) with combination of contiguous and non-contiguous CCs?

## Slide 4: Summary of company feedback
Not many companies responded to the moderator’s questions but based on the answers received it can be confirmed that the RAN2 CRs in RP-201199 impact only FR2 intra-band CA or DC with combination of contiguous and non-contiguous CCs and other cases are not impacted by the CRs.
No specific concerns related to single carrier as fallback for FR2 intra-band CA (or DC) with combination of contiguous and non-contiguous CCs were expressed.
But large number of companies expressed general concerns for the principle of UE not supporting all fallback cases in all the scenarios and wanted to maintain flexibility for the future purposes

## Slide 5: Next steps
Based on the feedback during the email discussion it was not possible to reach consesus of approving the technically endorsed RAN2 CRs in RP-201199
As the issue should be resolved in RAN#88e instead of continuing the discussion in RAN2 and RAN4, it should be discussed next if consensus could be reached to approve CRs to the RAN4 specifications to align the RAN2 and RAN4 specifications on UE’s fallback support for FR2 intra-band CA with combination of contiguous and non-contiguous CCs.
But it is important to re-confirm that in future when RAN4 requests signalling support from RAN2, RAN2 shall implement the RAN4 request