## Slide 1: 3GPP TSG RAN Meeting #88e RP-20xxxx Electronic Meeting, June 29 - July 3, 2020
Title: Draft proposal for Flex_BW
Source: Vodafone (moderator)

## Slide 2: Draft proposal
Agree on the following:
  Define TRS bandwidth sizes of 28, 32, 36, 40, 44, and 48 RBs.
    [All TRS configured with the proposed TRS bandwidth sizes for a UE span the same set of RBs]
    [All allocated PDSCH bandwidth are confined within the bandwidth spanned by the TRS configured]
  Supported for 10MHz UE channel bandwidth and 15kHz SCS, in FDD bands.
    Note: No new performance requirement on UE is introduced here.
  A single optional UE capability per band
  Introduce from Release 16
Still open:
  Whether to further split the single UE capability for 28 and >28 RB TRS.
  Further comments on 15MHz and 20MHz channel bandwidth support welcome (only KDDI made a concrete proposal for it so far).