3GPP TSG RAN Meeting #90-e 	                                                    RP-20XXXX

e-Meeting, December 7th –11th, 2020

Agenda Item: 9.8.7

Source: Moderator (MediaTek)

Title: [90E][28][Secondary_DRX]

Document for: Discussion and Decision

# Introduction

In RAN #89-e meeting [1], it is concluded to further discuss 2nd DRX related proposal(s) submitted to RAN#90 e-meeting. In moderator summary last meeting [2], it is encouraged for companies to provide justification for: Benefit for UE power saving, potential specification change(s), work group involvement and interactions, and suggested start timing.

In this RAN#90-e meeting, there are three contributions submitted [3][4][5], and the email thread [90E][28][Secondary_DRX] is kicked off per chairman assignment, as quoted below:

Dear all, This is the formal kick off of the email thread on finding a way forward on Secondary DRX handling. Goal: Generate an agreeable way forward. Input contributions covered: 2407, 2686, 2717. Moderator: Weide Wu. Br, Balazs.

In the following sections, we will first check companies’ understanding on the potential enhancement items for 2nd DRX in Rel-17 and then check companies’ views on whether and where to include an enhancement item, if agreed. Please kindly provide your inputs by 12:29 PM UTC 12/8 for initial round of email discussion.

# Potential Enhancement Items for 2nd DRX in Rel-17

From the contributions, the following collect the potential enhancement items related to 2nd DRX in Rel-17. Companies are invited to check and suggest revision, if any.

Topic 1: The potential enhancement items for 2nd DRX in Rel-17 include:

- Specify UE behaviors that enable joint configuration between secondary DRX group and DCP/wakeup signalling, SCell dormancy, or cross-carrier scheduling

- Specify means to enable selective wakeup of one or both DRX groups upon DCP/wakeup signalling indication

- Specify means to wake up one DRX group from another by a MAC CE

- enable UE to report UE assistance information for preferred DRX for either default DRX group or the secondary DRX group

- Other potential enhancement item not listed in the above; please specify, if any

Please provide your views/suggestions for Topic 1 in Table 1 below.

Table 1: Whether the potential enhancement items in Topic 1 are complete and clear and what is the suggested revision/addition, if any

| Company name | Company views on Topic 1 |
| --- | --- |
| OPPO_ShiCong | Clarification: The intention of bullet c) is not clear to us. Now the secondary DRX is there in the spec, meanwhile we have introduced DCP which can be used to trigger the start of on-duration or not, the only restriction is that DCP can not be configured together with secondary DRX, so why we need to introduce MAC CE to wake up DRX group from the other. Other potential enhancement: in R16, the UE assistance information for preferred DRX is introduced in Power Saving Working Item, however, due to time limitation, preferred DRX only applies to default DRX even if the secondary DRX group is configured, which is a limitation. Thus, one potential enhancement is to enable UE to report UE assistance information for preferred DRX for either default DRX group or the secondary DRX group, which was the majority view in RAN2. |
| CATT | The discussions of specification impact are limited to feature interaction between secondary DRX group and DRX adaptation (WUS)/SCell dormancy, which leads to mutual exclusive configuration between secondary DRX group and DRX adaptation or between secondary DRX group and SCell dormancy. There is no discussion on feature interaction between secondary DRX group and cross-slot scheduling. The selected wakeup of DRX groups were not supported in Rel-16 UE power saving feature due to the overlapped with SCell dormancy. We don’t see any benefit of introducing selected wakeup of DRX groups by DCP or MAC. We had shown the aspects and additional works in RAN1 in RP-202717 when secondary DRX group is jointly configured with DRX adaptation and/or SCell dormancy. We need additional TUs in Rel-17UE power saving in both RAN1 and RAN2 if additional objective is added. |
| Futurewei | b) is conditioned on the availability of a). |
| MediaTek | We add OPPO’s proposal as d). From our point of view, the 4 listed enhancements are separated in scope. We understand that a) is to lift the restriction, i.e., to complete the leftover of R16. The other 3 enhancements are new and have no dependency of existing R17 PS features. |
| ZTE_YuanGao | For bullet c), we share similar understanding with OPPO that some clarification is needed for the motivation. Since we have already specified DCP in Rel-16 to wake up the default DRX group, it is naturally to use it to also wake up the secondary DRX group or both of the default and secondary DRX group if we agree to support joint configuration of DCP with secondary DRX group in later release. |
| Huawei, HiSilicon | We think this question is premature to answer, whether the above are complete and clear depend on whether companies have common understanding on the necessity for each objective. |
| Samsung | It is beneficial to further save UE consumption power with a), b) and c). On the other hand, the motivation of ‘cross-carrier scheduling’ seems unclear in a). d) can be also studied. |
| vivo | For a), we share similar with CATT that feature interaction between secondary DRX group and cross-slot scheduling is not necessary since no evidences show benefits of such operation. For c), we are confused to introduce MAC CE based solution to wakeup DRX group(s) other than DCP which is captured in b). What is more popular as we discussed in Rel-16 is to wake up one DRX group from another by DCP. We are fine to further discuss it. At this stage, it is too early to restrict to higher layer solutions. Meanwhile, we think b) should be the sub-bullet for a), as b) is the detailed design for a). |
| Qualcomm Incorporated | We think the list covers potential enhancements that have been identified so far. To OPPO’s comment on MAC CE: Our proposal is to allow the network to use the MAC CE during the active time. DCP as defined today is always sent outside DRX active time. Please see other explanations below on the use case. To OPPO’s comment on MAC CE: Our intention in proposing MAC CE is to avoid RAN1 impact. To CATT’s comment on SCell dormancy: In a dormancy SCell, the UE still needs to perform CSI measurements (and reporting on other active UL BWP). Whereas if secondary DRX group with selective wakeup is used, those are not required, i.e. more power can be saved. |

# View Collection for Each Potential Enhancement Item

In this Section, companies’ views on whether and where each enhancement item should be included in Rel-17 will be collected.

Topic 2: Whether and where should the potential enhancement item 1-a) in Topic 1 be included in Rel-17?

- Yes, in Rel-17 WI of UE power saving enhancements for NR with [RAN2] (please specify) as leading WG

- Yes, in Rel-17 TEI

- No

- Other opinion (please clarify)

Companies are invited to provide views on Topic 2 in Table 2 below:

Table 2: Whether and where should the potential enhancement item 1-a) in Topic 1 be included in Rel-17

| Company name | Company views on Topic 2 |
| --- | --- |
| OPPO | Either i) or ii) is fine for us, however, it seems it may have impact on RAN1, which is more suitable to put it in R17 Power Saving WI. |
| CATT | Yes. Option iv) We can support only modified objective a) in Rel-17 UE power saving in the following only if the TU is reasonably increased Specify UE behaviors that enable joint configuration between secondary DRX group and DCP/wakeup signalling, or SCell dormancy, or cross-carrier scheduling |
| Futurewei | iii) No. WUS/DCP and SCell dormancy use dynamic signalling to enable power saving, while secondary DRX depends more on semi-dynamic configuration to achieve power saving. It is not clear if there is much more power saving gain from additional semi-dynamic configuration when WUS/DCP and SCell dormancy can already allow dynamic on/off of transmission/reception on SCell. |
| MediaTek | iii) No. Joint configuration complicated test cases and deployment, therefore, we should only enable joint configuration under the condition that it brings real benefits. However, in our contribution RP-202686, it is shown, when DCP/WUS, SCell dormancy or cross-carrier scheduling takes effect, whether 2nd DRX is configured is irrelevant since there is no PDCCH monitoring in SCell(s). Since SCell dormancy provides better performance regardless, there is no need for network to configure both features at the same time, a network should configure SCell dormancy whenever it is possible (e.g. considering the capability of itself and the UE); if SCell dormancy configuration is not available, 2nd DRX can be configured instead. |
| ZTE | iii) No. But we are okay if there is a significant majority to do it in Rel-17 (e.g. as part of TEI-17) - i.e. option ii), assuming the scope is limited and suitable for TEI |
| Huawei, HiSilicon | iii) We think [4] made a good analysis on the gains, which we largely agree. We understand the gains compared with Rel-16 should use WUS and SCell dormancy as the baseline, and the gains are seen limited. With limited gains, but more complicated configurations handling from both UE and network sides as well as various impacts on the R1/R2 specifications (also analysed in [5]), it seems no much value to have such enhancements. |
| Samsung | i) seems suitable because there could be slightly RAN1 impact, but we support CATT’s suggestion. |
| vivo | Either ii) or iii) is acceptable for us. Regarding i), considering the TU for current WI is very limited, it is better to firstly ensure the completion of existing scope in the WI. The progress and whether the allocated TUs are enough for each item are not clear enough, and this lack-of-time situation becomes even worse by eMeetings. How to ensure the current scope of each item could be completed in-time is uncertain. Technically, we are positive on this objective. But we prefer to consider it later for approach i), based on the progress of relevant Wis. |
| Qualcomm Incorporated | We prefer Release-17 power saving WI. We agree with CATT that enhancements related to cross-carrier scheduling should be removed to avoid much RAN1 impact. We can further discuss general direction for DCP/WUS to avoid RAN1 impact. WUS should be configured only on SpCell, as in release-16. Conditions for WUS monitoring is completely determined by DRX state of SpCell and independent from DRX state of the secondary DRX group. For example, UE monitors WUS if SpCell is not in DRX active time, even if secondary DRX group is in DRX active time at the same time. If WUS is not received or does not indicate wakeup, none of UE’s carriers should wake up, as in legacy; If a WUS occasion is not monitored (e.g., SpCell is already in DRX active time) or WUS indicates wakeup, UE should start DRX on duration timers of both DRX groups at their respective next occurrence. |

Topic 3: Whether and where should the potential enhancement item 1-b) in Topic 1 be included in Rel-17?

- Yes, in Rel-17 WI of UE power saving enhancements for NR with [RAN2] (please specify) as leading WG

- Yes, in Rel-17 TEI

- No

- Other opinion (please clarify)

Companies are invited to provide views on Topic 3 in Table 3 below:

Table 3: Whether and where should the potential enhancement item 1-b) in Topic 1 be included in Rel-17

| Company name | Company views on Topic 3 |
| --- | --- |
| OPPO | Either i) or ii) is fine for us, however, it seems it may have impact on RAN1, which is more suitable to put it in R17 Power Saving WI. |
| CATT | iii) No. SCell dormancy would provide more power saving gain than the selected wakeup of DRX group. |
| Futurewei | iii) No. Similar comment as for topic 2. |
| MediaTek | iii) No. As clarified in our contribution RP-202686 and in topic 2, we do not see additional benefit for joint configuration. When SCell dormancy/DCP/WUS is configured, there is sufficient control on PDCCH monitoring of SCell, therefore, this enhancement is merely a function duplication with no additional benefit. |
| ZTE | iii) No. But we are okay if there is a significant majority to do it in Rel-17 (e.g. as part of TEI-17) - i.e. option ii), assuming the scope is limited and suitable for TEI |
| Huawei, HiSilicon | iii) Similar comments as the above. |
| Samsung | i) seems suitable because there could be slightly RAN1 impact. |
| vivo | Either ii) or iii) is acceptable for us. Regarding i), considering the TU for current WI is very limited, it is better to firstly ensure the completion of existing scope in the WI. The progress and whether the allocated TUs are enough for each item are not clear enough, and this lack-of-time situation becomes even worse by eMeetings. How to ensure the current scope of each item could be completed in-time is uncertain. Technically, we are positive on this objective. But we prefer to consider it later for approach i). |
| Qualcomm Incorporated | i) Our proposal is to introduce a semi-static configuration by RRC, to avoid RAN1 impact. Note that this is augmented by the item c), “Specify means to wake up one DRX group from another by a MAC CE”. For instance, semi-statically configure FR2 DRX group should not wake up and allow the network to use the MAC-CE to dynamically wake up FR2 DRX group depending on the traffic needs. |

Topic 4: Whether and where should the potential enhancement item 1-c) in Topic 1 be included in Rel-17?

- Yes, in Rel-17 WI of UE power saving enhancements for NR with [RAN2] (please specify) as leading WG

- Yes, in Rel-17 TEI

- No

- Other opinion (please clarify)

Companies are invited to provide views on Topic 4 in Table 4 below:

Table 4: Whether and where should the potential enhancement item 1-c) in Topic 1 be included in Rel-17

| Company name | Company views on Topic 4 |
| --- | --- |
| OPPO | No |
| CATT | iii) No. |
| Futurewei | iii) No. The usefulness and benefit seem to be marginal. |
| MediaTek | iii) No, same concerns of no benefit and function duplication. |
| ZTE | iii) No. |
| Huawei, HiSilicon | iii) It is a bit unclear what the exact proposal is on 1-c. There was no clear proposal from the reference paper and also the gains are not shown clearly. |
| Samsung | i) seems fine so that c) can be discussed together with a), b) and d) in R17 UE power saving. |
| vivo | iii) No, see the reason in Topic 1. |
| Qualcomm Incorporated | i) The intention is the network can configure FR2 DRX group should not wake up (item b) and then use the MAC-CE to dynamically wake up FR2 DRX group depending on the traffic needs. Again, RAN1 impact should be avoided. |

Topic 5: Whether and where should the potential enhancement item 1-d) in Topic 1, if specified, be included in Rel-17?

- Yes, in Rel-17 WI of UE power saving enhancements for NR with [RAN2] (please specify) as leading WG

- Yes, in Rel-17 TEI

- No

- Other opinion (please clarify)

Companies are invited to provide views on Topic 5 in Table 5 below:

Table 5: Whether and where should the potential enhancement item 1-d) in Topic 1, if specified, be included in Rel-17

| Company name | Company views on Topic 5 |
| --- | --- |
| OPPO | The UE assistance information enhancements for the secondary DRX is a pure RAN2 one, we are fine to put it TEI17 or in R17 Power Saving WI. |
| CATT | iii) No |
| Futurewei | iii) No for now. |
| MediaTek | iii) or ii) if there is majority. We agree UE assistance information enhancement only concerns RAN2 and orthogonal to current R17 PS discussion. Considering its scope and no dependency, TEI is suitable. |
| ZTE | iii) No. |
| Huawei, HiSilicon | iii) No |
| Samsung | i) seems fine so that d) can be discussed together with a), b) and c) in R17 UE power saving. |
| vivo | iii) No |
| Qualcomm Incorporated | ii) Agree with OPPO’s comment above. |

# Summary

(To be supplied)

# Reference

RP-202124, “Draft Meeting Report for TSG RAN meeting #89e”, RAN#89-e

RP-202032, “Moderator's summary for email discussion [89E][29][R17_secondary_DRX]”, 	Moderator (MediaTek), RAN#89-e

RP-202407, “Enhancements to DRX groups in R17”, Qualcomm, Ericsson, Samsung

RP-202686, “Discussion on Secondary DRX Group for NR CA”, MediaTek

RP-202717, “Discussion on the support of feature interaction between secondary DRX group and DRX adaptation/SCell dormancy in Rel-17”, CATT