3GPP TSG RAN Meeting #90-e 	                                                    RP-20XXXX

e-Meeting, December 7th –11th, 2020

Agenda Item: 9.8.7

Source: Moderator (MediaTek)

Title: [90E][28][Secondary_DRX]

Document for: Discussion and Decision

# Introduction

In RAN #89-e meeting [1], it is concluded to further discuss 2nd DRX related proposal(s) submitted to RAN#90 e-meeting. In moderator summary last meeting [2], it is encouraged for companies to provide justification for: Benefit for UE power saving, potential specification change(s), work group involvement and interactions, and suggested start timing.

In this RAN#90-e meeting, there are three contributions submitted [3][4][5], and the email thread [90E][28][Secondary_DRX] is kicked off per chairman assignment, as quoted below:

Dear all, This is the formal kick off of the email thread on finding a way forward on Secondary DRX handling. Goal: Generate an agreeable way forward. Input contributions covered: 2407, 2686, 2717. Moderator: Weide Wu. Br, Balazs.

In the following sections, we will first check companies’ understanding on the potential enhancement items for 2nd DRX in Rel-17 and then check companies’ views on whether and where to include an enhancement item, if agreed. Please kindly provide your inputs by 12:29 PM UTC 12/8 for initial round of email discussion.

# Potential Enhancement Items for 2nd DRX in Rel-17

From the contributions, the following collect the potential enhancement items related to 2nd DRX in Rel-17. Companies are invited to check and suggest revision, if any.

Topic 1: The potential enhancement items for 2nd DRX in Rel-17 include:

- Specify UE behaviors that enable joint configuration between secondary DRX group and DCP/wakeup signalling, SCell dormancy, or cross-carrier scheduling

- Specify means to enable selective wakeup of one or both DRX groups upon DCP/wakeup signalling indication

- Specify means to wake up one DRX group from another by a MAC CE

- Other potential enhancement item not listed in the above; please specify, if any

Please provide your views/suggestions for Topic 1 in Table 1 below.

Table 1: Whether the potential enhancement items in Topic 1 are complete and clear and what is the suggested revision/addition, if any

| Company name | Company views on Topic 1 |
| --- | --- |
| OPPO_ShiCong | Clarification: The intention of bullet c) is not clear to us. Now the secondary DRX is there in the spec, meanwhile we have introduced DCP which can be used to trigger the start of on-duration or not, the only restriction is that DCP can not be configured together with secondary DRX, so why we need to introduce MAC CE to wake up DRX group from the other. Other potential enhancement: in R16, the UE assistance information for preferred DRX is introduced in Power Saving Working Item, however, due to time limitation, preferred DRX only applies to default DRX even if the secondary DRX group is configured, which is a limitation. Thus, one potential enhancement is to enable UE to report UE assistance information for preferred DRX for either default DRX group or the secondary DRX group, which was the majority view in RAN2. |

# View Collection for Each Potential Enhancement Item

In this Section, companies’ views on whether and where each enhancement item should be included in Rel-17 will be collected.

Topic 2: Whether and where should the potential enhancement item 1-a) in Topic 1 be included in Rel-17?

- Yes, in Rel-17 WI of UE power saving enhancements for NR with [RAN2] (please specify) as leading WG

- Yes, in Rel-17 TEI

- No

- Other opinion (please clarify)

Companies are invited to provide views on Topic 2 in Table 2 below:

Table 2: Whether and where should the potential enhancement item 1-a) in Topic 1 be included in Rel-17

| Company name | Company views on Topic 2 |
| --- | --- |
| OPPO | Either i) or ii) is fine for us, however, it seems it may have impact on RAN1, which is more suitable to put it in R17 Power Saving WI. |

Topic 3: Whether and where should the potential enhancement item 1-b) in Topic 1 be included in Rel-17?

- Yes, in Rel-17 WI of UE power saving enhancements for NR with [RAN2] (please specify) as leading WG

- Yes, in Rel-17 TEI

- No

- Other opinion (please clarify)

Companies are invited to provide views on Topic 3 in Table 3 below:

Table 3: Whether and where should the potential enhancement item 1-b) in Topic 1 be included in Rel-17

| Company name | Company views on Topic 3 |
| --- | --- |
| OPPO | Either i) or ii) is fine for us, however, it seems it may have impact on RAN1, which is more suitable to put it in R17 Power Saving WI. |

Topic 4: Whether and where should the potential enhancement item 1-c) in Topic 1 be included in Rel-17?

- Yes, in Rel-17 WI of UE power saving enhancements for NR with [RAN2] (please specify) as leading WG

- Yes, in Rel-17 TEI

- No

- Other opinion (please clarify)

Companies are invited to provide views on Topic 4 in Table 4 below:

Table 4: Whether and where should the potential enhancement item 1-c) in Topic 1 be included in Rel-17

| Company name | Company views on Topic 4 |
| --- | --- |
| OPPO | No |

Topic 5: Whether and where should the potential enhancement item 1-d) in Topic 1, if specified, be included in Rel-17?

- Yes, in Rel-17 WI of UE power saving enhancements for NR with [RAN2] (please specify) as leading WG

- Yes, in Rel-17 TEI

- No

- Other opinion (please clarify)

Companies are invited to provide views on Topic 5 in Table 5 below:

Table 5: Whether and where should the potential enhancement item 1-d) in Topic 1, if specified, be included in Rel-17

| Company name | Company views on Topic 5 |
| --- | --- |
| OPPO | The UE assistance information enhancements for the secondary DRX is a pure RAN2 one, we are fine to put it TEI17 or in R17 Power Saving WI. |

# Summary

(To be supplied)

# Reference

RP-202124, “Draft Meeting Report for TSG RAN meeting #89e”, RAN#89-e

RP-202032, “Moderator's summary for email discussion [89E][29][R17_secondary_DRX]”, 	Moderator (MediaTek), RAN#89-e

RP-202407, “Enhancements to DRX groups in R17”, Qualcomm, Ericsson, Samsung

RP-202686, “Discussion on Secondary DRX Group for NR CA”, MediaTek

RP-202717, “Discussion on the support of feature interaction between secondary DRX group and DRX adaptation/SCell dormancy in Rel-17”, CATT