3GPP TSG-RAN Meeting #89-e	RP-20xxxx

Online, 7-11 December, 2020

Agenda item:	9.1.5

Source: 	Moderator(Qualcomm)

Title: 	E-mail discussion on the scope of OTA work for Rel.17

Document for:	Discussion

# Introduction

This paper will summarize the companies inputs regarding the scope of the OTA work for Rel.17.

# Discussion

## Study on radiated metrics and test methodology for FR2 NR UEs under dynamic test environment

### Proposed SI Scope

The proposed SI scope is shown below [1]:

### Objective of SI or Core part WI or Testing part WI

The objective of this Study Item is to define end-to-end testing methodology for the verification of FR2 NR UEs performance in a dynamic environment. The test methodology for multi-panel UE should also be considered.

The study proceeds within the following scope:

-	For the following device types:

-	Smartphone is the first priority.

-	Other UE types are not precluded for discussion as a second priority

-	Identify test scenarios:

-	Stage 1: UE rotation-based scenario

- Change UE rotation during the testing

- Study the feasibility of reusing 3D-MPAC system

-    Stage 2: UE travel-based scenario

- Change both UE rotation and beams from gNB(s) during the testing

- Study the enhancement on 3D-MPAC system

- Up to 2 beams is the first priority

- Identify each test scenario with proper justification and avoid unnecessary overlapping test cases.

- Test metric should be based on the current core/performance requirements.

Note: RAN4 will not start Stage 2 before Stage 1 is completed.

-    The test methodology shall include both NSA and SA.

- For setups intended for measurements of UE characteristics in non-standalone (NSA) mode, an LTE link antenna setup is used to configure the NR link

-	Using the channel models defined in TR38.901 as the starting point to develop dynamic environment

-    Channel model framework in TR38.827 should be taken as the basis

-	Study whether and which parameters for channel mode defined in TR38827 will have big impact on UE performance and could be reused for dynamic testing.

-	Study the applicable test methodology verification procedures

-	Study the preliminary uncertainty budget for the methodology

-     The uncertainty budget in TR38827 should be the basis for developing the uncertainty.

-     Study the additional uncertainty due to the dynamic environment

-	The test methodology shall initially assume a black box approach to ensure the test of multi-panel Tx/Rx UE is covered.

-	The dynamic environment tests shall take the test system complexity and test time into account to keep the whole test costs within a reasonable level.

During this study item, ongoing communication with 3GPP RAN WG5, CTIA OTA Working Group (MOSG, 5G mm-wave OTA Sub-Working group and MUSG), and CCSA TC9 WG1 shall be maintained to ensure industry coordination on this topic.

### Main Points for Discussion

Companies should express their opinions/comments related to the following main points.

- Comments to fine tune the objectives

- What could be streamlined/downscoped to limit the number of Tus per meeting

- Should the study on testing for 52.6-71GHz also be handled in this SI to have a unified/compatible test approach

### Companies’ Comments

| Company | Comments |
| --- | --- |

### Summary

# Conclusion

# References

- RP-202634, “New SID: Study on Dynamic OTA Testing for FR2”, Qualcomm Incorporated