## Slide 1: Motivation for Support of Wireless Industrial Ethernet
Agenda Item: 15
Source: Lenovo, Motorola Mobility
Document for: Discussion
3GPP TSG RAN Meeting #91-e RP-210675
Electronic Meeting, March 16 – 26, 2021

## Slide 2: Introduction
In smart factory, one of the most challenging and demanding is the motion control use case requiring closed loop control application.
A motion control system is responsible for controlling moving and/or rotating parts of machines in a well-defined manner by providing set points to actuators for the controlling the robotic arm movements/rotations by utilizing constant feedback from sensors.
Using wirelessly connected devices for these movements/rotations of components can result in the replacement of slip rings, cable carriers, etc., thereby reducing abrasion, maintenance effort, costs etc., and creating a compact, modular production lines

## Slide 3: Background: Rel-17 work on TSN
The factory automation leverage on the existing industrial wired TSN design for wireless TSN framework in 3GPP from Rel 15 to 17 - Higher Reliability of 99.9999%, cycle time of 1ms, and high precise clock synchronicity of ~1µs
In Rel-17, wireless TSN integration focuses on precise clock synchronicity of ~1µs for various indoor and outdoor use case starting from motion control application in a factory to smart grid, assistance signaling of tolerable consecutive packet loss with survival time and estimated burst arrival time
Reliability enhancement schemes like selective UL packet duplication, A-CSI reporting, intra-UE multiplexing are currently being investigated in Rel-17

## Slide 4: Support of Industrial Ethernet Protocol
Industrial Ethernet technologies such as Sercos®, PROFINET® IRT or EtherCAT® are commonly used in closed-loop motion control applications in industry, supporting cycle times below 50 µs, and allowing for faster and more accurate movements/rotations
Such industrial ethernet technologies coexist with TSN providing isochronous real time operations with almost zero jitter
Operating principles of EtherCAT; SERCOS-3 are based on circulating/travelling ethernet frame containing data for all nodes

## Slide 5: Rel-18 Proposal for Wireless Ethernet Protocol
In Rel-18, NR should study on supporting industrial Ethernet technologies such as Sercos®, PROFINET® IRT or EtherCAT® by study their traffic pattern, topologies and enhancing Layer1/2 protocols to efficiently deliver Ethernet packets under TSN protocols and meet service performance requirements, e.g. reliability, latency