## Slide 1: Consideration on Sidelink positioning and Ranging xiaomi
3GPP TSG RAN Meeting #93
Electronic Meeting, Sep. 13 – 17, 2021
RP-211778

## Slide 2: Clarification on the relationship of sidelink positioning & ranging
According to 22.261, relative positioning and ranging are defined as:
  Ranging: refers to the determination of the distance between two UEs and/or the direction of one UE from the other one via direct device connection.
  Relative positioning: relative positioning is to estimate position relatively to other network elements or relatively to other UEs.
Based on the above definition, we have the following observations:
  Observation 1: Ranging emphasizes on acquiring one component of 2D/3D coordinates, e.g. direction, angle.
  Observation 2: Positioning emphasizes on acquiring 2D/3D absolute/relative coordinates of a UE.
Thus, we have the following conclusion:
  For sidelink positioning, it is to acquire 2D/3D absolute/relative coordinates.
  For Ranging, it is to acquire one component of 2D/3D coordinates, e.g. direction, angle.
Given that for different use cases, either the whole 2D/3D coordinates or one component of 2D/3D coordinates are required, we suggest that:
Proposal 1: RAN to agree to use both term of sidelink positioning and ranging.
Proposal 2: Solution should allow acquiring either the whole 2D/3D coordinates or only one component of 2D/3D coordinates, e.g. distance or angle.
Although the slight requirement differences in sidelink positioning and ranging, technical solutions are quite similar.
Proposal 3: A unified solution is applicable for sidelink positioning and Ranging.

## Slide 3: Use cases to consider
There are two SI/WIs related to sidelink positioning and ranging
  R17 RAN level SI: FS_NR_pos_cov (TR38.845)
    Focus on V2X and public safety use case.
    KPIs include absolute/relative horizontal accuracy, vertical accuracy, confidence level, latency, etc.
  R18 SA1 SI/WI: Ranging based services (TR22.855/TS22.261)
    Focus on commercial use cases and public safety.
      For commercial use cases, e.g. smart home, smart city, smart retailor, there are imperious demands from the market to support ranging. Although currently UWB is applied in smart phones like apple, xiaomi, it suffers from power consumption issue (rely on BLE for power management), cost of independent RF, and high interference from WiFi. 3GPP has the potential to overcome these drawbacks and develops more competitive technology for ranging.
    KPIs include distance accuracy, direction accuracy, confidence level, latency, effective ranging distance, ranging interval, concurrent ranging operations, etc.
Open the door
if distance < e.g. 1m
bed lamp
Phone pops up the control interface of TV
Phone pops up the control interface of bed lamp
point to TV
point to lamp
Smart Home
Smart City

## Slide 4: Uniqueness of commercial use cases from V2X
Power consumption
  Different from vehicle and smart phone, IoT devices require to work for months when applying sidelink positioning/Ranging
Low cost
  IoT devices requires low cost
    For low positioning/ranging accuracy requirement, support Redcap UE
    For high positioning/ranging accuracy requirement, consider to support large positioning/ranging signal bandwidth and small communication bandwidth.
Security and privacy
  The position IoT devices may not link to user’s location. sidelink positioning/ranging may be performed without security, e.g. broadcast mode.
Capacity
  Unlike V2X and public safety, their might be a large number of IoT devices in an area, the positioning/ranging capacity in an area should be considered.
  Proposal 4：Both commercial and V2X use cases need to be considered in sidelink positioning and Ranging
  Proposal 5: power consumption and cost reduction for IOT device should be considered.

## Slide 5: Spectrum
For V2X
  V2X can be deployed on ITS spectrum, however, in some country, e.g. china, the available ITS bandwidth is only 20MHz. To support 10cm accuracy, much larger bandwidth is required.
For commercial use case
  commercial use case is much sensitive to the cost and is more tolerant to the reliability, unlicensed spectrum has more advantage than licensed spectrum.
  Sidelink positioning/ranging signal occupies large bandwidth( far more than 100MHz for 10cm accuracy), which is not efficient to use licensed spectrum
  In sum, for both V2X and commercial use case, very large bandwidth is required, unlicended spectrum is the best choice.
  Proposal 6: unlicensed spectrum is supported for sidelink positioning and ranging.
Country in Asia Pacific | ITS band
China | 5905-5925(Trial)
Japan | 755.5-764.5 and 5770-5850
Korea | 5855-5925
Australia | 5855-5925

## Slide 6: Scenario consideration
Sidelink based VS Sidelink assisted
  Sidelink based positioning and ranging: UE’s position or distance/angle is estimated from the signal transmited on sidelink
  Sidelink assisted positioning and ranging: UE’s position or distance/angle is estimated from signal transmitted on both Uu and sidelink
Uu
position or distance/angle estimation based only on SL signal measurement
SL
Uu
Measurement on SL signal
SL
Measurement on Uu signal
Output of UE’s position or distance/angle based on the combination of SL and Uu measurements
Uu
assist info
input
Sidelink based positioning and ranging
Sidelink assisted positioning and ranging
Sidelink assisted positioning and ranging

## Slide 7: Scenario consideration
Sidelink based positioning and ranging
  Applicable for the scenario that Uu based solution is not available or accurate, e.g. indoor, out of coverage, NLOS.
Sidelink assisted positioning and ranging
  Applicable for the scenario that both Uu based and SL based solution are available but not accurate.
    The scenario is limited.
    The gain may be marginal.
  Prefer to combine the SL and Uu solution based on implementation, i.e. without spec impact.
Proposal 7: Down prioritize the scenario of sidelink assisted positioning and ranging, no spec impact implementation is preferred

## Slide 8: DAS
Distributed Antenna System
  Mainly used in car, where multiple antennas can be deployed at different parts of the car.
  The antenna numbers, distribution pattern are diversed
    The antenna distribution can be any shape:
Proposal 8: DAS is preferred to be supported without spec impact.
Antenna #1
Antenna #2
Antenna #3
Antenna #4
Examples of distribution pattern of antennas
Due to the diversity in antenna pattern distribution, it is very hard to standardize the antenna distribution pattern. Solutions requires the antenna pattern info (e.g. number, distance interval, shape) on car is not applicable. Besides, reveal DAS information might not be acceptable for car vendor.

## Slide 9: Summary of proposals
Proposal 1: RAN to agree to use both term of sidelink positioning and ranging.
Proposal 2: Solution should allow acquiring either the whole 2D/3D coordinates or only one component of 2D/3D coordinates, e.g. distance or angle.
Proposal 3: A unified solution is applicable for sidelink positioning and Ranging.
  Proposal 4：Both commercial and V2X use cases need to be considered in sidelink positioning and Ranging
  Proposal 5: power consumption and cost reduction for IOT device should be considered.
  Proposal 6: unlicensed spectrum is supported for sidelink positioning and ranging.
  Proposal 7： Down prioritize the scenario of sidelink assisted positioning and ranging, no spec impact implementation is preferred.
  Proposal 8: DAS is preferred to be supported without spec impact.

## Slide 10: Potential Scope
Coverage: in coverage, partial coverage and out-of-coverage
Spectrum: licensed spectrum, Unlicensed band up to 71 GHz
Bandwidth: up to [400MHz] are considered
Sidelink based positioning and ranging with high priority, Sidelink assisted positioning with low priority
Power consumption: support power efficient positioning/ranging
Low cost: support Redcap UE, support high positioning/ranging signal bandwidth and small communication bandwidth
Support one-hop positioning/ranging
Support both network initiated and UE initiated positioning & Ranging
Support positioning/ranging signal on unlicensed band and control signaling on licensed band
  Sidelink positioning and ranging considering V2X, public safety and commercial use cases:

## Slide 11: Thanks