## Slide 1
Agenda Item: 9.0.2
Source: Samsung
Title: Sidelink enhancement for Rel-18
Document for: Discussion and Decision
3GPP TSG RAN Meeting #93-e
Electronic Meeting, September 13 - 17, 2021
RP-211796

## Slide 2: Motivation
New types of devices have been introduced in the industry and Rel-18 sidelink enhancement should be able to support those devices efficiently
  XR devices including AR glasses and HMDs (Head Mounted Displays)
  Unmanned Aerial Vehicles (UAV)
  Very low power (VLP) devices
  UEs for Public Safety based on NR (PS-NR)
  Self-driving cars for V2X
Rel-16/17 NR sidelink have been more focused on V2X use cases and further optimization is necessary for Commercial use cases and Public Safety in Rel-18 sidelink enhancement

## Slide 3: Key Features
LBT (listen-before-talk) for sidelink operation over unlicensed spectrum
  Channel access mechanism
  PHY channel structure
  Sidelink CSI feedback and sidelink HARQ procedures
Sidelink carrier aggregation
  To support license-assisted approach for Rel-18 completion on time and to keep backward compatibility with Rel-16/17 sidelink UEs
  To provide higher throughput for Rel-18 sidelink UEs operating in licensed spectrum
Multi-beam operation for sidelink not only in unlicensed spectrum but also in licensed spectrum
Performance comparison with Wi-Fi direct in terms of latency, power consumption, coverage and throughput
Licensed carrier
Unlicensed carrier
License-assisted approach
UE-1
UE-2
Multi-beam operation
UE-1
UE-2
West
East
North
South
A
B
C
D
FR2

## Slide 4: Proposed work scope for Rel-18
Category | Possible objectives | Working groups
CA | PC5 operation for CA | RAN1/2/4
 | Packet duplication | RAN2/3
Unlicensed band operation | Synchronization procedure | RAN1/2
 | Channel access procedure (LBE, FBE) | RAN1/2
 | Frame structure (time, frequency) considering regulations (LBT, OCB and PSD requirements) | RAN1
 | Resource allocation/scheduling (mode 1 and mode 2) | RAN1/2
 | HARQ procedure, power control | RAN1/2
 | CA specific operation (NSA, HARQ, CSI, …) | RAN1/2
MIMO | Increased layer or codewords (MIMO codebook, RS design) | RAN1/2
 | CSI enhancement (CSI contents) | RAN1/2