## Slide 1
Reconfigurable Intelligent Surfaces and Smart Repeaters for 5G-Advanced
3GPP TSG RAN Meeting #93-e
September 13-17, 2021
Agenda Item: 9.0.2
RP-212166
Source: Sony

## Slide 2: What are intelligent surfaces?
Broadly speaking, intelligent surfaces are electromagnetically active artificial structures with strong beamforming capabilities that can be used to reshape the propagation environment such as to improve capacity, coverage and energy efficiency.
They come in several flavors/types:
Type | Characteristics
Reflecting intelligent surfaces, a.k.a. reconfigurable intelligent surfaces (RISs) | Semi-passive and low-cost, due mainly to passive elements, i.e., no signal amplification or digital processing.
Relaying intelligent surfaces | Provide signal amplification but no signal regeneration or digital processing.
Active intelligent surfaces | Fully digital signal generation, i.e., extra-large massive MIMO.

## Slide 3: Reconfigurable intelligent surfaces for 5G-advanced
Of the three types of intelligent surfaces, RISs approach maturity, and the technology is becoming widely available. Thus, it is time to turn attention to standardization.
RISs can improve coverage and capacity in general and in particular for the following use cases:
  Remote video production.
  Immersive VR.
  Industrial IoT.
  Home entertainment.
  Indoor office.
RIS
UE
BS

## Slide 4: Study phase: Start with channel model enhancements for RIS
A channel model should be in place before an evaluation on the benefits of introducing RISs can be done, e.g., outage and peak data rates.
At least the following aspects should be covered in a study:
  Simulation scenarios and network layout
    Indoor and outdoor scenarios for FR1 and FR2.
  RIS device modeling
    Sizes and topologies under consideration.
    Radiation pattern of unit cells, polarization properties, amplitude/phase shift quantization, state-dependent radiation efficiency.
  Propagation aspects
    Whether near-field and spherical-wave propagation effects need to be modeled.
    Modeling of gNB-RIS and RIS-UE links, including association of paths in delay-angle, pathloss, NLOS/LOS, large-scale parameters (DS, AS, SF, K).
    Modifications to statistical channel models, e.g., CDL models, to account for RISs deployment density.

## Slide 5: Reconfigurable intelligent surfaces and smart repeaters
A related discussion topic is smart repeaters, which can be seen as an evolution of traditional repeaters combined with some side control information:
  Spatial Tx/Rx information (i.e., beamforming configuration information), timing information and TDD UL/DL split, ON/OFF information, transmit power information and bandwidth information.
Compared to RIS, smart repeaters can address different trade-offs between cost, HW complexity and power consumption:
  RIS likely requires larger aperture, while smart repeaters contain active components and RF combiners/splitters.
  Smart repeaters may enable larger cell-radius extension, due to active amplification, while RIS might be swiftly deployed to address blind coverage spots. Other co-existence strategies are also possible.
Important synergies between RIS and smart repeaters have been identified:
  Beam management of RIS and smart repeaters, which is also the main feature of smart repeaters compared to traditional ones. Potential enhancements, e.g., for RS measurements, CSI reporting, RACH procedure, etc. to reduce overhead due to additional beam combinations can also be studied.
  Design of the interface between gNB and RIS/smart repeaters to convey the aforementioned side control information, including physical layer transport mechanism.
  Interference mitigation of, e.g., inter-operator contamination by RIS and inter-cell interference by smart repeaters.

## Slide 6: Proposal for the Introduction of Reconfigurable Intelligent Surfaces and Smart Repeaters in Rel-18
To exploit synergies and make efficient use of time-units, it is proposed to study RIS and smart repeaters under the same Rel-18 SI.
Start with a study of RIS channel model enhancements and determine important use cases/scenarios.
Study the following items, common to both RIS and smart repeaters:
  Beam management of RIS and smart repeaters, including the need for potential enhancements to reduce overhead of, e.g., RS measurement, CSI reporting, and RACH procedure.
  Design of interface between gNB and RIS/smart repeaters, including the physical layer transport mechanism.
  Interference mitigation of, e.g., inter-operator contamination by RIS and inter-cell interference by smart repeaters, if needed.