## Slide 1: Discussion on the progress of Rel-17 NR MBS
Huawei (rapporteur)
RP-212267
Agenda Item: 9.3.2.4

## Slide 2: Scope clarification for intra-DU SFN for Rel-17 NR MBS
Discussions in RAN1#106e:
  Proposals regarding scrambling sequence initialization for PDCCH/PDSCH and TRS configured as QCL source for broadcast were discussed in RAN1#106e, in particular to support transmission in the SFN area. There was controversy at RAN1#106e whether SFN is in Rel-17 scope.
  NR MBS WID (RP-201038) implies support intra-DU SFN by transparent transmission and up to network implementation. However, as shown in RAN1#106e, intra-DU SFN for broadcast cannot be purely left up to network implementation and some essential components have to be specified to enable support of intra-DU SFN for broadcast, including
    Configurable scrambling sequence initialization for PDCCH/PDSCH and DMRS sequence generator initialization for PDCCH/PDSCH for broadcast transmission for broadcast as supported for RRC_CONNECTED UE.
    Configuring TRS as QCL sources for broadcast transmission as supported for RRC_CONNECTED UE.
  Pursuing the above discussions of SFN in RAN1 WG may continue facing the same argument that RAN1 is not responsible for the relevant objective as in the WID:
    Study the support for dynamic control of the Broadcast/Multicast transmission area within one gNB-DU and specify what is needed to enable it, if anything [RAN2, RAN3]
Proposal: To facilitate WG discussions,
  revising the WID to include RAN1 into the relevant objective:
    Study the support for dynamic control of the Broadcast/Multicast transmission area within one gNB-DU and specify what is needed to enable it, if anything [RAN1, RAN2, RAN3]
  Alternatively, confirm the support of intra-DU SFN in Rel-17 NR MBS and specify necessary components to enable its support.

## Slide 3: One controversial issue for broadcast in RAN1#106e
Discussions on common frequency resource (CFR) for broadcast in RAN1#106e:
  It has been agreed that the UE may assume the initial BWP as the default common frequency resource for group-common PDCCH/PDSCH, if a specific common frequency resource is not configured.
  When CFR is configured, it has been agreed that the CFR has the same size as the initial BWP, where the initial BWP has the same frequency resources as CORESET0 (i.e., Case A)
  In addition, supporting which case(s) among the same size as SIB1 configured initial BWP (case C), smaller size than SIB1 configured initial BWP (case D), and the other initial BWP with the size larger than SIB1 configured initial BWP (case E) was intensely discussed but without progress due to objection from one a single company at RAN1#106e on a proposed working assumption
  As most companies commented in RAN1#106e, supporting at least one more option with the size larger than CORESET0 is required for MTCH. Case C and case E may be both useful since the size of SIB1 configured initial BWP is up to network implementation.
  To speed up RAN1 WG discussion on broadcast, agreeing on the proposal from RAN1 chair notes can be the compromised way forward.
Proposal (from RAN1@106e): Support the following proposal from RAN1 chair notes:
  Proposal:
  For a configured/defined CFR for GC-PDCCH/PDSCH carrying MCCH and MTCH for broadcast reception with UEs in RRC IDLE/INACTIVE state.
  Support Case-C
  Working assumption: Support at least one of Case D and Case E.
    Down-selection to be made at RAN1#106b-e
  Note: Case C, D and E are defined in previous agreements