3GPP TSG RAN Meeting #93e	draft-RP-21xxxx

eMeeting, 13 - 17, September 2021	(Update of RP-210870)

# Source:	ZTE Corporation

# Title:	Work Item on NR smalldata transmissions in INACTIVE state

# Document for:	Approval

Agenda Item:	9.3.2.7

3GPP™ Work Item Description

Information on Work Items can be found at http://www.3gpp.org/Work-Items 
See also the 3GPP Working Procedures, article 39 and the TSG Working Methods in 3GPP TR 21.900

# Title: 	Updated Work Item on NR small data transmissions in INACTIVE state

## Acronym: NR_SmallData_INACTIVE

## Unique identifier:

NOTE:	For new WIs/SIs leave the Unique identifier empty and make a proposal for an Acronym.

For a revised WI/SI: Take Unique identifier and acronym as shown in 3GPP workplan.

If this is a RAN WID including Core and Perf. part, then Title, Acronym and Unique identifier refer to the feature WI.

Please tick (X) the applicable box(es) in the table below:

Either:

| This WID includes a Core part | X |
| --- | --- |
| This WID includes a Performance part | X |

or:

| This WID includes a Testing part |  |
| --- | --- |
| and it addresses the following 3GPP work area: | Radio Access |  |
|  | Core Network |  |
|  | Services |  |

## 1	Impacts

| Affects: | UICC apps | ME | AN | CN | Others (specify) |
| --- | --- | --- | --- | --- | --- |
| Yes |  | X | X |  |  |
| No | X |  |  | X |  |
| Don't know |  |  |  |  | X |

## 2	Classification of the Work Item and linked work items

### 2.1	Primary classification

This work item is a …

| X | Feature |
| --- | --- |
|  | Building Block |
|  | Work Task |
|  | Study Item |

### 2.2	Parent Work Item

| Parent Work Items |
| --- |
| Unique ID | Title |

NOTE:	RAN agreed some time ago, that it describes the feature WI + Core/Perf. part WI or Testing part WI in one WID. Therefore the table above should just include the feature WI Unique ID and title.

### 2.3	Other related Work Items and dependencies

| Other related Work Items (if any) |
| --- |
| Unique ID | Title | Nature of relationship |

NOTE:	Also related or dependent WIs/SIs in other TSGs should be indicated.

## 3	Justification

NR supports RRC_INACTIVE state and UEs with infrequent (periodic and/or non-periodic) data transmission are generally maintained by the network in the RRC_INACTIVE state. Until Rel-16, the RRC_INACTIVE state doesn’t support data transmission. Hence, the UE has to resume the connection (i.e. move to RRC_CONNECTED state) for any DL (MT) and UL (MO) data. Connection setup and subsequently release to INACTIVE state happens for each data transmission however small and infrequent the data packets are. This results in unnecessary power consumption and signalling overhead.

Specific examples of small and infrequent data traffic include the following use cases:

- Smartphone applications:

  - Traffic from Instant Messaging services (whatsapp, QQ, wechat  etc)

  - Heart-beat/keep-alive traffic from IM/email clients and other apps

  - Push notifications from various applications

- Non-smartphone applications:

  - Traffic from wearables (periodic positioning information etc)

  - sensors (Industrial Wireless Sensor Networks transmitting temperature, pressure readings periodically or in an event triggered manner etc)

  - smart meters and smart meter networks sending periodic meter readings

As noted in 3GPP TS 22.891, the NR system shall:

- be efficient and flexible for low throughput short data bursts

- support efficient signalling mechanisms (e.g. signalling is less than payload)

- reduce signalling overhead in general

Signalling overhead from INACTIVE state UEs for small data packets is a general problem and will become a critical issue with more UEs in NR not only for network performance and efficiency but also for the UE battery performance. In general, any device that has intermittent small data packets in INACTIVE state will benefit from enabling small data transmission in INACTIVE.

The key enablers for small data transmission in NR, namely the INACTIVE state, 2-step, 4-step RACH and configured grant type-1 have already been specified as part of Rel-15 and Rel-16. So, this work builds on these building blocks to enable small data transmission in INACTIVE state for NR.

## 4	Objective

### 4.1	Objective of SI or Core part WI or Testing part WI

This work item enables small data transmission in RRC_INACTIVE state as follows:

- For the RRC_INACTIVE state:

  - UL small data transmissions for RACH-based schemes (i.e. 2-step and 4-step RACH):

    - General procedure to enable transmission of small data packets from INACTIVE state (e.g. using MSGA or MSG3) including a CCCH message in the first UL message [RAN2]

    - Enable flexible payload sizes larger than the Rel-16 CCCH message size that is possible currently for INACTIVE state for MSGA and MSG3 to support UP data transmission in UL (actual payload size can be up to network configuration) [RAN2]

    - Context fetch and data forwarding (with and without anchor relocation) in INACTIVE state for RACH-based solutions [RAN2, RAN3]

Note 1: The security aspects of the above solutions should be checked with SA3

  - Transmission of UL data on pre-configured PUSCH resources (i.e. reusing the configured grant type 1) – when TA is valid

    - General procedure for small data transmission over configured grant type 1 resources from INACTIVE state including a CCCH message in the first UL message [RAN2]

    - Configuration of the configured grant type1 resources for small data transmission in UL for INACTIVE state [RAN2]

  - Specify RRM core requirements for small data transmission in RRC_INACTIVE, if needed [RAN4]

No new RRC state should be introduced in this WID. Transmission of smalldata in UL, subsequent transmission of smalldata in UL and DL and the state transition decisions should be under network control.

Focus of the WID should be on licensed carriers and the solutions can be reused for NR-U if applicable.

Specify configuring of SRB1 and SRB2 for small data transmission in RRC_INACTIVE state by reusing the framework for DRBs.

Note 2: Any associated specification work in RAN1 that is needed to support the above set of objectives should be initiated by RAN2 via an LS.

### 4.2	Objective of Performance part WI

NOTE:	Leave empty if the WI proposal does not contain a RAN performance part.

- Specify RRM test cases.

### 4.3	RAN time budget request (not applicable to RAN5 WIs/SIs)

NOTE:	For all new RAN related WIs/SIs which are not led by RAN WG5 the WI/SI rapporteur has to fill out the attached Excel table to request time budgets for corresponding RAN WG meetings.
The Excel table has to be filled out for all affected RAN WGs and up to the target date of the WI/SI.
One time unit (TU) corresponds to ~ 2 hours in the meeting.
If no TU is needed, then leave the field empty otherwise enter a number >0 in the field.

For revisions of already approved WI/SI descriptions: Please remove the Excel table from the WID/SID's zip file. The time budgets are already recorded. If you want to modify them, then this has to be done via the status report and not via a revised WID/SID.

If this WID is covering Core and Performance part, then please fill out one line for each part in the attached Excel table.

additional comments to the time budget request in the attached Excel table:

## 5	Expected Output and Time scale

| Impacted existing TS/TR {One line per specification. Create/delete lines as needed} |
| --- |
| TS/TR No. | Description of change | Target completion plenary# | Remarks |
| 38.300 | NR and NG-RAN Overall Description | TSG#95 | Core part |
| 38.331 | NG-RAN; Radio Resource Control (RRC) Protocol Specification | TSG#95 | Core part |
| 38.321 | NG RAN; Medium Access Control (MAC) protocol specification | TSG#95 | Core Part |
| 38.423 | NG-RAN; Xn Application Protocol (XnAP) | TSG#95 | Core part |
| 38.306 | NR; User Equipment (UE) radio access capabilities | TSG#95 | Core part |
| 38.133 | NR; Requirements for support of radio resource management | TSG#95 | Core part |
| 38.133 | NR; Requirements for support of radio resource management | TSG#97 | Performance part |

## 6	Work item Rapporteur(s)

Eswar Vutukuri

Company: ZTE Corporation

Email: eswar.vutukuri@zte.com.cn

## 7	Work item leadership

Primary: RAN2

Secondary: RAN3, RAN4

## 8	Aspects that involve other WGs

{Specify all the other WG(s) to be involved and, if specific, their task. E.g.: "SA2, SA3, SA5. CT6 for storage, and potentially SA4". If not applicable, indicate "None" or "None identified yet".}

See Note 1 and Note 2 above.

## 9	Supporting Individual Members

Supporting IM name

ZTE Corporation

Sanechips

LG Electronics

Panasonic

Interdigital

Oppo

Vivo

Huawei

HiSilicon

Futurewei

Intel

Qualcomm Incorporated

Nokia

Nokia Shanghai Bell

CMCC

China Unicom

China Telecom

APT

Fraunhofer HHI and Fraunhofer IIS

Apple

Xiaomi

Sony

Spreadtrum

Sierra Wireless

Blackberry

CATT

Sharp

Mediatek

Ericsson

Lenovo

Motorola Mobiility

NEC

Reliance Jio