3GPP TSG RAN#93e	RP-21xxxx

e-Meeting, September 13th – 17th, 2021

Agenda item:

Source: 	Thales (moderator)

Title: 	[93e-34-NR-NTN-WID] Email Summary

Document for:	Discussion/Decision

# Introduction

In this document, we will provide a summary on the discussion related to the revision of the Rel-17 NR-NTN-WID and whether to add new technical specifications.

The discussion will use as input

- RP-211784 NR-NTN-solutions WID revision, Thales

  - It provides reference for 3 new technical specifications/report added as per RAN#92-e agreement and provide corrections to one title and the email address of a rapporteur

- RP-212468 Considerations on upcoming submissions to ITU, Ericsson/Qualcomm

  - Proposal 1: Create new separate TS specifying UE radio transmission and reception for satellite access (Including satellite bands)

  - Proposal 2: Create new separate TS specifying Radio resource management requirements for satellite access

# Discussion

## Initial Round

Question: Should separate RAN4 Technical Specifications be created in order to specify satellite capable UE and RRM requirements for satellite access as per RP-212468 ?

| Company | Views |
| --- | --- |
| Thales | It is agreeable to create the two new TS specifying UE radio transmission and reception for satellite access (Including satellite bands) and Radio resource management requirements for satellite access However These TS should only apply to non-handheld terminals and refer to selected requirements of respectively TS 38.101-1 and TS 38.133 as needed. The TS 38.101-1 and TS 38.133 should be enriched with NTN bands since the characteristics of handheld NTN UE are very similar/same to the handheld TN UE and therefore, we do not see the need to create separate TSs for NTN handheld UE. |

Question: If the response to the previous question is positive, what should be the titles of the new technical specifications ?

| Company | Views |
| --- | --- |
| Thales | We suggest that the two additional technical specifications be entitled TS “User Equipment (UE ) radio transmission and reception (for non-handheld devices served by satellite access)” TS “Requirements for support of radio resource management (for non-handheld devices served by satellite access)” |

The moderator assumes that the suggested revisions in RP-211784 are not controversial and should be agreeable as is. However if there are some comments, companies can express their views here below.

| Company | Views |
| --- | --- |
| Thales | Revisions in RP-211784 are agreeable |

## Intermediate Round

## Final Round

# Conclusion

Based on the email discussion, the following are proposed:

TBD

# References

RP-211784 NR-NTN-solutions WID revision, Thales

RP-212468 Considerations on upcoming submissions to ITU, Ericsson/Qualcomm