## Slide 1: Views on Rel-18 UAV
Agenda Item: 8A.2
Source: Intel Corporation
Document for: Discussion
3GPP TSG RAN #94-e
e-Meeting, December 6th – 17th, 2021
RP-212916

## Slide 2: Status from October email discussion
Current objectives from draft WID created during October email discussion (RP-212715)
Specify the following enhancements on measurement reports [RAN2]:
  UE-triggered measurement report based on configured height thresholds
  Reporting of height, location and speed in measurement report
  Flight path reporting
  Measurement reporting based on a configured number of cells (i.e. larger than one) fulfilling the triggering criteria simultaneously
  Note: Work done in LTE is a starting point for this objective. NR-specific enhancements can be considered, if needed
Specify the signaling to support subscription-based aerial-UE identification [RAN3/SA2 interaction/RAN2]
  Note: Work done in LTE is a starting point for this objective.
[Specify needed enhancements for broadcast of UAV identification [RAN2, RAN1, SA2 interaction]]
  Applicable to both LTE and NR
  Note: This description is a placeholder for a more detailed objective to be drafted once SA2 will have concluded their study on the architectural aspects.
[Second priority] Study and, if needed, specify additional trigger condition(s) for CHO [RAN2].
[Second priority] Study and, if needed, specify the enhancements on beam management, with the following assumptions [RAN1, RAN4, RAN2]:
  FR1 with directional antenna at UE side
  gNB uptilt beamforming

## Slide 3: Comments on objectives in draft WID
Objectives 1-3 have wide support and should be included in the Rel-18 WI on UAV
Objective 4 and 5 are both indicated as ‘second priority’ and in this paper we provide some comments on these objectives
Comments on objective 4 on CHO enhancements for UAV
  The existing CHO mechanisms can be applied to UAVs in the same way as other UEs.
  Not critical to provide CHO enhancements specific to UAVs, in particular when WG capacity is considered
Proposal 1: Do not include objective 4 in the final WID on UAV

## Slide 4: Comments on beam management enhancements
There is no critical need to address beam management enhancements for FR1 with directional antenna at UE side.
  Digital beamforming with multiple antenna ports can be used to address issue of high interference generated by UAV at least for PUSCH
If beam management enhancements for FR1 are considered,
  Standardization efforts shall be minimized focusing on existing features for FR2 with updates to support FR1 SCS and FDD; consideration of new features will require more TUs in RAN1
  It should be clarified whether Rel-15 spatial relation or Rel-17 uplink TCI framework are expected to be used for FR1 beam management,
  At least RRM may be impacted and require RAN4 input, it should be clarified whether RAN4 has available TUs for this work.
gNB beamforming is already supported in FR1/FR2 by configuring multiple SSBs, there is no need to do additional study/work.
Proposal 2: Do not include objective 5 in the final WID on UAV