## Slide 1
3GPP TSG RAN Meeting #94-e RP-213045
Electronic Meeting, December 6 - 17, 2021
Views on upper layer aspects of Smart Repeaters project

## Slide 2: Upper layer aspects of Smart Repeater
The draft SID (RP-212703) includes the following high-level objectives:
  Scenarios and assumptions
  Side control information
  Smart repeater management
The objective on smart repeater management includes:
  Identification and authorization of smart repeater
  RF requirements for smart repeater
Aspects related to the smart repeater’s control- and user-plane functionality were also addressed in the Rel-18 RAN email discussions, but they have not been included in the draft SID.
  The discussions on these aspects did not converge sufficiently well to derive explicit assumptions in the SID. For that reason, they need to be further studied during the study item.
  This study should be included in the SID as an objective under “smart repeater management”.
  The study should be led by RAN2. RAN3 and RAN1 should also contribute to this study.
Proposal: The SID to include: “Study on control- and user-plane functionality for smart repeater [RAN2-led, RAN3, RAN1].”

## Slide 3: Proposed modification of SID objectives
4.1 Objective of SI or Core part WI or Testing part WI
The study on NR smart repeaters are to focus on the following scenarios and assumptions:
Consider smart repeaters used for extension of network coverage on FR1 and FR2 bands. Prioritize FR2 TDD deployments for both outdoor and O2I scenarios.
For only single hop stationary smart repeaters
Assuming smart repeaters are transparent to UEs
Smart repeater can maintain the gNB-repeater link and repeater-UE link simultaneously
Cost efficiency is a key consideration point for smart repeaters
Study and identify which side control information is necessary for smart repeaters including at least [RAN1, RAN2, RAN4]
Beamforming information
Timing information to align transmission / reception boundaries of smart repeater
Information on UL-DL TDD configuration
Power control information for efficient interference management
ON-OFF information for efficient interference management and improved energy efficiency
Study the following aspect of smart repeater management
Study on control and user plane functionality for the smart repeater [RAN2-led, RAN3, RAN1]
Identification and authorization of smart repeaters [RAN2, RAN3]
RF requirements for smart repeater, including max transmission power and other applicable RF requirements [RAN4]

## Slide 4: Conclusion
The following proposal has been made for the study on smart repeaters:
Proposal: The SID to include: “Study on control- and user-plane functionality for smart repeater [RAN2-led, RAN3, RAN1].”