## Slide 1: Way forward on unlicensed spectrum support for sidelink positioning/ranging in positioning enhancement WI Xiaomi, Philips, Robert Bosch GmbH, Qualcomm
3GPP TSG RAN Meeting #94
Electronic Meeting, Dec. 6 – 17, 2021
RP-213198

## Slide 2: Motivation for Unlicensed Spectrum
Issue of ITS spectrum
  The maximum ITS bandwidth in all regions is 80MHz. In some region, e.g. china, the available ITS bandwidth is only 20MHz.
  Note 1: According to the regulation, the maximum occupied bandwidth should be limited to 10 MHz
  Note 2: the final situation in Europe is not clear; usage of the whole 70 MHz by one technology or release is not finalized
  Note 3: based on the latest FCC rule, 5.850-5.895 GHz is designated to WiFi
  Observation 1: The ITS bandwidth in all the regions are no more than 80MHz, and in some regions, it is only 20MHz, far from enough to support V2X accuracy requirement.
  Observation 2: In some regions, the maximum occupied bandwidth is restricted
Country | ITS band | Bandwidth
China | 5905-5925(Trial) | 20
Japan | 755.5-764.5 and 5770-5850 | 80
Korea | 5855-5925(Note 1) | 70
Australia | 5855-5925 | 70
Singapore | 5875 – 5925 | 50
Europe | 5855-5925(Note 2) | 70
US | 5895-5925(Note 3) | 30

## Slide 3: Motivation for Unlicensed Spectrum
Issue of licensed spectrum
  Although licensed spectrum can provide large bandwidth (e.g. 500MHz), operators are in general reluctant to consume so much bandwidth for positioning services:
    Business mode is unclear: operators are unclear about how to make money from it
    Some operators do no have so many bandwidth available.
    Cost added to Customer: especially for commercial use case, the added cost for paying for licensed band will reduce their willingness to use this technology.
  Observation 3: Operators may have no desire/capability to use a large licensed spectrum bandwidth for sidelink positioning and Ranging .
  Out of coverage issue
    For commercial use cases, the typical scenario is indoor, where out of coverage is very common
    For V2X, there are scenarios e.g. tunnels, underground parking lot that may be out of coverage.
  Observation 4: For out of coverage scenario, e.g. indoor/tunnels, licensed spectrum can not be used.

## Slide 4: Main aspects to address to enable use of unlicensed spectrum
Aspect 1：Rel-17 SL does not support unlicensed spectrum yet
  One possible solution to address this:
    at initial stage, SL-enhancement designs the general LBT procedure for unlicensed spectrum;
    at a later stage, after SL pos & and ranging SI/WI has finished the design of the positioning/ranging signal, then SL-enhancement takes into account the positioning/ranging signal for LBT.
Proposal : Add a note in the Release 18 sidelink enhancement WID to clarify that sidelink positioning/ranging signal in unlicensed spectrum should be considered in the design, after SL pos and ranging in the positioning WI has progressed with the design of the signal.
Aspect 2: Several companies do not yet see the necessity of considering unlicensed band support, and say that it e.g. depends on whether the current ITS band can support the V2X accuracy requirement
  We suggest to further evaluate the needs for considering unlicensed spectrum for sidelink positioning in the study phase and study the accuracy that can be achieved for both licensed and unlicensed for the various bandwidths. Based on the results of the study phase, we can progress with unlicensed spectrum additionally in the work item phase.

## Slide 5: Proposed Way Forward
Given that it seems controversial whether the ITS band is capable of meeting the accuracy requirement of V2X. It is too early to make decision on what spectrum will be considered for SL positioning and ranging.
Proposal 1: Include in the SL Positioning study phase scope, the study and evaluation of the spectrum and bandwidth requirements in order to meet the positioning and ranging accuracy.
Proposal 2: Add a note in the Release 18 sidelink enhancement WID to clarify that sidelink positioning/ranging signal in unlicensed spectrum should be considered in the design, after SL pos and ranging in the positioning WI has progressed with the design of the signal.

## Slide 6: Thanks