## Slide 1
On AI/ML study over air interface
3GPP TSG RAN Meeting #94e RP-213266
e-Meeting, December 6th – 17th , 2021
Source: vivo
Document for: Discussion & Decision
Agenda Item: 8.A.1

## Slide 2
Proposal 1: The 5 use cases summarized in RP-212708 for AI/ML study over air interface is a well balanced set for study as a starting point. Further down-selection in RANP-94e is not needed.
Proposal 2: The description of the 4 use cases led by RAN1 can be further refined to be more specific to include RS overhead reduction.
Proposal 3: The target of RRM mobility enhancement should be more generic and also include higher experience throughput/system efficiency.
On use case for AI/ML study over air interface
Use cases to focus on:
Initial set of use cases includes:
  CSI feedback enhancement, e.g., RS and payload overhead reduction, improved accuracy, prediction [RAN1]
  Beam management, e.g., beam prediction in time, and/or spatial domain for overhead and latency reduction, RS overhead reduction, beam selection accuracy improvement [RAN1]
  Positioning accuracy enhancements and RS overhead reduction for different scenarios including, e.g., those with heavy NLOS conditions [RAN1]
  DM-RS overhead reduction [RAN1]
  RRM Mobility, e.g., prediction in time or frequency for robustness, interruption and overhead reduction, higher experienced throughput/system efficiency [RAN2]
Finalize representative set of use cases (reduced from the initial set and minimizing sub use cases) for characterization and baseline performance evaluations

## Slide 3
On AI/ML application over DMRS overhead reduction
  The near-optimal AI/ML network largely reduces the MSE with lower DMRS overhead and without assistance of TRS.
AI
Channel on DMRS resources
Channel on all resources
With DMRS signal
Without DMRS signal
Chart: Tput for TDL-B 100ns, 90km/h
| 18 | 22 | 26 | 30 | 34
AI, 50% overhead | 1160109.2857 | 1512688.2857 | 1781904.7143 | 1929178.1429 | 2037041.2857
No AI, 100% overhead | 1160720.8571 | 1512032.5714 | 1779348 | 1923738.5714 | 2016582.8571
TDL-A, type1，MCS7
TDL-A, type1，MCS0
Parameters：UE speed 3km/h, delay spread 300ns, carrier frequency 3.5GHz, 1 gNB antenna, 1 UE antenna, 32 RBs. DMRS takes 6 subcarriers in 1 RB and 2 symbol in 1 slot.

## Slide 4
On AI/ML application over DMRS overhead reduction
Experiments with channel emulators
  The near-optimal AI/ML network largely reduces the MSE, without assistance of TRS, with half overhead compared to Rel-15 NR design.
Parameters：One AI model is used for all scenarios. SNR -5~30dB, UE speed 0~90km/h, TDL-A/B/C/D/E, delay spread 0~300ns, carrier frequency 3.5GHz, 1 gNB antenna, 4 UE antennas, 16 RBs. DMRS takes 6 subcarriers in 1 RB and 2 symbol in 1 slot.
Channel emulator
X86+FPGA
Signal transeiver (USRP)
Signal generator

## Slide 5
On AI/ML application over DMRS overhead reduction
Experiments over the air
  The near-optimal AI/ML network largely reduces the MSE, without assistance of TRS, with half overhead compared to Rel-15 NR design.
  The model is trained with limited LLS generated data set, but still show performance gains when directly applied over the air.
Parameters：One AI model is used for all positions. This AI model is trained by using LLS channel data, in which SNR 0~34dB, UE speed 0~1km/h, TDL model with random delay and random power for each path, maximum delay spread 0~200ns, carrier frequency 3.5GHz, 1 gNB antenna, 4 UE antennas, 4 RBs for AI model input and 48 RBs for air test. DMRS takes 6 subcarriers in 1 RB and 2 symbol in 1 slot.
Transmit antenna
Position 1 of receive antennas
Position 2 of receive antennas
Position 3 of receive antennas
Position 4 of receive antennas

## Slide 6
On AI/ML application for SRS overhead reduction for DL CSI
Parameters： LLS, UE speed 3km/h, CDL-B 300ns, carrier frequency 3.5 GHz, 16 gNB antennas, 4 UE antennas, 12 RB, maximum 1 layer, wideband or PRG2.
…
comb size
SRS for antenna switching
AI
Pre-coding wideband/subband
In comparison with comb 2 SRS in Rel 15/16,
  AI-based DL CSI acquisition for comb size = 12 achieves similar throughput performance without power boosting
  AI-based DL CSI acquisition for comb size = 12 obtains more than 2dB gain in low SNR range if power boosting applied
SRS

## Slide 7
On AI/ML application for CSI-RS overhead reduction for DL CSI acquisition
  Using 50% CSI-RS overhead, AI based CSI-RS compression could achieve better throughput than traditional algorithm with 100% CSI-RS overhead.
Parameters：LLS, UE speed 3km/h, CDL-C 300ns, carrier frequency 3.5G Hz, 32 gNB antennas, 32 CSI-RS ports, 4 UE antennas, 52 RBs. AMP and LAMP use 50% CSI-RS overhead.
CSI-RS compression
Full antenna ports
Wireless Channel
Less CSI-RS ports
AI based estimation
Estimation of Full antenna ports
gNB
UE