## Slide 1: RP-213519 Moderator’s summary for [94e-29-R18-gNB-CU]
NTT Docomo (Moderator)

## Slide 2: Necessity of the project / Justifications
Majority thinks study is needed/acceptable, at least for identifying scenarios and see if solutions
  Inter-node coordination required on “entire node failure”.
  Need for inter-operable solutions.
Still some oppositions:
  “Equipment-level stability” is enough
  If not enough, resiliency can still be improved by private implementations
    TS 38.401 says:
    NOTE: For resiliency, a gNB-DU may be connected to multiple gNB-CUs by appropriate implementation.
  Many scenarios to look at
Opponents wants to have clear scenario that cannot be solved by private implementations
This needs “solution” discussion at the plenary level

## Slide 3: Justifications
The split NG-RAN architecture is characterised by the presence of a single logical gNB-CU-CP connected to multiple logical gNB-DUs and logical gNB-CU-UPs, for each split gNB. Such architecture is affected by a single point of failure at the gNB-CU-CP. Failures at the gNB-CU-CP may cause interruption of UP traffic and disconnection of UEs.
For these reasons, failure scenarios which cannot be solved by currently specified means and corresponding interoperable recovery solutions should be studied that allow to recover from such failures ideally without any UP interruptions or UE disconnections/interruptions at CP level. Any potential solution studied should be based on the current NG-RAN architecture.
Alignment to the change in the objective sections
Minor improvements

## Slide 4: Objectives
The study should be based on the current architecture framework for the NG-RAN (i.e. no new interfaces should be defined).
The detailed objectives of the SI are listed as follows:
Define and study failure scenarios associated with the gNB-CU-CP
  Focus on scenarios involving an entire node failure of the gNB-CU-CP.
Identify and study solutions for recovery of failures at the gNB-CU-CP, for enhanced resiliency
  NOTE 1: Solutions for gNB-CU-CP failure recovery should minimise signalling towards the UE and signalling load towards the network
  NOTE 2: Solutions for gNB-CU-CP failure recovery should minimise UP interruptions, namely they should minimize the service downtime from the end-user perspective.
  NOTE 3: Solutions for minimisation of control plane interruptions should also be targeted
  NOTE 4: No new signalling between the UE and the network should be defined
Focus on “entire node failure” scenario
Clarify that no Uu spec impact is intended
Other minor improvements

## Slide 5: SI or TEI
No consensus
This question is almost identical to the necessity of this project.
Study cannot be managed without structured discussion based on a SID scope, guidance from SI rapporteur, documentation of scenarios & associated solutions in a TR etc.
Promotors of TEI think that no “study phase” is needed, and want interested companies to first clarify specific standardization impacts
  One of the promotors assume “Stage-2 clarifications”

## Slide 6: Moderator Recommendations
1: Study failure scenarios and potential solutions
2: Finalize the SID next week
Background (observations)
  High interest from companies
  Necessity and feasibility of potential solutions, and/or standardization can still be assessed
  Opponents’ doubt on the necessity of the project would not progress without structured technical discussions on failure scenarios