## Slide 1
3GPP TSG RAN Meeting #98e RP-222837
Electronic Meeting, December 12-16, 2022
Agenda item : 9.3.1.4
Source : Samsung
Title : Checkpoint assessment: NR MIMO evolution for downlink and uplink
Document for : Discussion

## Slide 2: Background | WID per RP-213598
RAN1:
Study, and if justified, specify CSI reporting enhancement for high/medium UE velocities by exploiting time-domain correlation/Doppler-domain information to assist DL precoding, targeting FR1, as follows:
  Rel-16/17 Type-II codebook refinement, without modification to the spatial and frequency domain basis
  UE reporting of time-domain channel properties measured via CSI-RS for tracking
Specify extension of Rel-17 Unified TCI framework for indication of multiple DL and UL TCI states focusing on multi-TRP use case, using Rel-17 unified TCI framework.
Study, and if justified, specify larger number of orthogonal DMRS ports for downlink and uplink MU-MIMO (without increasing the DM-RS overhead), only for CP-OFDM,
  Striving for a common design between DL and UL DMRS
  Up to 24 orthogonal DM-RS ports, where for each applicable DMRS type, the maximum number of orthogonal ports is doubled for both single- and double-symbol DMRS
Study, and if justified, specify enhancements of CSI acquisition for Coherent-JT targeting FR1 and up to 4 TRPs, assuming ideal backhaul and synchronization as well as the same number of antenna ports across TRPs, as follows:
  Rel-16/17 Type-II codebook refinement for CJT mTRP targeting FDD and its associated CSI reporting, taking into account throughput-overhead trade-off
  SRS enhancement to manage inter-TRP cross-SRS interference targeting TDD CJT via SRS capacity enhancement and/or interference randomization, with the constraints that 1) without consuming additional resources for SRS; 2) reuse existing SRS comb structure; 3) without new SRS root sequences
  Note: the maximum number of CSI-RS ports per resource remains the same as in Rel-17, i.e. 32
Study, and if justified, specify UL DMRS, SRS, SRI, and TPMI (including codebook) enhancements to enable 8 Tx UL operation to support 4 and more layers per UE in UL targeting CPE/FWA/vehicle/Industrial devices
  Note: Potential restrictions on the scope of this objective (including coherence assumption, full/non-full power modes) will be identified as part of the study.
Study, and if needed, specify the following items to facilitate simultaneous multi-panel UL transmission for higher UL throughput/reliability, focusing on FR2 and multi-TRP, assuming up to 2 TRPs and up to 2 panels, targeting CPE/FWA/vehicle/industrial devices (if applicable)
  UL precoding indication for PUSCH, where no new codebook is introduced for multi-panel simultaneous transmission
    The total number of layers is up to four across all panels and total number of codewords is up to two across all panels, considering single DCI and multi-DCI based multi-TRP operation.
  UL beam indication for PUCCH/PUSCH, where unified TCI framework extension in objective 2 is assumed, considering single DCI and multi-DCI based multi-TRP operation
    For the case of multi-DCI based multi-TRP operation, only PUSCH+PUSCH, or PUCCH+PUCCH is transmitted across two panels in a same CC.
Study, and if justified, specify the following
  Two TAs for UL multi-DCI for multi-TRP operation
  Power control for UL single DCI for multi-TRP operation where unified TCI framework extension in objective 2 is assumed.
For the case of simultaneous UL transmission from multiple panels, the operation will only be limited to the objective 6 scenarios.
Check RAN1 workload situation at RAN#98 (Dec 2022). (emphasis added)
Dec 2022 (RAN#98) checkpoint assessment:
Whether the progress of each objective is on track
Whether the progress of overall WI is on track
Whether scope refinement and/or reduction is needed to ensure successful Core completion:
  RAN1: by Sept 2023
  RAN2/4: by Dec 2023
”On track” assessment:
A total of 8 RAN1 meetings starting from RAN1#109-e
  Less TU allocation in the first meeting
By RAN#98, 4 RAN1 meetings have occurred
  Since RAN2/4 Core work hasn’t started, ~40-45% completion in Core is expected to be “on track”

## Slide 3: Assessment | Rapporteur perspective
Most of the topics in the objectives are on or ahead of schedule while some are progress-challenged
Despite the hurdles, the overall progress is good and the WI in on track for successful completion
Obj | Topic | Work scope | Status | Hurdles to be overcome
1 | High/medium velocity CSI | Medium | On track: Type-II codebook ahead of schedule, TRS-based TD reporting slightly behind schedule | Divergent views on TD reporting type (expected to be resolved in RAN1#112)
2 | Unified TCI mTRP | Medium | On track: on schedule with some contentious detailed issues | Divergent views on TCI signaling, and details on associating indicated TCIs to TRPs (incl. sTRP/mTRP switching)
3 | Increased # DMRS ports | Small | On track: ahead of schedule | None
4 | Coherent JT (CJT) mTRP CSI and SRS | Medium | On track: Type-II codebook ahead of schedule. SRS for TDD CJT behind schedule | A number of unresolved “study” issues and options for SRS for TDD CJT
5 | 8Tx DMRS, SRS, TPMI/SRI for >=4 layers | Large | On track: DMRS ahead of schedule, SRS on schedule, TPMI/SRI behind schedule | A number of unresolved TPMI/SRI “study’ issues and options related to 2-CW (if confirmed), partial/non-coherent codebooks, and UL full-power modes
6 | Two-panel simultaneous-TX (STx2P) | Medium | On track: UL precoding on schedule, beam indication (overlap with obj. 2) on schedule | Divergent views on SRI/TPMI design and SRS configuration depending on beam indication and panel assumption
7 | 2TA for M-DCI and UL PC for S-DCI | Small | On track: 2TA on schedule, UL PC for S-DCI slightly behind schedule | Divergent views on TAG ID association, key issues of UL PC for S-DCI awaiting outcomes from obj. 2

## Slide 4: Conclusion | Rapporteur perspective
Each objective is on track for successful completion
  Some sub-objectives are ahead of schedule, some other are on schedule, with a few progress-challenged topics
  Essential to limit the work to what is clearly described/defined by the objective – no scope expansion
The overall WI is on track for successful completion
  By RAN#98, ~40-45% Core completion (RAN1 only)
From rapporteur perspective, no immediate need for scope refinement and/or reduction in RAN#98
Some TUs are allocated for RAN2/4 starting in April/Feb 2023 for Rel-18 MIMO Evolution:
  RAN1 can provide early inputs to RAN2/4 to start some work
  Facilitate smoother process and successful Core completion in RAN2/4