## Slide 1: Channel modelling issue for Rel-19 Sensing
3GPP TSG RAN#98-e
Electronic Meeting, 12th – 16th December, 2022
RP-222842
Xiaomi

## Slide 2: Difficulties found for channel model used for sensing evaluation
Observation 1: It is difficult to use the channel model(s) given in 38.901 to evaluate the sensing feasibility/performance.
We found the following difficulties while reusing the channel model(s) (including TDL (Tapped Delay Line), CDL (Clustered Delay Line), fast fading model and so on) given in 38.901:
It is difficult to define the interference caused by the environment (e.g. reflection interference caused by environment object), especially for RX/TX collocated sensing.
  The LOS channel of reflection from the environment object causes strong interference to the receiver.
  It is difficult to define the location of the environment object, which is critical to determine the environment interference to the receiver.
    It is difficult to use TDL to locate the environment object, as TDL has no angle information.
    It is difficult to use CDL/fast fading model to locate the environment object, as the angle from CDL/fast fading model is based on statistics (which could be based on one or more reflections for one cluster).
It is difficult to define the small-scale two-way channel path.
It is difficult to define the sensing target/object, especially when the target is not a UE.
The RCS(s) (Radar cross-section) for many substances and frequencies are missing.

## Slide 3: Solution directions for sensing channel model
Proposal 1: Two solution directions, i.e., creating channel model based on CDL and creating channel model based on ray tracing can be considered for sensing channel model.
The following solution directions can be considered for sensing channel model:
Solution direction 1: Creating channel model based on CDL.
  The geometric description covers arrival angles from the last bounce scatterers and respectively departure angles to the first scatterers interacted from the transmitting side. The angle information and delay information cannot match.
    Option 1: To locate the environment object based on AOD, ZOD, and delay.
    Option 2: To locate the environment object based on AOD, ZOD, AOA, and ZOD.
    Option 3: Modelling the multi-bounce scatters, e.g., 2-bounce.
  Relatively small workload (slightly preferred).
Solution direction 2: Creating channel model based on ray tracing.
  It is not clear how to model the correlation between environment object and sensing object.
  Relatively large workload.
Illustration of cluster locations generated by option 1

## Slide 4: Solution directions for two-way channel path of sensing channel model
Proposal 2: RAN is kindly requested to provide guidance for the channel modelling of Rel-19 Sensing.
The following solution directions can be considered for two-way channel path of sensing channel model:
Solution direction 1: LOS-only, only LOS paths are considered.
  Low model complexity, low model accuracy, similar with the current Radar systems.
Solution direction 2: Fully-connected, N paths are considered in the forward link, and the ith path has N echo paths, totally N2 paths.
  High model complexity, high model accuracy, may introduce false-target in the Radar detection profile.
Solution direction 3: Randomly-coupled, N paths are considered in both the forward link and reverse link, the paths of two ways are randomly coupled, totally N paths.
  Moderate model complexity, moderate model accuracy.
Observation 2: Different two-way channel path modellings can make a trade-off between model accuracy and model complexity.
Solution direction 1
Solution direction 2
Solution direction 3

## Slide 5: Conclusion
Observation 1: It is difficult to use the channel model(s) given in 38.901 to evaluate the sensing feasibility/performance.
Observation 2: Different two-way channel path modellings can make a trade-off between model accuracy and model complexity.
Proposal 1: Two solution directions, i.e., creating channel model based on CDL and creating channel model based on ray tracing can be considered for sensing channel model.
Proposal2: RAN is kindly requested to provide guidance for the channel modelling of Rel-19 Sensing.

## Slide 6: Thanks