## Slide 1: WI scope for Network Energy Saving from RAN2 perspective
LG Electronics

## Slide 2: SI scope in RP-213554
1. Definition of a base station energy consumption model [RAN1]
  Adapt the framework of the power consumption modelling and evaluation methodology of TR38.840 to the base station side, including relative energy consumption for DL and UL (considering factors like PA efficiency, number of TxRU, base station load, etc), sleep states and the associated transition times, and one or more reference parameters/configurations.
2. Definition of an evaluation methodology and KPIs [RAN1]
  The evaluation methodology should target for evaluating system-level network energy consumption and energy savings gains, as well as assessing/balancing impact to network and user performance (e.g. spectral efficiency, capacity, UPT, latency, handover performance, call drop rate, initial access performance, SLA assurance related KPIs), energy efficiency, and UE power consumption, complexity. The evaluation methodology should not focus on a single KPI, and should reuse existing KPIs whenever applicable; where existing KPIs are found to be insufficient new KPIs may be developed as needed.
  Note: WGs will decide KPIs to evaluate and how.
3. Study and identify techniques on the gNB and UE side to improve network energy savings in terms of both BS transmission and reception, which may include:
  How to achieve more efficient operation dynamically and/or semi-statically and finer granularity adaptation of transmissions and/or receptions in one or more of network energy saving techniques in time, frequency, spatial, and power domains, with potential support/feedback from UE, and potential UE assistance information [RAN1, RAN2]
  Information exchange/coordination over network interfaces [RAN3]
  Note: Other techniques are not precluded

## Slide 3: TUs allocated for NES SI/WI
According to the latest TU budget (RP-221925)
  The SI is converted to WI from R2#121
  For WIs, total 6 TUs are allocated, 1 TU/meeting for 6 meetings.
  The WI should focus on essential topics to be fit to the allocated TUs.

## Slide 4: Topics discussed in SI phase
DTX/DRX mechanism
SSB/SIB-less/paging
Cell selection/re-selection
Connected mode mobility
  CHO and group mobility
Others
  Wake-up signal, resource adaptation, BWP adaptation, NES state determination and signaling
Not all the above topics can be discussed in WI phase.
It is important to pick essential topics from the above.

## Slide 5: Considerations on RAN2 topics - DTX/DRX mechanism
RAN2#120 agreements
Observation
  Signaling design, DTX/DRX operation, activation and deactivation, and DTX/DRX alignment are essential feature of NES. Estimated TU is 4 TUs.
Proposal
  Cell DTX/DRX mechanism should be developed in WI phase.

## Slide 6: Considerations on RAN2 topics - SSB/SIB-less/paging
RAN2#120 agreements
Observation
  Introduction of non-anchor cell has huge impacts on RAN2, e.g. system information design, accessing non-anchor cell, acquiring system information in non-anchor cell. Estimated TU is 6 TUs.
Proposal
  SSB/SIB-less/paging is a secondary feature of NES, and do not consider in Rel-18.

## Slide 7: Considerations on RAN2 topics - Cell selection/re-selection
RAN2#120 agreements
Observation
    Barring legacy UE to NES cell is a necessary feature, and it minimizes the RAN2 impacts. Estimated TU is 2 TUs.
  Proposal
    Legacy UE barring mechanism to NES cell should be developed in WI phase.

## Slide 8: Considerations on RAN2 topics - Connected mode mobility
RAN2#120 agreements
Observation
  CHO framework is an optimization feature of NES enabling faster on/off loading. Estimated TU is 3 TUs. Other features related to connected mode mobility is already excluded in RAN2.
Proposal
    Connected mode mobility is an optimization feature, and do not consider in Rel-18.

## Slide 9: Considerations on RAN2 topics - Other aspects
RAN2#120 agreements
Observation
  Wake-up signal is an optimization feature of NES enabling further power saving. If it is introduced, there are some impacts on RAN2. Estimated TU is 2 TUs.
  Other aspects e.g. resource adaptation, BWP adaptation, NES state determination and signalling are not fully discussed in RAN2.
Proposal
    Wake-up signal is an optimization feature, and do not consider in Rel-18.

## Slide 10: Summary of Proposed RAN2 Scope for NES
Rel-18 NES WI should include following topics
  Cell DTX/DRX mechanism
    Signaling design, configuration and operation, and activation and deactivation
  Legacy UE barring mechanism to NES cell
Do not consider following topics in Rel-18 NES WI
  SSB/SIB-less/paging (non-anchor cell)
  Connected mode mobility (CHO, group handover)
  Other aspects (WUS, resource adaptation, BWP adaptation, NES state determination and signaling)