## Slide 1: Discussion on XR enhancement SI from RAN2 perspective
LG Electronics

## Slide 2: SI scope in RP-220285
Objectives on XR-awareness in RAN (RAN2):
  Study and identify the XR traffic (both UL and DL) characteristics, QoS metrics, and application layer attributes beneficial for the gNB to be aware of.
  Study how the above information aids XR-specific traffic handling.
Objectives on XR-specific Power Saving (RAN1, RAN2):
  Study XR specific power saving techniques to accommodate XR service characteristics (periodicity, multiple flows, jitter, latency, reliability, etc...). Focus is on the following techniques:
    C-DRX enhancement.
    PDCCH monitoring enhancement.
Objectives on XR-specific capacity improvements (RAN1, RAN2):
  Study mechanisms that provide more efficient resource allocation and scheduling for XR service characteristics (periodicity, multiple flows, jitter, latency, reliability, etc…). Focus is on the following mechanisms:
    SPS and CG enhancements;
    Dynamic scheduling/grant enhancements.

## Slide 3: Original plan for XR enhancement SI/WI
  The SI is planned to be converted to WI from R2#121.
  For WIs, total 12 TUs are allocated, 2 TU/meeting for 6 meetings.
  According to the latest TU budget (RP-221925)
SA2 status
  SA2 decides to postpone the completion date to December 2022.

## Slide 4: Topics discussed in SI phase
XR-awareness
  PDU sets and data bursts
    How PDU sets can be mapped to DRBs and how the LCH configuration works.
    How “traffic flow without PDU set” fits in with XR traffic awareness.
  PDU prioritization
    Whether PDU prioritization is needed for XR traffic, and how should it work, e.g. whether there are impacts to LCP mechanism, how does the PDU set importance work.
  PDU discard
    How to handle PDU discarding of XR traffic, e.g. do we need new discard timers, how to handle PDU discard in PDCP and/or RLC.
XR-specific power saving
  DRX enhancements
    How DRX can be configured for XR, how to switch between DRX configurations and how does that impact power saving.
    Whether/what RAN2 needs for the non-integer DRX periodicity.
    Whether XR requires multiple DRX configurations active at the same time.
  Other enhancements
    How traffic and QoS related information on uplink traffic should be provided to RAN for UE power savings
XR-specific capacity improvements
  Feedback enhancements
    How enhanced BSR works for XR (e.g. information needed, overhead, impact to capacity, etc.).
  Scheduling enhancements
    Scheduling enhancements to improve XR capacity.
    CG enhancements and UE assistance information for XR.

## Slide 5: Considerations on XR-awareness
PDU sets and data bursts
  For PDU set – QoS flow – DRB mapping, 4 alternatives were discussed, and one of them (1 QoS flow – N DRBs) was excluded.
  Feasibility of mapping between different types of PDU sets to the same QoS flow, and whether to have different treatment of different types of PDU in the same QoS flow in RAN (e.g. splitting DRB into multiple LCHs) is subject to SA2 decision.
  RAN2 needs more time to finalize mapping alternatives considering SA2 decision.
PDU prioritization
  It was agreed that legacy mechanisms of SDAP SDU handling, retransmission, and LCP procedure are sufficient for XR.
  No further work is needed in WI phase.
PDU discard
  It was agreed that timer-based discard operation applies to all SDUs/PDUs belonging to the same PDU set.
  Details of discard mechanism for PDU set can be progressed in WI phase.

## Slide 6: Considerations on XR-specific power saving
DRX enhancements
  It was agreed that non-integer DRX periodicity is supported at least in a semi-static manner.
  Details of support for non-integer DRX periodicity can be progressed in WI phase.
  Other aspects of DRX enhancements were not much discussed, and only vague agreements were made.
    RAN2 can study e.g. periodicity, arrival time, jitter and frame-size variations for XR awareness to enable power savings and capacity enhancements. Can study also how often such parameters change (i.e. how dynamic they are).
    RAN2 to focus on the following issues for power saving, as well necessary parameters XR-awareness to support such enhancements, i.e.:
      DRX enhancements to address the issues of DRX cycle mismatch and jitter;
      Identify necessary parameters from CN for XR-awareness for power saving.
    RAN2-specific aspects can be studied based on contributions (e.g. multiple XR traffic flows with different periodicities, SFN wrap-around, RAN2-specific CDRX aspects, …).
  RAN2 needs more time to make concrete scope of DRX enhancement.
Other enhancements
  Various proposals were submitted, but not much discussed. Anyway, essentiality of other enhancements were not justified.
  No further work is needed for XR-specific power saving other than DRX enhancements.

## Slide 7: Considerations on XR-specific capacity improvements
Feedback enhancements
  It was agreed to enhance BSR mechanism including BSR table, BSR trigger, and BSR format.
  Details of BSR enhancement for XR can be progressed in WI phase.
Scheduling enhancements
  It was agreed that uplink CG can be enhanced subject to RAN1 decision.
  It was agreed that downlink SPS is not beneficial for XR.
  Details of CG enhancement for XR can be progressed in WI phase, subject to RAN1 decision.

## Slide 8: Summary of XR progress in SI phase in RAN2
XR-awareness
  Discard mechanism for PDU set can be progressed in WI phase.
  PDU set – QoS flow – DRB mapping, and splitting DRB to multiple LCHs requires SA2 input.
  No other mechanism for PDU prioritization is needed.
XR-specific power saving
  Support for non-integer DRX periodicity can be progressed in WI phase.
  More time is required to make concrete scope of DRX enhancement.
  No other mechanism for XR-specific power saving is needed.
XR-specific capacity improvements
  BSR enhancement for XR can be progressed in WI phase.
  CG enhancement for XR can be progressed in WI phase, subject to RAN1 decision.

## Slide 9: Proposals
Extend the XR enhancement SI for one quarter
For Q1 2023, the SI focus should be on;
  PDU set – QoS flow – DRB mapping, and splitting DRB to multiple LCHs.
  Concrete scope of DRX enhancement (what is in and what is out), e.g.
    Multiple DRX configurations
    Dynamic DRX configuration switch
    SFN wrap-around