## Slide 1: Proposal on conducting the study of Integrating Sensing and Communication in NR
China Telecom
December 2022
3GPP TSG RAN #98-e
Electronic Meeting, December 12 – 16, 2022
Agenda: 9.1
RP-222951

## Slide 2: Background
5G New Radio (NR) systems are deployed to offer high data rates and ultra-reliable low latency services. Vertical industries start to apply 5G to improve the industry automation and digitalization, in many scenarios, the Integrated Sensing and Communication(ISAC) is a key enabler to provide high quality services. The ISAC can extend the capability of network from “listen and talk” to “see and feel” and create a digital sense augmenting human intelligence.
With ISAC, the smart devices will have the capability to sense their surroundings, and exchange their observations through communication. In addition, with Artificial Intelligence (AI) combined with sensing capability, the network will have the cognitive ability to fuse the physical and biological worlds with cyber worlds and provide various intelligent services for consumers and industry customers.
Local Space
Intelligent Factory
Smart Home
Smart Office
Healthcare
Open Space
Automatic Driving
UAV Network
Environment Monitoring
Space-Terrestrial Integrated Network
Figure1 - Diverse applicable scenarios for wireless sensing

## Slide 3: Motivation
Many new emerging businesses require sensing capability to provide accurate and timely services, however, traditional radar technology is high cost to deploy and not flexible enough to extent to current diverse services.
Although 5G already offer the positioning functions by means of beam detection/tracking, many studies show that ISAC can provide more accuracy and richer sensing content than the 5G existing sensing capability.
With the use of higher frequency bands (from mm-Wave to THz), wider bandwidth, and denser distribution of massive arrays in 5G and future 6G systems, it is possible to enable the integration of wireless sensing and communication in a single system and mutually enhance each other.
  Sensing exploration: With sensing capability, the 5G system as a whole can serve as a sensor and explore the radio wave transmission, reflection, and scattering to sense and better understand the physical world, providing a broad range of new services.
  Communication enhancement: The capabilities of high-accuracy localization, imaging, and environment reconstruction obtained from sensing could help improve the communication performance such as more accurate beamforming, faster beam failure recovery, and less overhead to track the channel state information (CSI).
As the process of industrial automation and digitalization has begun in 5G, the research of 5G ISAC is very meaningful for promoting 5G network to provide more intelligent services to consumer and industrial customers, at the same time, it can also make technical preparations for 6G ISAC design. So, it is proposed to start a study item of ISAC in Rel-18 to study the integrating sensing and communication on the existing 5G network.

## Slide 4: Use cases description (1)
  Typical use cases for ISAC:
    Use Case#1: Autonomous vehicles need real-time sensing for vehicle driving environment. With wireless sensing, it is easy to imagine that an autonomous driving car could work well or even better in all types of weather and light conditions.
    Use Case#2: UAV could be used as an air base station for various emergency scenarios, such as disaster rescue. Wireless sensing can provide all-weather service, increase UAV mobility and flexibility, help UAV cluster formation flight, hazard detection, collision avoidance and compliance with UAV regulations.
    Use Case#3: Real-time monitoring can be used in a smart home or intelligent factory to monitor the movement of robots or smart devices, it requires real-time sensing for the environment and the surroundings, with wireless sensing, more accuracy and timely sensing content can be provided.
1. Autonomous vehicles:
2. Unmanned Aerial Vehicle:
3. Real-time monitoring:

## Slide 5: Use cases description (2)
4. Ultra-high precision positioning:
5.Weather or air pollution monitoring:
  Typical use cases for ISAC:
    Use Case#4: Ultra-high precision positioning is very useful in many other use cases, such as autonomous driving, the wireless sensing can provide accurate position of the neighbor vehicles and the barriers, improve the safety of autonomous driving.
    Use Case#5: Weather or air pollution monitoring is meaningful for the agricultural industry and social governance, the wireless sensing can obtain environmental information such as temperature, humidity and air particle concentration with the transmission characteristics of radio signals. By analyzing attenuation characteristics of the millimeter wave, we can monitor rainfall or other changes in the atmospheric environment, such as water vapor, air pollutants and insects.

## Slide 6: Applications requiring enhancement on existing network
  ISAC provides performance gain in various aspects:
    Positioning performance: ISAC provides centimeter-level accuracy based on the reflected signals with high throughput communication simultaneously, whereas NR support the interactive positioning only.
    Recognition performance: tests showed that the imaging can reach the millimeter-level accuracy, and the heart/breath rate detection error less than 2 times per minute.
    Network enhancement: ISAC reduces 70% THz/mmWave beam misalignment probability in highway and urban cases.
Chart: 
| Rel 17 | Rel 18 | ISAC
ranging accuracy [m] | 1 | 0.5 | 0.2
Chart: 
| Rel 17 | Rel 18 | ISAC
angle accuracy [deg] | 10 | 8 | 5
Chart: 
| Rel 17 | Rel 18 | ISAC
velocity accuracy [m/s] | 0 | 0 | 0.2
 | Heart rate | breathe
frequency | 75/min | 20/min
error | 2.08 | 2

## Slide 7: Applications requiring capabilities beyond positioning
  Typical use cases require not only localization but also recognition capabilities:
    Enable recognition capability: A prominent feature of ISAC is the support of recognition capabilities, which is a new dimension of sensing distinguished from localization and is necessary for the aforementioned use cases. Therefore, the recognition capabilities which has not been supported in Rel-18 is a strong motivation for NR ISAC study.
Capability | Detail | Description | Typical Use case |  |  | Currently fulfill | ISAC fulfill
 |  |  | Autonomous vehicles | Smart home | Environment monitoring |  | 
Localization | Velocity | State of motion |  |  |  |  | 
 | Angle | Azimuth/elevation of target |  |  |  |  | 
 | Range | Distance from target |  |  |  |  | 
Recognition | Imaging(reconstruction) | Object or surroundings remodeling |  |  |  |  | 
 | Body shape identification | Human-computer interaction/Posture/gesture |  |  |  |  | 
 | Existence detection | Intrusion detection、electronic fence， etc. |  |  |  |  | 
 | Health monitoring | Heart rate/breathe/pulse/sleep/fitness record/counting |  |  |  |  | 
 | Environment(geoscience) | Temperature/humidity/sleet/air quality/weather prognosis/insect |  |  |  |  | 

## Slide 8: SA1 SID ongoing
3GPP SA has acknowledged that 5G-based sensing services can be beneficial for intelligent transportation, factories, enterprise and so on, while sensing-assisted communication can improve the performance with more accurate user location and channel environments. Hence, SA1 has started a SID “New SID on Integrated Sensing and Communication” to study the ISAC technic.
The objectives of the study include:
Study use cases and potential requirements for enhancement of the 5G system to provide integrated communication and sensing services addressing different target verticals/applications, e.g. autonomous/assisted driving, V2X, aviation/UAVs, 3D map reconstruction, smart city/factories, public sectors, healthcare, smart home, maritime sector.
Identify potential service requirements in the areas of:
  collection and reporting of the sensing information;
  exposure of the sensing capabilities and information to 3rd party.
Identify KPIs related to NR based sensing (e.g. range, motion, velocity) and performance requirements for transferring sensing related data.
Aspects related to security, privacy, regulatory requirements and charging.
Gap analysis between the identified potential requirements and existing 5GS requirements or functionalities.

## Slide 9: Why 3GPP needs to start work on ISAC in 5G-A
Observation：
  With ISAC, operators can quickly provide various sensing services for vertical industry or enterprise customers on their 5G networks, meanwhile the sensing ability can assist the network access and management, and improve communication performance and resource scheduling efficiency;
  Some requirements from industrial and V2X scenarios, such as speed measurement, distance and angle measurement etc., have not been supported in current 5G networks, while a lots of research and experiments have shown that ISAC can bring good performance on these aspects. With ISAC, operators can provide industry the new sensing services and accelerate the penetration of 5G system into the vertical industry;
  ISAC is a complex technic including new ISAC channel model, sensing modes, sensing signal design, and so on. If we could do some pre study and specify some initial sensing functions in 5G-A, on the one hand it can enhance 5G functionality, on the other hand it can accumulate standardized experience for the comprehensive integration of 6G sensing and communication.

## Slide 10: On the stepwise study on ISAC
The research on ISAC includes many aspects, such as use cases and related KPIs, Sensing Modes, ISAC Channel Model, Sensing signal design and so on. If we want to implement all sensing functions on 5G-A system once for all, the standardization work is too complex to be completed. We should consider gradually supporting ISAC on 5G-A, as follows:
  Phase 1: To select the sensing functions for evaluation and standardization with the existing 5G methodology and the simplified channel model.
  Phase 2: To evaluate and standardize more complex sensing functionalities which may require new channel model or new transmission wave design and so on.
Q4
December
2022
2023
2024
Q1
March
Q2
June
Q3
September
Q4
December
Q1
March
Q2
June
Q3
September
Q4
December
Identify scope of Phase 1 (SI)
Phase 1 WI
Channel model for Phase 2 SI
Phase 2 SI
Phase 1 SI(Sub group evaluation)

## Slide 11: Proposed objectives for the study of ISAC Phase 1
In Phase 1 of ISAC, the study targets at enabling some sensing functions in 5G without major changes to the existing 5G system. The potential objectives are as below:
Identify the suitable use cases and related requirements under which the sensing performance can be evaluated with the existing 5G methodology, at least the use cases/services agreed in SA1’s “New SID on Integrated Sensing and Communication” could be used as a baseline for discussion.
Formulate a set of sensing design targets based on the requirements from the identified use cases, at least including
  Accuracy of distance measurement
  Resolution of distance measurement
  Accuracy of angle measurement
  Resolution of angle measurement
  Accuracy of velocity measurement
  Positioning accuracy
NOTE: The study shall aim to provide better positioning accuracy compared to existing 3GPP positioning technologies for the relevant use cases.

## Slide 12: Proposed objectives for the study of ISAC Phase 1
Compare and assess the feasibility of meeting the design targets for identified use cases, and identify assumptions on required functionality to be supported.
  The feasibility study could start by evaluating the sensing performance targets(including distance, angle, velocity etc.) for the 5G-A system.
  The existing 5G-A methodology and simple channel models are assumed in the Phase 1 study.
  Distinguished from the positioning project, this feasibility study aims to identify the assumptions under which the existing 5G-A system could achieve the sensing performance targets in addition to positioning accuracy.
NOTE: Meeting the sensing design targets should not be at the cost of the obvious degradation of communication performance.
NOTE: The discussion could start in RAN level to confirm the Phases plan for the study of ISAC.

## Slide 13: Thanks！