## Slide 1: Motivation on AI/ML for NR air interface high layer
China Telecom
December 2022
3GPP TSG RAN #98-e
Electronic Meeting, December 12 – 16, 2022
Agenda: 9.1.2
RP-222954

## Slide 2: Background
AI/ML for NR air-interface study item focuses on the study of three typical physical layer use cases.
AI/ML used for radio resource management (RRM) has been drawn a lot of interests in recent academic research. In Rel-18 workshop, many AI/ML enabled high-layer use cases have been raised by companies.
Based on the current working progress, more use cases related with high layer may be initiated discussion to forward the AI/ML research on high layer use cases.

## Slide 3: Motivation
Three types of scenario (i.e., eMBB, URLLC, mMTC) have been defined in terms of new services and markets of 5G. Many new technologies and features, e.g., dynamic TDD, have been introduced to support diversified service requirements in the former releases.
However, although the standardization of key technical features provides high degree of flexibility and potential performance improvement, the complexity of traditional implementation methods to solve RRM problem of multi-dimensional optimization is too high, and it is difficult to obtain best solution. Therefore, these well-defined features are usually applied practically with some simplifications and restrictions, which leads to inefficient use of radio resources and degraded performance.
AI/ML is a powerful technology that can be used to solve extremely complex problems and is expected to realize RRM with more flexible, intelligent and efficient way.
Besides, the performance of AI/ML is more reliable on tremendous and high-quality wireless big data, more high layer enhancements should be considered to enable specific use cases and take care of data privacy.

## Slide 4: Use case 1: dynamic TDD
Background
  Dynamic TDD describes a mode of operation in which a network adapts the DL/UL subframe pattern according to traffic conditions.
  The transmission pattern depends on the following signalling combination:
    Cell-level RRC signalling, UE-level RRC signalling, UE group common PDCCH signalling (SFI), and UE-specific PDCCH signalling (UL grant or DL scheduling assignment)
  Former releases have made progresses and conclusions to deal with the technical barriers:
    Rel-16 WI cross link interference (CLI) handling to support flexible resource adaptation for unpaired NR cells has specified CLI measurements and reporting at a UE(i.e., CLI-RSSI and SRS-RSRP), and network coordination mechanism(s) (i.e., exchange of intended DL/UL configuration) in order to avoid co-channel CLI within the same network.
    According to conclusions about adjacent carrier leakage (ACL) in TR38.828, dynamic TDD can be used in indoors (indoor-2-indoor, indoor and macro) and certain micro (e.g., FR2) deployments as long as care is taken.

## Slide 5: Use case 1: dynamic TDD
Motivation
  There are strong demands for dynamic TDD in B5G specific scenarios
    Requirements of low latency, high data-rate and hot plugging in smart factory, automation control and other industry scenarios will lead to the requirement of adaptive subframe configurations.
    Smart Home, smart building and office have different service requirements at different time.
  Current 5G network configurations
    Usually adopt a fixed subframe configuration, which cannot meet the above scenarios’ requirements simultaneously.
  If we rely on manual configuration and optimization, it will lead to huge workloads and can not dynamically adapt to the requirement of service and network load as well as guarantee users’ QoS/QoE.

## Slide 6: Use case 1: dynamic TDD
Benefit and impact of AI/ML introduced
  AI/ML can be introduced to learn from the environment and service and help to generate flexible subframe configurations accordingly.
    AI/ML based subframe optimization with semi-static/dynamic configurations can be studied:
      At least AI/ML based semi-static configuration of cell-level RRC signalling and UE-level RRC signalling (UL/DL configuration dedicated message) can be considered.
      At least AI/ML based dynamic configuration with CLI management can be considered for UE group common PDCCH signalling. UE specific PDCCH signalling may be included or not.
  The existing CLI measurement reports and performance metrics can be reused or need enhancement for AI/ML life cycle management.
  AI/ML may be implemented based on a centralized or distributed architecture, for which L2/L3 enhancement may be required.
  Multi-TRP coordination will benefit flexible and dynamic subframe configurations as well as improve network operation efficiency.

## Slide 7: Use case 2: positioning
Motivation
  Ongoing evaluations of AI/ML based positioning enhancement demonstrate the remarkable performance compared with the traditional positioning method.
  In practice, high-quality labeled data samples are relatively small compared with the present evaluation assumptions.
  Data security and personal privacy are crucial
  issues with public concern.
  Further enhancement may be investigated
  on AI/ML based positioning enhancement.
Figure1 - Diverse applicable scenarios for AI/ML based positioning enhancement
Intelligent Factory
XR/Metaverse
Automatic Driving
Multi-TRP
coordination
Multi-carrier coordination
Multi-RAT coordination

## Slide 8: Use case 2: positioning
Benefit and impact of AI/ML introduced
  Study distributed/federal learning based positioning enhancement to satisfy data security and personal privacy requirements.
  Study data integrated based positioning enhancement, such as data integrated based on multi-TRP, multi-carrier and multi-RAT.
  Study potential Xn and F1 interface enhancements.

## Slide 9: Use case 2: positioning
Simulation results
  Observation 1: Federal learning based positioning enhancement can achieve faster convergence and better positioning accuracy.
  Observation2: The data integrated positioning enhancement may significantly improve the performance of AI/ML based positioning.
Figure2. performance with different dataset sizes
Figure1. performance of federal learning
(a)
(b)

## Slide 10: Use case 3: mobility management
Motivation
  Temporal beam prediction is studying as a sub-use case of AI/ML based beam management use case and is also helpful for improving mobility performance due to the UE trajectory prediction.
  Mobility enhancement specified at RAN3 is mainly focusing on AI/ML model deployed at Network-side.
  Therefore, further enhancements may be investigated to improve mobility performance of UE, especially for high-speed users.
Benefit and impact of AI/ML introduced
  AI/ML is expected to be used to make better HO decisions to reduce HOF rate, ping-pong HO rate and short time of stay rate.
  Model generalization should be investigated in terms of high-speed mobility.
  Besides, PC5-based coordination may be studied to improve model generalization and robustness.

## Slide 11: Use case 4: service awareness RRM
Background
  There are several service-oriented techniques supported in NR to satisfy the requirement of specific users.
  Several resource allocation management mechanisms have been identified to improve QoS, decrease power consumption etc.
Benefit and impact of AI/ML introduced
  RRM mechanisms, such as DRX, power control, link adaptation etc., are expected to be improved by introducing AI/ML.
  AI/ML can be used to process service awareness, interference management, user scheduling, as well as generate signalling and policy of UE or network.

## Slide 12: Proposal
Start initial discussion on AI/ML for NR air interface high layer use cases
  Identify AI/ML enabled high layer use cases.
  Study performance evaluation methodology of AI/ML enabled high layer use cases.
  Study specification impact of high layer use cases.

## Slide 13: Thanks！