## Slide 1: On open issues: Enhanced support of reduced capability NR devices
Nordic Semiconductor ASA
3GPP TSG RAN meeting #98e
Electronic Meeting
December 12 - 16, 2022 Agenda Item: 9.3.1.7
RP-222964

## Slide 2
Outline of contribution
Support of R17 RedCap UE with Peak throughput reduction in R18
Peak throughput target for R18 UE
Separate Early identification
Connectivity restrictions
RAN #97-e agreement
Check in RAN#98-e regarding:
Whether UE peak data rate reduction for UE is limited only with UE BB bandwidth reduction or standalone
Whether or not/how a separate early indication can be supported
Other restrictions of the WI (e.g., connectivity restrictions, band, etc.)

## Slide 3: Support of R17 RedCap UE with Peak reduction
RAN1 agreements for R18 Redcap UEs are the following:
  UL follows BW3, i.e transmission is confined within 5MHz
  DL broadcast follows R17 UE behavior
  DL unicast follows PR3, i.e. number of PRBs that gNB can schedule within 20MHz is restricted from 106/51 to 25/11
  Observation-1: RAN1 design based on PR1+PR3+BW3 allows for 10% complexity reduction from R17 to R18 RedCap UE
  Observation-2: Based on existing agreements, no additional capability is required to support PR1+PR3+BW3 at the UE side.
Proposal-1: R17 RedCap UE + PR1 is not supported in R18
  R18 RedCap + CAT1(bis) as fallback
    CAT1 bis and RedCap need to process the same amount (100 vs. 106) of PRBs and data (10MBits) per ms, however
      NR PDCCH processing timeline is 2x stricter than that of CAT1 PDCCH
      Frequency of interrupts in NR is higher compared to LTE due to significantly reduced processing timelines -> this creating processing overhead
  R18 RedCap + LTE-M1(M2) as fallback
    RedCap requirements are dominant
  Observation-3: PDSCH/PUSCH processing requirements of 20MHz NR (R17 Redcap UE + PR1) are higher than those of 20MHz LTE (CAT1) despite peak throughput being the same.
  Observation-4: “R17 Redcap UE + PR1” would bring further fragmentation to RedCap market, due to need of different scheduler than that of R18 RedCap UE

## Slide 4: Peak throughput target for R18 UE
Proposal-2: For FD R18 Redcap DL, consider to lower target peak rate from 10 to 6 Mbps
  One open issue is DL peak rate target, which has been agree in RAN1 as working assumption
  From Nordic point of view 6Mbps would be fully sufficient peak throughput for Industrial IoT
  The reduction in modem complexity from RAN1 point of view is insignificant.
  On the other hand, L2 buffer, IP buffers, etc. scale linearly with peak throughput, further peak reduction would have significant benefit on size and complexity of a module overall.
Agreement
UE peak data rate reduction is supported at least as an add-on to UE BB bandwidth reduction,
  The constraint vLayers·Qm·f ≥ 4 is relaxed to vLayers·Qm·f ≥ X.
  FFS: the value of X
If UE peak data rate reduction is supported as a standalone feature,
  The constraint vLayers·Qm·f ≥ 4 is relaxed to vLayers·Qm·f ≥ Y.
  FFS: the value of Y
  Note: Whether this option is supported will be decided in RAN plenary.
Agreement
The minimum DL peak rate target (for FD-FDD) is [10] Mbps based on peak data rate calculation according to 38.306.
The same value for X is used for DL and UL

## Slide 5: Support of Early identification
Proposal-3: MSG3 separate early identification is supported
Proposal-4: MSG1 separate early identification is strongly considered
  Separate Early identification
  MSG3 separate early identification is required for gNB to confine MSG4 to 25/12PRBs
  MSG1 separate early identification is not strictly needed, but it would tackle the following issues
    If X=0 -> performance degradation for MSG2 reception is expected
    If X>0 -> indicated K2 of MSG3 must be slightly increased for legacy UEs
Agreement
For UE BB bandwidth reduction, for RAR (PDSCH) to Rel-18 RedCap UEs, the scheduling of RAR PDSCH is allowed to be larger than the maximum number of unicast PRBs that the UE can process per slot.
When the scheduling of RAR PDSCH is within the maximum number of unicast PRBs that the UE can process per slot, the legacy time between RAR reception and Msg3 transmission (not smaller than NT,1 + NT,2 + 0.5 ms) is applied.
When the scheduling of RAR PDSCH is larger than the maximum number of unicast PRBs that the UE can process per slot,
  The UE receives the RAR and correspondingly transmits Msg3 if the TDRA for Msg3 in UL grant in RAR indicates that the time between RAR reception and Msg3 transmission is NOT smaller than NT,1 + NT,2 + 0.5 + X ms.
    FFS: value(s) of X
  Otherwise, the UE behavior is up to the UE implementation.
Note: it does not mean early indication is needed
Note: it will not be used as example for unicast PDSCH

## Slide 6: Connectivity restrictions
Proposal-5: Above yellow highlighted R17 RedCap restrictions apply also for R18 RedCap
  In RAN1#97, there has been some discussion on band support CA, EN-DC in RAN#97
  In our opinion, inheriting R17 RedCap restrictions (see on right) is a baseline for R18 RedCap.
Specify definition of one RedCap UE type including capabilities for RedCap UE identification and for constraining the use of those RedCap capabilities only for RedCap UEs, and preventing RedCap UEs from using capabilities not intended for RedCap UEs including at least carrier aggregation, dual connectivity and wider bandwidths. [RAN2, RAN1]
  The existing UE capability framework is used; changes to capability signalling are specified only if necessary.
……
This WI focuses on SA mode and single connectivity with operation in a single band at a time.