## Slide 1
RP-223004
3GPP TSG RAN Meeting #98e
Electronic Meeting, December 12 - 16, 2022
Source: Huawei
Title: Motivation for 5G-Advanced WI on Network energy savings for NR (phase 1)
Document for: Information
Agenda Item: 9.1.1

## Slide 2
BS energy consumption model
  Reference configuration for FR1 TDD/FDD and FR2
  Deep/light/micro sleep states with corresponding relative power, transition time and energy consumption based on two BS categories
  Scaling rules for active DL/UL power states considering BS power split into static part and dynamic part, with the latter further reflecting the dynamic power consumption with respect to transmission/reception resource configurations in time, frequency, spatial and power domains.
Evaluations
  The study is not only focusing on the energy saving gains, but also considering other KPI performance including UPT, UE power consumption, access delay and other KPIs (optionally)
    e.g., Energy efficiency(EE), coverage etc.
  The evaluation baseline includes at least NR R15 mandatory without capability features and others can be optionally reported
  SLS is considered as baseline evaluation method and others like LLS and numerical analysis can also be considered
Technical part
  Techniques in time/frequency domains aim to reduce power consumption for dynamic part by shutdown more symbols on one or more carriers for micro sleep, and even the static power part by enlarging the interval between contiguous active transmission/reception occasions for light sleep.
  Techniques in spatial/power domains aim to reduce power consumption of TRX chains and PAs by shutdown more spatial elements and/or reduce power spectrum density, or increase PA efficiency.
Rel-18 NES SI outcome
[1] R1-2213007 , 3GPP TR 38.864 V0.5.0, Study on network energy savings for NR.

## Slide 3
  Conclusion highlights
  Based on the study and summary, from time and frequency domain,
    Technique A-4 of adaptation of DTX/DRX, including the alignment of Cell DTX/DRX with UE DRX, is beneficial for network energy savings.
    Adaptation/reduction/elimination of common channels/signals (UE WUS can also be considered) in single or multi-carrier operation are beneficial for network energy savings.
  Based on the study, at least a technique based on C-1 is beneficial for network energy savings, and can be recommended. Technique C-2 also has the potential to provide large network energy saving gain.
  Based on the study, at least a technique based on D-1 is beneficial for network energy savings.
  It is recommended that the normative phase includes not only energy saving techniques (the necessary enhancements would need to be further identified during the normative phase) but also the mitigation of their impacts when network applies network energy savings technique(s).
  Other considerations
  Coverage impact is not shown however also critically important for common signals like SSB
  Compatibility with legacy UEs should be properly considered(e.g., bar legacy UEs if needed), however may not prevent solutions having large energy saving potential from being specified
    SID requirement of the following is fulfilled：legacy UEs should be able to continue accessing a network implementing Rel-18 network energy savings techniques, with the possible exception of techniques developed specifically for greenfield deployments.
  Views on detailed solutions (see slide in next page)
Rel-18 NES SI summary, and other considerations from Huawei
[1] R1-2213007 , 3GPP TR 38.864 V0.5.0, Study on network energy savings for NR.

## Slide 4
Summary of evaluated schemes and Huawei views
ES scheme | # of sources | Range of ES gain | Huawei view
technique A-1-1 of simplified SSB without PBCH or with partial PBCH | 3 | 0.7%~30.49% | Specification impact should be minimized, if recommended. No new channel.
technique A-1-2 of skipping one or more of SSB/SIB1 transmission | 2 | 0.3%~25.4% | Negative impact on SSB coverage
technique A-1-3 of adapting the periodicity of SSB | 9 | 0.9%~84.8% | UPT loss/latency increase significantly and negative impact on SSB coverage If recommended, main work is expected in RAN4
A-1-4 of adapting Paging or SSB transmission patterns | 1 for paging 1 for SSB | 0.2%~42.3% for Paging enhancement 10.3% for SSB enhancement, | For paging enhancement, May rely on long SSB periodicity and heavy paging load, with BS category 1 If recommended, it can be RAN2/RAN3 led
technique A-1-5 of adapting RACH periodicity/occasions | 1 | 14.4%~24.9% | Unclear on the rationale of the gain since the evaluations show the gain from static/longer RACH periodicity, which is possible today Latency increases significantly
technique A-1-6 of scheduling SIB1 by SSB | 1 | 4.8%~14.8% | 
A-3 of UE WUS triggering gNB | 6 | -2.4%~93% | Specification impact could be non-trivial Can be in combination of other techniques so useful in several scenarios, e.g. with on-demand SSB or SSB-less
A-4 of adaptation of UE DTX/DRX towards Cell DT/DRX | 6 | 0.2%~71.4% | If recommended, it can be RAN2 led
A-5-2 of on-demand SSB/SIB1 | 3 | 2.6%~43.4% | May be useful in combination of other techniques, e.g., as complementary of SSB/SIB-less for better sync/mobility
A-5-1/B-1-1 of SSB- and/or SIB1-less operation | 8 (5 for SSB-less only; 5 for SIB-less only; 4 for both SSB&SIB-less) | 0.3%~98.4% on the energy saving cell/carrier with -2.3%~ -18.9% on the associated cell/carrier | SSB-less: recommended, and main work is expected in RAN4 SIB1-less: recommended, and it is expected as RAN2 led
B-1-2 of UE-group PCell switching | 1 | 5.8%~37.5% | Group handover is not to be further considered in RAN2
B-2 of BWP adaptation of multiple UEs within a carrier | 1 | 17.4%~52.2% | Unclear whether UE specific BWP switching can already achieve the similar gain Unclear gain if compared to a baseline with a small BW for low or light load Meanwhile considerable UPT loss is observed
C-1 of adaptation of spatial elements | 12 | 0~48.2% | Recommended in WG already
C-2 of TRP muting in multi-TRP operation | 3 | 19.7%~41.6% | Possibly combined with technique C-1 However, limited gain if baseline is TRP shutdown with R17 MTRP scheme
D-1 of transmission power adaptation | 10 | 2.3%~51.5% | Multiple CSIs can facilitate gNB for dynamic power backoff with limited UPT loss
D-2 of over the air digital pre-distortion D-3 of channel aware tone reservation D-5 of UE post-distortion | 1 | 8.9% 2.1%~9.5% 16.1% | The gain is not promising and the useful scenario is unclear given that some settings are not reported, e.g. traffic load
[1] R1-2213007 , 3GPP TR 38.864 V0.5.0, Study on network energy savings for NR.

## Slide 5
  Core part
  Specify the following techniques in time and frequency domains
  Necessary procedures to reduce the transmission of common channels/signals
    SSB-less SCell operation for inter-band CA where a UE measures SSB transmitted on PCell or another SCell for an SCell’s time/frequency synchronization [RAN4-led]
    SIB1-less operation where a UE in either RRC_IDLE or RRC_INACTIVE obtains system information for a cell from another cell [RAN2-led]
    On-demand SSB/SIB1 transmission triggered by UE
    Simplified SSB without PBCH or with partial PBCH
    SSB transmission periodicity longer than 160 ms (up to 1280 ms) [RAN2-led]
    Note: No new UL channel/signal to be introduced
  enhancement on DTX/DRX mechanism and related procedures, including the alignment of Cell DTX/DRX with UE DRX, inter-node information exchange on Cell DTX/DRX [RAN2-led]
  Specify the following techniques in spatial and power domains
  Enhancements on CSI related procedures and signaling to enable efficient adaptation on spatial elements (e.g. number of active transceiver chains, number of active antenna panels, number of TRPs at gNB), including
    CSI resource and/or CSI report (re)configurations via L1/L2 signaling, for the adaption of spatial elements
    Multiple CSIs corresponding to different numbers of spatial elements in one CSI report
  Enhancements for adaptation of power offset values between PDSCH and CSI-RS
    L1 signaling for indication of power offset between PDSCH and CSI-RS
    Multiple CSIs corresponding to different power offset values between PDSCH and CSI-RS in one CSI report
Proposed Rel-18 NES WI objectives (1/2)

## Slide 6
  Mechanism(s) to prevent legacy UEs camping on cells adopting the above techniques, if necessary [RAN2]
  Specify, if necessary, inter-node beam activation and paging enhancements [RAN3]
  Specify the corresponding RRM/RF core requirements, if necessary, for the above features [RAN4]
  Performance part [RAN4]
  Specify corresponding RRM performance requirements and test cases for the network energy saving techniques
  Specify the necessary demodulation performance and CSI reporting requirements
  Specify the necessary BS conformance tests, if necessary
Proposed Rel-18 NES WI objectives (2/2)
R1 | R2 | R3 | R4RF | R4RD | RAN | R1 | R2 | R3 | R4RF | R4RD | R1 | R2 | R3 | R4RF | R4RD | RAN | R1 | R2 | R3 | R4RF | R4RD | RAN | R1 | R2 | R3 | R4RF | R4RD | R1 | R2 | R3 | R4RF | R4RD | RAN
112 | 121 | 119 | 106 | 106 | 99 Mar.23 | 112bis-e | 121bis | 119bis | 106bis | 106bis | 113 | 122 | 120 | 107 | 107 | 100 Jun.23 | 114 | 123 | 121 | 108 | 108 | 101 Sep.23 | 114bis | 123bis | 121bis | 108bis | 108bis | 115 | 124 | 122 | 109 | 109 | 102 Dec.23
1 | 1 | 0.5 |  |  |  | 2 | 1 | 0.5 | 0.25 | 0.25 | 2 | 1 | 0.5 | 0.5 | 0.5 |  | 2 | 1 | 0.5 | 0.5 | 0.5 |  |  | 1 | 0.5 | 0.5 | 0.5 |  | 1 | 0.5 | 0.5 | 0.5 | 

## Slide 7: Thank you !