## Slide 1: Agenda Item: 7（Liaison activities of TSG RAN） Source: OPPO Document for: Approval Title: Consideration on solutions for BWP operation without bandwidth restriction
3GPP TSG RAN Meeting #98-e RP-223030
Electronic Meeting, December 12-16, 2022

## Slide 2: Backgrounds
CSI-RS based RLM/BM/BFD is not supported in active BWP. So those L1 measurement can only relies on CD-SSB out of active BWP
Many UE vendors including OPPO argued that it can be resolved by CSI-RS based solution considering UE capability 1-7(CSI-RS based RLM) and FG 2-24 (SSB/CSI-RS for beam measurement) are all mandatory with capability signaling. Feature 1-31(Beam failure recovery) are mandatory with capability signaling for FR2 but optional for FR1. Some BS vendors confirmed actually the CSI-RS based solution is deployed in the field.
Since many companies are open for Rel18 solution, all solutions in RAN4’s LS R4-2214355 are kicked back to RAN4 to do high level analysis in last RAN#97 and come back to RAN#98 again based on assumption no RAN4 TU will be impacted.
RAN4 has done the high-level analysis in the two RAN4 meetings and reach agreements.

## Slide 3: RAN4 agreements in RAN4#104bis-e-meeting
In RAN4#104-bis-e meeting, RAN4 agreed to perform high-level analysis from the following 4 aspects/criteria on options for UE performing RLM/BFD/BM when CD-SSB is outside active BWP:
  RRM requirements impact (Spec impact) / workload in RAN4
  Mobility performance impact
  Throughput impact (Data interruption)
  UE power consumption / UE complexity

## Slide 4: RAN4 agreements in RAN4#105
RAN4 agreed to deprioritize some of the options. Solutions based on shared MG/NCSG or separate RF chain are precluded.
Candidate options
  Option A) Perform BM/RLM/BFD based on CSI-RS within active BWP
  Option B) Perform BM/RLM/BFD based on SSB outside active BWP
    Option B-1) UE’s capability not requiring additional measurement gap for BM/RLM/BFD
      Option B-1-1) Using larger BW covering SSB outside active BWP without interruptions
      Option B-1-2) Using larger BW covering SSB outside active BWP with interruptions
    Option B-2) BM/RLM/BFD on SSB outside BWP within measurement gaps
      Option B-2-2) Dedicated MG or NCSG for RLM/BFD/BM measurements
  Option C) NCD-SSB approach which would work with existing UE hardware architectures (FG6-1) and be compatible with existing RAN4 specifications for BM/RLM/BFD

## Slide 5: Highest-level analysis
Highest-level analysis on options:
Options | RRM requirements impact/workload in RAN4 | Power consumption | UE complexity | Mobility performance impact | Throughput impact (Data interruption)
Option A) | Low | Low | Low | Low | None
Option B-1-1) | Low | High | Low to medium | Low | None
Option B-1-2) | Low or Medium | Medium | Low to Medium | Low | Low to Medium
Option B-2-2) | NCSG: Low or Medium MG: Medium | Low | Medium | Low | NCSG: Low to Medium MG: Medium
Option C) | Low | Low | Low | Low | None
Note : “Low”/ “Medium” correspond to the low/medium negative impact

## Slide 6: Views on how to specify
About how to perform further down-selection in RAN-P
  Option A and C have the lowest impact to both RRM requirements and UE implementation based on RAN4’s common understanding.
  Compared to Option B-1-2 or B-2-2 with either interruptions or NCSG, option B-1-1 has less RRM requirements impact and similar UE complexity.
  OPPO prefers the following prioritization order if RAN was to further down-select
      Option A/C ＞ option B-1-1 ＞ option B-1-2/B-2-2
  About where to handle the enhancements of BWP operation without restriction
    Considering the progress in R18 eFeRRM is going quite well and RRM requirements impact is not big, we suggest to specify this issue under the umbrella of WI eFeRRM.
    Revised WID for eFeRRM can be approved based on the conclusion in RAN#98，and related work can be started in Feb. RAN4#106 if agreed.

## Slide 7: Reference
[1] RP-222630 Moderator's summary for discussion [97e-05-BWP-WithoutRestriction], Vodafone
[2] R4-2220437, LS on BWP operation without bandwidth restriction, vivo