## Slide 1: Discussion on representative sub-use case for AI/ML in NR air interface
Xiaomi
3GPP RAN #98-e
December 12-16, 2022
Electronic Meeting
Agenda Item: 9.2.8
RP-223090

## Slide 2: Background
In RAN#94 RAN plenary meeting, the SI on Artificial Intelligence (AI)/Machine Learning (ML) for NR Air Interface was approved
One checkpoint is to finalize the representative sub use cases:
    Initial set of use cases includes:
      CSI feedback enhancement, e.g., overhead reduction, improved accuracy, prediction [RAN1]
      Beam management, e.g., beam prediction in time, and/or spatial domain for overhead and latency reduction, beam selection accuracy improvement [RAN1]
      Positioning accuracy enhancements for different scenarios including, e.g., those with heavy NLOS conditions [RAN1]
    Finalize representative sub use cases for each use case for characterization and baseline performance evaluations by RAN#98
      The AI/ML approaches for the selected sub use cases need to be diverse enough to support various requirements on the gNB-UE collaboration levels

## Slide 3: CSI feedback – Sub-use case in RAN1
The following two agreements on representative sub-use cases were achieved in RAN1

## Slide 4: CSI feedback – Evaluation for CSI compression
Agreements on evaluation of AI/ML based CSI compression
Fig.1 Transformer based AI model
 | Spectrum efficiency
Ideal CSI feedback | 5.052 (100%)
eType II codebook | 4.315 (-15%)
AI CSI compression | 4.802 (-5%)
 | Testing Dataset | 
Training Dataset | UMa | UMi
UMa | SGCS = 0.70 | SGCS = 0.66
UMi | SGCS = 0.69 | SGCS = 0.71
Mixed | SGCS = 0.71 | SGCS = 0.70
Table 2, AI model generalization evaluation
Table 1, System level performance evaluation
Evaluation results of AI/ML based CSI compression.
  A Transformed based two sided AI CSI compression is used in the evaluation.
  In Table 1, the SLS performance result shows that AI/ML based CSI compression can improve the spectrum efficiency, the performance gain is around 10% compared with eType II codebook.
  In Table 2, the SGCS results shows that AI/ML based CSI compression has good generalization performance among different scenarios.
Agreement
For the performance evaluation of the AI/ML based CSI feedback enhancement, system level simulation approach is adopted as baseline
Agreement
For the evaluation of the AI/ML based CSI feedback enhancement, as a starting point, take the intermediate KPIs of GCS/SGCS and/or NMSE as part of the ‘Evaluation Metric’ to evaluate the accuracy of the AI/ML output CSI

## Slide 5: CSI feedback – Collaboration level
The following agreement and conclusion on CSI compression using two-sided AI/ML model training collaboration were achieved in RAN1. Our views on the relationship between training type and collaboration level are given in Table 1.
AI/ML training type | Potential Collaboration level
Type 1 | Collaboration level z or level y
Type 2 | Collaboration level y
Type 3 | Collaboration level y
Table 1: The relationship between training type
And collaboration level

## Slide 6: CSI feedback – Potential specification impact
The following potential specification impact on CSI compression using two-sided AI/ML model have been discussed and agreed for study:
  Model output type/dimension/configuration and potential post processing
  AI/ML model monitoring, e.g., UE-side or NW-side performance monitoring
  CSI reporting, e.g., CSI generation model output and/or CSI reconstruction model input，CQI, RI.
  The assistance signaling UE’s or NW’s data collection or delivery of the datasets
  Quantization/dequantization method and feedback message size between UE and NW

## Slide 7: CSI feedback – Feasibility
CSI compression using two-sided AI/ML model as a representative sub-use case is feasible due to following reasons:
  Reason 1: In massive MIMO systems, it is feasible CSI can be efficiently compressed in spatial-frequency domain by using the channel correlation of spatial-frequency domain.
  Reason 2: Training data can be obtained at UE or NW side according to the downlink, uplink reference signal(e.g., CSI-RS, SRS) or assistance information transmission between UE and NW side, such that UE and NW can jointly or separately train two-side AI/ML model.
  Reason3: Complexity of AI/ML model inference is less than that of legacy Type II codebook which requires a lot of singular value decomposition of channel matrix.
  Reason4: Significant performance gain is obtained compared with legacy Rel-16 Type II codebook.

## Slide 8: CSI feedback – Time domain CSI prediction
  The following concerns on time domain CSI prediction using one-sided AI/ML model as a representative sub-use case need to be considered:
  Workload: Both specification impact and simulation evaluation should be studied for time domain CSI prediction, which may make the workload be unaffordable due to limited TU in Rel-18 SI on AI/ML.
  Performance baseline: The performance baseline should be Rel-18 MIMO CSI using time domain CSI prediction. However, the work item on Rel-18 MIMO CSI has not been finished.
  Collaboration level: Time domain CSI prediction is sub-use case using one-sided AI/ML model which has been used by other sub-use case, e.g., time domain/ spatial domain beam prediction, or positioning. Since time domain/spatial domain beam prediction has been selected as a sub-use case in RAN1. It is not necessary to study the use case using one-sided model for CSI feedback from specification impact perspective.

## Slide 9: CSI feedback – Conclusion
Based on above observations and analyses, the following proposals on representative sub-use case for AI/ML based CSI feedback are given.
  Proposal 1: Spatial-frequency domain CSI compression using a two-sided AI/ML model is selected as a representative sub use case in Rel-18 SI on AI/ML.
  Proposal 2: Time domain CSI prediction should be studied with low priority in Rel-18 SI on AI/ML.

## Slide 10: Beam management- Sub use cases for study
RAN1-109’s Agreement
For AI/ML-based beam management, support BM-Case1 and BM-Case2 for characterization and baseline performance evaluations
BM-Case1: Spatial-domain DL beam prediction for Set A of beams based on measurement results of Set B of beams
BM-Case2: Temporal DL beam prediction for Set A of beams based on the historic measurement results of Set B of beams
FFS: details of BM-Case1 and BM-Case2
FFS: other sub use cases
Note: For BM-Case1 and BM-Case2, Beams in Set A and Set B can be in the same Frequency Range
RAN1-110b’s Conclusion
For AI/ML based beam management, RAN1 has no consensus to support on studying any other sub use case in addition to BM-Case1 and BM-Case2
Note: this conclusion is independent of the discussion on the alternatives of AI/ML model inputs for BM-Case1 and BM-Case2

## Slide 11: Beam management- Performance for BM-case1
Assumptions | Number of beam pairs in Set A |  | 256 |  | 
 | Number of beam pairs in Set B |  | 64 |  | 
 | Baseline scheme |  | Option1: exhaustive beam sweeping |  | 
AI/ML model input/output | Model input |  | Scheme 1: L1-RSRP and beam pair ID |  | 
 |  |  | Scheme 2: L1-RSRP |  | 
 | Model output |  | L1-RSRP of all beam pairs |  | 
Data Size | Training |  | 47500 |  | 
 | Testing |  | 2500 |  | 
AI/ML model | Short model description |  | Fully Connected Neural Network |  | 
 | Model complexity |  | number of model parameters: 558848 |  | 
 |  |  | size (e.g. Mbyte): 6.44 |  | 
 | Computational complexity |  | FLOPs: 0.557 M |  | 
 |  |  | Baseline | Scheme 1 | Scheme 2
Evaluation results With AI/ML/baseline | Beam prediction accuracy (%) | Top 1 (%) | 100 | 61 | 80
 |  | Top-2/1 (%) |  | 72 | 87
 |  | Top-4/1 (%) |  | 91 | 98
 |  | Top 1 (%) with 1 dB margin |  | 69 | 91
 | L1-RSRP Diff | Average ideal L1-RSRP diff (dB) | 0 | 1.3 | 0.2
 |  | Average diff between ideal L1-RSRP and predicted L1-RSRP when Top 1 predicted beam is same as Top 1 genie-aided beam (dB) |  | 2.3 | 0.4
 | System performance | RS overhead Reduction (%): Option 1 | 0 | 75% | 
Note: UE side model is assumed AI scheme Scheme 1: Variable set B with 64 beam pairs, with L1-RSRP and beam pair ID as input Scheme 2: Fixed set B with 64 beam pairs, with L1-RSRP as input |  |  |  |  | 
Table 1. Evaluation results for BM-Case1 without model generalization for Tx-Rx beam pair prediction
Observation: Scheme 2 can provide 98% beam prediction accuracy and Scheme 1 can provide 91% beam prediction accuracy with Top-4 predicted beams based on only 25% RS overhead of exhaustive beam sweeping.

## Slide 12
Figure 1, Scheme 1 of AI based beam prediction for BM case 2
Figure 2, Scheme 2 of AI based beam prediction for BM case 2
Beam management- Performance for BM-case2 (1/2)
Sub-use case in BM Case2
  Scheme 1:the periodicity of latest measurement instances is same as that of future time instances. And the beam results of future time instance can’t be considered as AI/ML model input.
  Scheme 2: the periodicity of latest measurement instances is L times of the periodicity of future time instances. And the beam results of the long periodicity can be considered as AI/ML model input which means a sliding window can be provided by this use case.

## Slide 13
Table 2. Evaluation results for BM-Case2 without model generalization for Tx-Rx beam pair prediction
Assumptions | Number of beam pairs in Set A |  | 256 |  | 
 | Number of beam pairs in Set B |  | 256 |  | 
 | Number of measurement instance |  | 4 |  | 
 | Number of future time instance (M) |  | 1 |  | 
 | Periodicity of future instance |  | 80ms |  | 
 | Periodicity of measurement instance |  | Scheme 1: 80ms |  | 
 |  |  | Scheme 2: 80ms*(number of future instance+1) |  | 
 | Baseline scheme |  | Option 1a: exhaustive beam sweeping |  | 
AI/ML model input/output | Model input |  | L1-RSRP |  | 
 | Model output |  | Top-K beam/beam pair ID |  | 
Data Size | Training |  | 95000 |  | 
 | Testing |  | 5000 |  | 
AI/ML model | [Short model description] |  | Long-Short Term Memory |  | 
 | Model complexity |  | number of model parameters: 248608 |  | 
 |  |  | size (e.g. Mbyte): 2.88 |  | 
 | Computational complexity |  | FLOPs: 0.412 M |  | 
 |  |  | Baseline | Scheme 1 | Scheme 2
Evaluation results With AI/ML / baseline | [Beam prediction accuracy (%)] | Top 1 (%) | 100 | 93 | 90
 |  | Top-2/1 (%) |  | 96 | 92
 |  | Top-4/1 (%) |  | 98 | 94
 |  | Top 1 (%) with 1 dB margin |  | 99 | 98
 | L1-RSRP Diff | Average ideal L1-RSRP diff | 0 | 0.06 | 0.10
 | System performance | RS overhead Reduction (%) | 0 | 20% | 50%
Note: UE side model is assumed AI scheme Scheme 1: the periodicity of latest measurement instances is same as that of future time instances Scheme 2: the periodicity of latest measurement instances = (the number of future time instance+1) * the periodicity of future time instances |  |  |  |  | 
Beam management- Performance for BM-case2 (2/2)
Observation: Scheme 1 can provide 98% beam prediction accuracy based on 80% RS overhead of exhaustive beam sweeping, and Scheme 2 can provide 94% beam prediction accuracy based on 50% RS overhead of exhaustive beam sweeping with Top-4 predicted beams.

## Slide 14
RAN1-109’s Agreement
Take the following network-UE collaboration levels as one aspect for defining collaboration levels
Level x: No collaboration
Level y: Signaling-based collaboration without model transfer
Level z: Signaling-based collaboration with model transfer
RAN1-110b
Working Assumption
Define Level y-z boundary based on whether model delivery is transparent to 3gpp signalling over the air interface or not.
Note: other procedures than model transfer/delivery are decoupled with collaboration level y-z
Clarifying note: Level y includes cases without model delivery.
Agreement
Clarify Level x/y boundary as:
Level x is implementation-based AI/ML operation without any dedicated AI/ML-specific enhancement (e.g., LCM related signalling, RS) collaboration between network and UE. (Note: The AI/ML operation may rely on future specification not related to AI/ML collaboration. The AI/ML approaches can be used as baseline for performance evaluation for future releases.)
RAN1-111’s Agreement
For the sub use case BM-Case1 and BM-Case2, at least support Alt.1 and Alt.2 for AI/ML model training and inference for further study:
Alt.1. AI/ML model training and inference at NW side
Alt.2. AI/ML model training and inference at UE side
The discussion on Alt.3 for BM-Case1 and BM-Case2 is dependent on the conclusion/agreement of Agenda item 9.2.1 of RAN1 and/or RAN2 on whether to support model transfer for UE-side AI/ML model or not
  Alt.3. AI/ML model training at NW side, AI/ML model inference at UE side
Beam management- Potential collaboration level
Alt 1
Alt 2
Alt 3
Level x
Level y
Level z
Potential collaboration level

## Slide 15
RAN1-111’s Agreement
For the sub use case BM-Case1 and BM-Case2, at least support Alt.1 and Alt.2 for AI/ML model training and inference for further study:
Alt.1. AI/ML model training and inference at NW side
Alt.2. AI/ML model training and inference at UE side
The discussion on Alt.3 for BM-Case1 and BM-Case2 is dependent on the conclusion/agreement of Agenda item 9.2.1 of RAN1 and/or RAN2 on whether to support model transfer for UE-side AI/ML model or not
  Alt.3. AI/ML model training at NW side, AI/ML model inference at UE side
Beam management- Feasibility
Feasibility
  Alt.1: For AI/ML model training and inference at NW side, it is feasible for NW side to collect data for model training and inference with some enhancement.
  Alt.2: For AI/ML model training and inference at UE side,
    It is feasible for UE to collect data for model training and inference even without any enhancement, i.e., transparent to NW side. But there will be no spec impact and no RS overhead reduction.
    In order for RS overhead reduction, it is also feasible to support at least some enhancement on new procedure and signaling is needed to indicate AI/ML model is activated at UE side.
  Alt.3: Based on the model training at NW side, the model can be delivered to UE side for inference with some enhancement on model transfer.

## Slide 16: Beam management- Potential spec impact
Model training
  Signaling/configuration/measurement/report for data collection, e.g., signaling aspects related to assistance information (if supported), Reference signals
  Content/type of the collected data
  Other aspect(s) is not precluded
Model inference
  Enhanced or new configurations/UE reporting/UE measurement, e.g., Enhanced or new beam measurement and/or beam reporting
  Enhanced or new signaling for measurement configuration/triggering
  Signaling of assistance information (if applicable)
  Other aspect(s) is not precluded
Model monitoring
  Performance metric(s)
  Benchmark/reference for the performance comparison
  Signaling/configuration/measurement/report for model monitoring, e.g., signaling aspects related to assistance information (if supported), Reference signals
  Other aspect(s) is not precluded

## Slide 17
Beam management- Conclusion
Proposal: For AI/ML-based beam management, support BM-Case1 and BM-Case2 as representative sub use cases
  BM-Case1: Spatial-domain DL beam prediction for Set A of beams based on measurement results of Set B of beams
    Consider Set B is a subset of Set A with high priority.
  BM-Case2: Temporal DL beam prediction for Set A of beams based on the historic measurement results of Set B of beams

## Slide 18: AI-based positioning—Situation in RAN1
For AI-based positioning, both the direct AI/ML positioning and assisted positioning were extensively studied in RAN 1. And t he following agreements have been reached on the study of the sub use cases
Agreement(RAN1#110)
For characterization and performance evaluations of AI/ML based positioning accuracy enhancement, the following two AI/ML based positioning methods are selected.
Direct AI/ML positioning
AI/ML assisted positioning
Note 1: the selection does not intend to provide any indication of the prospects of any future normative project.
Note 2: further discussion (including selection of other sub use cases and/or down selection of selected sub use cases) are not precluded based on performance evaluation and potential specification impact study results
Agreement(RAN1#111)
For AI/ML based positioning accuracy enhancement, direct AI/ML positioning and AI/ML assisted positioning are selected as representative sub-use cases.

## Slide 19: AI-based positioning—Performance gain
Performance gain
  Observation : both direct AI/ML positioning and AI/ML assisted positioning can improve the positioning accuracy significantly compared to existing RAT-dependent positioning methods
Observation （RAN1#111）
Direct AI/ML positioning can significantly improve the positioning accuracy compared to existing RAT-dependent positioning methods when the generalization aspects are not considered.
For InF-DH with clutter parameter setting {60%, 6m, 2m}, evaluation results submitted to RAN1#111 indicate that the direct AI/ML positioning can achieve horizontal positioning accuracy of <1m at CDF=90%, as compared to >15m for conventional positioning method.
Observation （RAN1 #111）
AI/ML assisted positioning can significantly improve the positioning accuracy compared to existing RAT-dependent positioning methods when the generalization aspects are not considered.
For InF-DH with clutter parameter setting {40%, 2m, 2m}, evaluation results submitted to RAN1#111 indicate that the AI/ML assisted positioning can achieve horizontal positioning accuracy of <0.4m at CDF=90%, as compared to >9m for conventional positioning method.
For InF-DH with clutter parameter setting {60%, 6m, 2m}, evaluation results submitted to RAN1#111 indicate that the AI/ML assisted positioning can achieve horizontal positioning accuracy of <1m at CDF=90%, as compared to >15m for conventional positioning method.

## Slide 20: AI-based positioning—Collaboration level
Both direct AI/ML positioning and AI/ML assisted positioning could support various collaboration levels for different cases
 | AI model is trained by network | AI model is trained by UE or UE’s external server
Case 1 UE-based positioning with UE-side model, direct AI/ML or AI/ML assisted positioning | Level y or Level z | Level x or Level y
Case 2a UE-assisted/LMF-based positioning with UE-side model, AI/ML assisted positioning | Level y or Level z | Level x or Level y
Case 2b UE-assisted/LMF-based positioning with LMF-side model, direct AI/ML positioning | Level x or Level y | --
Case 3a NG-RAN node assisted positioning with gNB-side model, AI/ML assisted positioning | Level x or Level y | --
Case 3b NG-RAN node assisted positioning with LMF-side model, direct AI/ML positioning | Level x or Level y | --

## Slide 21: AI-based positioning-Feasibility(1/2)
Data collection can be performed by existing network entities with existing or enhanced procedure according to achieved agreement in RAN1
Agreement in RAN1#111
Regarding data collection for AI/ML model training for AI/ML based positioning,
The following options of entity and mechanisms to generate ground truth label are identified for further study
  For direct AI/ML positioning, ground truth label is UE location
    PRU with known location
    UE generates location based on non-NR and/or NR RAT-dependent positioning methods
    LMF generates UE location based on positioning methods
    LMF with known PRU location
    Note: user data privacy needs to be preserved
  For AI/ML assisted positioning, ground truth label is one or more of the intermediate parameter(s) corresponding to AI/ML model output
    PRU generates label directly or calculates based on measurement/location
    UE generates label directly or calculates based on measurement/location
    Network entity generates label directly or calculates based on measurement/location
The following options of entity to generate other training data at least measurement corresponding to model input are identified for further study
  For UE-based with UE-side model (Case 1) and UE-assisted positioning with UE-side (Case 2a) or LMF-side model (Case 2b)
    PRU
    UE
  For NG-RAN node assisted positioning with Network-side model (Case 3a and Case 3b)
    TRP
  Note: other options of entity to generate other training data are not precluded
Note: Existing PRU definition is in 38.305

## Slide 22: AI-based positioning-Feasibility(2/2)
3 Approaches are possible for the model training and inference
  Approach 1: AI model is trained and inferenced on the network side
  Approach 2: AI model is trained on the UE side (or on UE’s external server) and the inference is on the UE side as well
  Approach 3: AI model is trained on the network side and delivered to UE side for inference
For other LCM aspects, no critical issue is identified on the feasibility

## Slide 23: AI-based positioning-Potential specification impact
Data collection
  Request / report of the data collection
  Assistance signaling/ procedure
Model inference
  Potential new or enhanced measurement report
  Assistance signaling
Performance monitoring
  Definition of the monitoring metric
  Potential assisted data/ signaling
Other LCM aspects (e.g., model identification , model switch/fallback, model delivery/transfer )
  May reuse the general solution defined in AI framework

## Slide 24: AI-based positioning-Conclusion
Summary of direct AI/ML positioning and AI/ML assisted positioning
  Significant performance gain
  Variable collaboration level
  Feasibility in the real deployment
  Reasonable specification impact
Proposal: Confirm the RAN1’s agreement on the representative sub use case
  For AI/ML based positioning accuracy enhancement, direct AI/ML positioning and AI/ML assisted positioning are selected as representative sub-use cases

## Slide 25: Summary of the proposals
AI-based CSI feedback enhancement
  Spatial-frequency domain CSI compression using a two-sided AI/ML model is selected as a representative sub use case in Rel-18 SI on AI/ML.
  Time domain CSI prediction should be studied with low priority in Rel-18 SI on AI/ML.
AI-based beam management : support BM-Case1 and BM-Case2 as representative sub use cases
  BM-Case1: Spatial-domain DL beam prediction for Set A of beams based on measurement results of Set B of beams
    Consider Set B is a subset of Set A with high priority.
  BM-Case2: Temporal DL beam prediction for Set A of beams based on the historic measurement results of Set B of beams
AI-based positioning
  For AI/ML based positioning accuracy enhancement, direct AI/ML positioning and AI/ML assisted positioning are selected as representative sub-use cases

## Slide 26: Thanks