## Slide 1
3GPP TSG RAN Meeting #98-e RP-223099
Electronic Meeting, December 12-16, 2022
Source: vivo
Document for: Discussion & Decision
Agenda Item: 9.3.2.1
Discussion on Rel-18 XR WI scope

## Slide 2
  Background – SI progress in RAN1 and RAN2
  Project management
  WID objectives on
    Power saving
    Capacity enhancement
    Coordination with SA2
Contents

## Slide 3
Background
SI progress in RAN1 and RAN2
SI progress in RAN1:
SI progress in RAN2:
It could be observed that the objectives on power saving and capacity enhancement could be considered as completed in WGs, while the objective on XR awareness has not been completed in WG.
From RAN1 perspective, the Rel-18 XR study item in RAN1 is completed.
Majority of companies in RAN2 thinks the objective on XR awareness is not complete because of SA2 progress. Further discussion on how to handle RAN2 impacts of SA2 and SA4 decisions would be necessary (e.g. PDU set handling in AS). RAN2 thinks the objectives on power saving and capacity enhancement are completed.

## Slide 4
The study on XR-awareness in RAN2 was not completed, so RAN2 should continue the study on XR-awareness in next quarter:
  RAN2 TU reserved for XR WI (2TUs) could be used for this continue study.
  Limited scope only on XR awareness for the continue study in RAN2 in Q1 2023.
  Detailed objective on XR-awareness will be further refined in RAN#99 after RAN2 concluded the study on XR-awareness.
Given the study on XR-awareness in RAN2 was not completed, the following alternatives for Rel-18 XR WI/SI management can be considered:
  Alt-1: Allow one more quarter for RAN2 to complete the XR awareness study, WI does not start until March, 2023
    However, the potential WI objectives for power saving and capacity enhancements can be endorsed in RAN#98e.
    The already reserved RAN1 for XR WI may have to be reallocated to other WIs/SIs.
  Alt-2: Allow one more quarter for RAN2 to complete the XR awareness study, WI starts from 2023Q1 focus on objectives for power saving and capacity enhancements (slightly preferred)
    The WI objectives on XR awareness can be added in March, 2023 based on the outcome of study in RAN2.
    The already reserved RAN1 and RAN2 TU for XR WI can be kept.
Project management

## Slide 5
Progress in RAN1:
Conclusions in RAN2:
It could be observed that following objectives on power saving could be considered during WI phase:
  Specify mechanism for the non-integer DRX periodicity
  Specify the mechanism to switch between DRX configurations at least based on RRC pre-configuration
  Specify mechanism on PDCCH monitoring resume if UE transmits NACK after PDCCH skipping starts
No recommended techniques in RAN1. During SI in RAN1, following enhancement for PDCCH monitoring adaptation was proposed and intensively discussed: Proposal 3.1: Support PDCCH monitoring resume if UE transmits NACK after PDCCH skipping starts More details please see our contribution in [RP-223098]
At least RRC pre-configuration and switching of configurations of DRX could be considered for enhancements of XR power saving. Other solutions are not precluded and can be further discussed. RAN2 aims to allow XR frame rates that correspond to non-integer periodicities in at least semi-static manner (e.g. RRC). Details can be left to WI phase.
Power saving progress and conclusion

## Slide 6
Conclusions in RAN1:
Conclusions in RAN2:
It could be observed that following objectives on capacity enhancements could be considered during WI phase:
  Specify mechanism on multiple CG PUSCH transmission occasions in a period of a single CG PUSCH configuration.
  Specify mechanism on dynamic indication of unused CG PUSCH occasion(s) based on UCI (e.g., CG-UCI or a new UCI) by the UE.
  Introduce new BSR table(s) reduce the quantization errors (e.g. for high bit rates).
  Introduce additional BSR triggering conditions to allow timely availability of buffer status information at gNB.
  Specify the mechanism to introduce data volume information associated with delay information (e.g. remaining time) in a MAC CE Specify assistance information on UL XR traffic to network for efficient scheduling or configuration.
  Specify timer based PDCP discard per PDU set basis for UE transmitter.
  Specify PDCP discard based on the integrity of a PDU set for UE transmitter.
The following enhancements for configured grant based transmission are recommended: Multiple CG PUSCH transmission occasions in a period of a single CG PUSCH configuration; Dynamic indication of unused CG PUSCH occasion(s) based on UCI (e.g., CG-UCI or a new UCI) by the UE.
RAN2 thinks we need one or more additional BSR table(s) for XR. FFS whether these are static (=specified) or dynamic (e.g. generated, differs according to some RRC parameter), can be discussed in WI phase. RAN2 will introduce data volume information associated with delay information (e.g. remaining time) in a MAC CE. FFS if this is extension of BSR or new format. FFS how to do that (e.g. what exactly is reported) and how to ensure this information is up-to-date e.g. considering UL scheduling delay. RAN2 needs to discuss additional BSR triggering conditions to allow timely availability of buffer status information at gNB. This can be discussed in WI phase. RAN2 agrees some assistance information can be beneficial (e.g. periodicity, packet size). RAN2 assumes baseline could be TSCAI (pending SA2 conclusions), can discuss during WI phase whether something additional is needed on top of that. If any assistance information is needed, its definition should be standardized. For UE transmitter, the PDCP discard should be performed per PDU set basis. For UE transmitter, the PDCP discard is managed per SDU for PDU set, the PDCP entity discards all PDCP SDUs associated with the PDU set. RAN2 to support timer-based discarding of UL transmit side of PDCP PDU/SDUs of a PDU set. FFS how this is modelled in PDCP specification, can be discussed in WI phase.
Capacity enhancement conclusion

## Slide 7
In RAN2#120 and RAN3#118 meeting, network exposure of per QoS flow/per DRB congestion information in both DL and UL has been discussed. Both RAN2 and RAN3 confirm that:
  It is feasible for RAN to estimate the congestion information per-QoS flow and per-DRB in downlink and uplink directions.
  It is feasible for RAN to estimate the congestion information per-QoS flow and per-DRB in uplink without UE impacts.
In our understanding, the discussion on network exposure in SA2 would need some inputs from RAN side.
Thus, RAN2 and/or RAN3 should discuss/specify corresponding signaling (e.g. via NG or X2 interface), subject to SA2 progress and requirement e.g. per-QoS flow/per-DRB congestion information.
Coordination with SA2 aspects:

## Slide 8
Conclusions
WID objectives – on PowSav and Capacity enh.
Objectives on XR-specific Power Saving [RAN1, RAN2]:
Specify mechanism on DRX enhancements to address the issues of DRX cycle mismatch [RAN2, RAN1]:
  Specify mechanism for the non-integer DRX periodicity;
  Specify the mechanism to switch between DRX configurations at least based on RRC pre-configuration.
Specify the following enhancements for PDCCH monitoring adaptation for power saving [RAN1]:
  Specify mechanism on PDCCH monitoring resume if UE transmits NACK after PDCCH skipping starts.
To specify RRM core requirements for the power saving objectives, as necessary [RAN4].
Coordination with SA2:
Specify corresponding signaling (e.g. via NG or X2 interface), subject to SA2 progress and requirement e.g. per-QoS flow/per-DRB congestion information. [RAN3, RAN2, including coordination and alignment SA2 as required].
Objectives on XR-specific capacity improvements [RAN1, RAN2]:
Specify CG enhancements for capacity improvement [RAN1, RAN2]
  Specify mechanism on multiple CG PUSCH transmission occasions in a period of a single CG PUSCH configuration;
  Specify mechanism on dynamic indication of unused CG PUSCH occasion(s) based on UCI (e.g., CG-UCI or a new UCI) by the UE.
Specify BSR enhancements for capacity improvement [RAN2]:
  Introduce new BSR table(s) reduce the quantization errors (e.g. for high bit rates);
  Introduce additional BSR triggering conditions to allow timely availability of buffer status information at gNB.
Specify the mechanism to introduce data volume information associated with delay information (e.g. remaining time) in a MAC CE [RAN2].
Specify assistance information on UL XR traffic to network for efficient scheduling or configuration [RAN2].
Specify PDU(s)/PDU set(s) discard, including [RAN2]:
  Specify timer based PDCP discard per PDU set basis for UE transmitter.
  Specify PDCP discard based on the integrity of a PDU set for UE transmitter.
To specify RRM core requirements for the capacity improvements, as necessary [RAN4].