## Slide 1
3GPP TSG RAN Meeting #98-e RP-223105
Electronic Meeting, December 12-16, 2022
Source: vivo
Document for: Discussion & Decision
Agenda Item: 9.3.2.3
Discussion on R18 MUSIM WID

## Slide 2: TU relocation requirement
Current TU for R18 MUSIM
There is not RAN2 TU in Feb, it is hard for RAN2 to get the achievement whether the WI will have RAN4 and RAN3 impact for UE capability restriction topic if there is no online RAN2 discussion, i.e. only by email discussion.
  Proposal 1: Move 0.5 RAN2 TU from Apr. 2023 to Feb. 2023.
Identify the RAN4 and RAN3 impacts in RAN#99
One post-email was allocated to identify RAN4 or RAN3 impact

## Slide 3: Clarify the R17 MUSIM gap supporting in R18 MUSIM
MN-SN coordination for R17 MUSIM gap is left to NW implementation in R17 phase. There are some interest among companies to specify MN-SN coordination for R17 MUSIM gap in R18 WI since this can save more SN resources. The agreement on R17 MUSIM gap coordination for MR-DC case in RAN2 #119
Observation: MUSIM gaps may be more needed for MUSIM UE in case one UE uses all RF chains in one network. MN-SN MUSIM gaps coordination in INM can save the resource.
  Proposal 2: Specify MN-SN coordination of R17 MUSIM gaps with NR-DC in Rel-18.

## Slide 4: On network B requirement
At [RP-220955] there is one sub-objective as below:
  The following MUSIM gap requirements are considered
        Measurements in Network A
        Measurements in Network B in RRC idle/inactive
        Note: it is up to RAN4 decision whether to define requirements for Network B.
Network B requirements have been discussed for three meetings however there is no consensus on whether to define NW B requirements or not.
Based on the current status it is proposed:
Proposal 3: Suggest to remove NW B requirements in R18/ or move it to R19.

## Slide 5: Clarify on the collision between MUSIM gap an SMTC
In [RP-220955] there is one sub-objective as below:
  Identify and specify, if needed, solutions for MUSIM gap collision handling for the following cases [RAN4, RAN2]
      Case 1: Collisions between MUSIM gap and legacy measurement gap (i.e., Rel-15 to Rel-17 measurement gaps)
      Case 2: Collisions between MUSIM gap and SMTC
      Case 3: Collisions between different MUSIM gaps
      Note: RAN2 work can be triggered by RAN4 LS only, if needed
The scope of case 2 is broad and for a few RRM procedures, collision handling methods have even not been specified between the legacy measurement gaps and SMTC.
Proposal4:
  Add the following note in the case 2:
    Note: The scope of collisions between MUSIM gap and SMTC is limited to the scope where collisions between legacy measurement gap and SMTC are specified.

## Slide 6: Clarify RAN4 TU for Band Confliction for R18 MUSIM
The agreement for band confliction based on discussion in R2-2210485
However, there may be RAN4 RF impact based on above agreements, regarding potential impacts, there are two options
  Option 1: RAN4 discuss this issue based on RAN2 LS
  Option 2: allocate dedicated RAN4 RF TU
  Proposal 5: Discuss which option is adopted for band confliction.