## Slide 1
3GPP TSG RAN Meeting #98-e RP-223120
Electronic Meeting, December 12-16, 2022
Agenda Item: 9.3.1.7
Source: Xiaomi
Title: Views on further reduced capability NR devices
Document for: Discussion and decision

## Slide 2: Rel-18 RedCap WI approved in RAN#97e
The objective is to specify support for the following enhancements:
Power saving/energy efficiency enhancements
  Enhanced eDRX in RRC_INACTIVE (>10.24s) [RAN2, RAN3, RAN4]
    Note that this objective requires SA2 and CT1 involvement
Complexity/cost reduction
  Further reduced UE complexity in FR1 [RAN1, RAN2, RAN4]
    UE BB bandwidth reduction
      5 MHz BB bandwidth only for PDSCH (for both unicast and broadcast) and PUSCH, with 20 MHz RF bandwidth for UL and DL
      The other physical channels and signals are still allowed to use a BWP up to the 20 MHz maximum UE RF+BB bandwidth.
    UE peak data rate reduction
      Relaxation of the constraint (vLayers·Qm·f ≥ 4) for peak data rate reduction
      The relaxed constraint is, e.g., 1 (instead of 4).
      The parameters (vLayers, Qm, f) can be as in Rel-17 RedCap.
    Both 15 kHz SCS and 30 kHz SCS are supported.
    Aim to define at most one Rel-18 RedCap UE type for further UE complexity reduction.
    The existing UE capability framework is used, and changes to capability signalling are specified only if necessary. By default, all UE capabilities applicable to a Rel-17 RedCap UE are applicable unless otherwise specified.
Notes:
  The work defined as part of this WI is not to overlap with LPWA use cases.
  Coexistence with non-RedCap UEs and Rel-17 RedCap UEs should be ensured.
  This WI considers all applicable duplex modes unless otherwise specified.

## Slide 3: Outline
Remaining issues to be checked in RAN#98-e
Updated WI Scope

## Slide 4: Remaining issues
According to the discussion in RAN#97e meeting, the following issues should be checked in this RAN plenary meeting
  Whether UE peak data rate reduction for UE is limited only with UE BB bandwidth reduction or standalone
  Whether or not/how a separate early indication can be supported
  Other restrictions of the WI (e.g., connectivity restrictions , band, etc.)

## Slide 5: Remaining issue#1
  Remaining issue #1: Whether UE peak data rate reduction for UE is limited only with UE BB bandwidth reduction or standalone
  Xiaomi’s view:
    Analysis:
      UE peak data rate reduction has been supported as an add-on solution in RAN1 meeting
      According to the WID, the aim is to define at most one Rel-18 RedCap UE type for further UE complexity reduction
      The complexity reduction of PR1 is limited (~4%)
    UE peak data rate reduction for UE is limited only with UE BB bandwidth reduction
Agreements: UE peak data rate reduction is supported at least as an add-on to UE BB bandwidth reduction, The constraint vLayers·Qm·f ≥ 4 is relaxed to vLayers·Qm·f ≥ X. FFS: the value of X If UE peak data rate reduction is supported as a standalone feature, The constraint vLayers·Qm·f ≥ 4 is relaxed to vLayers·Qm·f ≥ Y. FFS: the value of Y Note: Whether this option is supported will be decided in RAN plenary.

## Slide 6: Remaining issue#2
  Remaining issue #2: Whether or not/how a separate early indication can be supported
    The timeline requirement between Msg2 and Msg3
    Observation 1
      For the case where the number of RBs allocated for RAR PDSCH is larger than 5MHz, separate early indication by Msg1 enables the gNB to identify the UE type before allocating appropriate time domain resources to meet the timeline requirements for both legacy UEs and Rel-18 RedCap UEs
Agreements: For UE BB bandwidth reduction, for RAR (PDSCH) to Rel-18 RedCap UEs, the scheduling of RAR PDSCH is allowed to be larger than the maximum number of unicast PRBs that the UE can process per slot. When the scheduling of RAR PDSCH is larger than the maximum number of unicast PRBs that the UE can process per slot, The UE receives the RAR and correspondingly transmits Msg3 if the TDRA for Msg3 in UL grant in RAR indicates that the time between RAR reception and Msg3 transmission is NOT smaller than NT,1 + NT,2 + 0.5 + X ms. FFS: value(s) of X Otherwise, the UE behavior is up to the UE implementation.

## Slide 7: Remaining issue#2
  Remaining issue #2: Whether or not/how a separate early indication can be supported
    Msg3 PUSCH bandwidth
    Observation 2
      For the case where the payload size of Msg3 is relatively large (e.g., for Msg3 group B, or for RA-SDT), it is necessary for gNB to recognize the UE type in advance before allocating the frequency domain resources, considering that the number of RBs for legacy UEs may need to be larger than 5MHz
Agreements: For UE BB complexity reduction, a UE is not expected to receive an UL grant in a RAR or in a DCI scrambled with TC-RNTI with a Msg3 PUSCH resource allocation spanning a bandwidth of more than ~5 MHz per slot or per hop, if applicable.

## Slide 8: Remaining issue#2
  Remaining issue #2: Whether or not/how a separate early indication can be supported
    Msg4 PDSCH bandwidth
    Observation 3
      For Msg4 PDSCH, the limit on the number of allocated RBs could follow the above agreement for unicast PDSCH
      The payload of Msg4 may be large to carry the RRC signaling for the master cell group configuration by cellGroupConfig
      Separate early indication via Msg1 or Msg3 is useful for the scheduling of Msg4
  Xiaomi’s proposal
      Support separate early indication via Msg1 and/or Msg3 for Rel-18 RedCap UEs
Agreements: For UE BB complexity reduction, a UE is able to receive a DL assignment in a DCI with a unicast PDSCH resource allocation spanning a bandwidth of more than ~5 MHz per slot. The number of PRB scheduled in DCI is not larger than the maximum number of PRB agreed in previous agreement from 110b-e

## Slide 9: Remaining issue#3
  Remaining issue #3: Other restrictions of the WI(e.g., connectivity restrictions , band, etc.)
    Xiaomi’s view:
      Analysis
      The Rel-17 RedCap UE supports only SA mode and non-CA operations
      Except for the baseband bandwidth of PDSCH and PUSCH, and the constraint value(vLayers·Qm·f ) in TS 38.306, functions of Rel-18 eRedCap UEs basically follow the ones of Rel-17 RedCap UEs
 This WI focuses on SA mode and single connectivity with operation in a single band at a time.

## Slide 10: Other clarification on e-DRX
  According to TS 38.304, In RRC_INACTIVE state, enhanced eDRX cycle for CN paging (TeDRX, CN) can already be configured longer than 10.24s while enhanced eDRX cycle for RAN paging (TeDRX, RAN) is restricted to no longer than 10.24s. And Rel-18 Redcap will study on extending TeDRX, RAN beyond 10.24s.
    Xiaomi’s view:
      To clarify in the WID that:
      Enhanced eDRX for RAN paging in RRC_INACTIVE (>10.24s)

## Slide 11: Updated WI scope
The objective is to specify support for the following enhancements:
Power saving/energy efficiency enhancements
  Enhanced eDRX for RAN paging in RRC_INACTIVE (>10.24s) [RAN2, RAN3, RAN4]
    Note that this objective requires SA2 and CT1 involvement
Complexity/cost reduction
  Further reduced UE complexity in FR1 [RAN1, RAN2, RAN4]
    UE BB bandwidth reduction
      5 MHz BB bandwidth only for PDSCH (for both unicast and broadcast) and PUSCH, with 20 MHz RF bandwidth for UL and DL
      The other physical channels and signals are still allowed to use a BWP up to the 20 MHz maximum UE RF+BB bandwidth.
    UE peak data rate reduction
      Relaxation of the constraint (vLayers·Qm·f ≥ 4) for peak data rate reduction
      The relaxed constraint is X, specify the value of X.
      The parameters (vLayers, Qm, f) can be as in Rel-17 RedCap.
    Separate early indication by Msg1/A and/or Msg3
    Both 15 kHz SCS and 30 kHz SCS are supported.
    Aim to define at most one Rel-18 RedCap UE type for further UE complexity reduction.
    The existing UE capability framework is used, and changes to capability signalling are specified only if necessary. By default, all UE capabilities applicable to a Rel-17 RedCap UE are applicable unless otherwise specified.
Notes:
  The work defined as part of this WI is not to overlap with LPWA use cases.
  Coexistence with non-RedCap UEs and Rel-17 RedCap UEs should be ensured.
  This WI considers all applicable duplex modes unless otherwise specified.
  UE peak data rate reduction for UE is limited only with UE BB bandwidth reduction
  This WI focuses on SA mode and single connectivity with operation in a single band at a time.