## Slide 1: Discussion the working scope for the Rel-18 NR-NTN
3GPP TSG RAN Meeting #98-e RP-223122
Electronic Meeting, December 12-16, 2022
Agenda Item: 9.3.2.7
Source: Xiaomi
Document for: Discussion

## Slide 2: Conclusion from the SI for network verification
For network verification of UE location in NR NTN with single satellite in view with DL-TDOA positioning:
From RAN1 perspective, if the UE’s RSTD measurements report can be assumed to be trusted, DL-TDOA positioning method can meet the accuracy requirement of less than 10km with 90% confidence, in case of:
  At least LEO600 based deployment
  Earth fixed cells
  Earth moving cell at least if UE dwell time within the cell is enough to perform at least two RSTD measurements
Note 1: the above is based on evaluation results that didn’t account for UE Clock drift
Note 2: the required over-the-air latency reported in evaluations ranged from less than 20s up to 180s
Note 3: The requirements of Network verification of UE location may not be met if realistic assumption on UE clock drift is considered.
For network verification of UE location in NR NTN with single satellite in view with multi-RTT positioning:
From RAN1 perspective, if the UE’s Rx-Tx time difference measurements report can be assumed to be trusted, multi-RTT positioning method using Rx-Tx time difference measurements can meet the accuracy requirement of less than 10km with 90% confidence, in case of:
  At least LEO600 based deployment
  Earth fixed cells
  Earth moving cell at least if UE dwell time within the cell is enough to perform at least two RTT measurements
Note: the required over-the-air latency reported in evaluations ranged from less than 10s up to 180s

## Slide 3: Analysis for the network verification
Issues for the network verification
  Issue 1: The normal UE’s GNSS information may be attacked which may result in a fake GNSS measurement results
    The UE may not be able to access the network
  Issue 2: The malicious UE may intentionally reports fake information
    Some information UE reported can be considered to be trusted
    The network should be able to deny the access of the malicious UE
Latency for the network verification
  The location verification be capable of being completed within a period of approximately 1 minute maximum and 30 seconds preferably based on the LS reply from SA2
  The latency for completing the network verification can be within the range [10s, 180s]
  Potential enhancement may be needed to meet the latency requirement

## Slide 4: Discussion on RAN2 work on coverage enhancement
According to the SID, RAN needs to decide in RAN #98 meeting whether the study phase has identified any need for NTN-specific coverage enhancements in Rel-18.
RAN2 has made the following agreement regarding coverage enhancement:
From RAN2 perspective we don’t consider msg3 repetition enhancements in R18 NR NTN (apart from msg3 for CFRA, if decided by RAN1)
RAN2 will consider enhancements to enable initial blind Msg3 retransmission grant reception in Rel-18 NTN
Frame aggregation and overhead reduction related:
  RAN2 doesn’t consider using shorter PDCP SN for VoNR in NTN.
  Using RLC TM mode for VoNR in NTN is not supported.
  RAN2 doesn’t consider MAC enhancement to reduce MAC header size for VoNR in NTN.
  RAN2 will not specify signalling whereby the RAN knows the UE’s frame aggregation information in a voice packet
Regarding msg3 repetition enhancements, RAN1 doesn’t discuss any enhancement related to msg3 repetition including CFRA case. Thus, there is no need to consider any enhancement related to msg3 repetition enhancement.
Regarding overhead reduction, RAN2 has concluded not to do PDCP/RLC/MAC enhancement.
Regarding frame aggregation, the only remaining issue is whether gNB can indicate recommended frame aggregation to UE. We are open to decide on this in the WI phase.
Regarding enhancements to enable initial blind Msg3 retransmission grant reception, it should be included in the WI scope.

## Slide 5: Recommendation on network verification of UE location
RAN to send the LS to SA3 to ask whether the UE’s reporting such as UE RX-TX time difference and RSTD can be trusted or not.
RAN to approve the normative work on supporting the network verified location, the detailed objective could be:
For network verification of UE location in NR NTN based on DL-TDOA, specify:
  If justified: NTN-specific definition of RSTD (RAN1)
  Other assistance data (e.g. ephemeris) to be transferred from gNB to the LMF. (RAN3, SA)
  If justified: Other assistance data (e.g. to resolve ambiguity on mirror position issue) to be transferred from UE to LMF (SA)
  If justified: Other potential solutions to meet the latency requirement

## Slide 6: Recommendation for RAN2 work on coverage enhancement
Specify enhancements to enable initial blind Msg3 retransmission grant reception

## Slide 7: Thanks